## Slide 1
Core Module-1
(120 hours)
Notes: In this section we will able to use basic hand tools which usually use in computer hardware and networking

## Slide 2: Able to use basic hand tools effectively
(3 hours)
Notes: In this section we will able to use basic hand tools which usually use in computer hardware and networking

## Slide 3: In this section, we will discuss:
Introduction to hand tools.
Usage of different tools
Soldering techniques
Cables and connectors
Safety hazards on hand toools
Notes: In this section, we will discuss
Introduction to hand tools.
Usage of different tools
Soldering techniques
Cables and connectors
Safety hazards on hand toools

## Slide 4: Introduction to different types of tools
What is tools?
An item or implement used for a specific purpose. A tool can be a physical object such as mechanical tools including saws and hammers or a technical object such as a web authoring tool or software program. Furthermore, a concept can also be considered a tool.
Image Source: Hand Tools & Its Safety – NSTI Dehradun (wordpress.com)
Notes: Hello and welcome to course,
Here we will learn about how use basic hand tools and its specification,
Lets start with the introduction to tools,
What is tools?
An item or implement used for a specific purpose. A tool can be a physical object such as mechanical tools including saws and hammers or a technical object such as a web authoring tool or software program. Furthermore, a concept can also be considered a tool.

## Slide 5: Types of tools
Basic types of tools
Tools categories in three types as below
Mechnical Tools
Measurement Tools
Power Tools
Tools
Mechanical Tools
Measurement Tools
Power Tools
Notes: This slide talks about the case if we have to divide a subtopic further.
Title Box - Parent Topic
Subtitle box - Sub Topic
Body Text - Subtopic divisions (Subtopics of subtopics)

## Slide 6: Mechnical Tools
Cutting Tools
Knives
Saw
Scissors
Blades etc.
Image source: https://sites.google.com/view/master-training
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 7: Mechnical Tools
Grabbinng and clamping Tools
C- Clamps
Pliers
Bench vise
Tweezers
Image source: https://sites.google.com/view/master-training
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 8: Mechnical Tools
Hammers and Mallets
Ball point Hammer
Nail Hammer
Track hammer
Mallet
Image source: https://sites.google.com/view/master-training
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 9: Mechnical Tools
Screw Drivers, Fasteners and spanners
Hand held tools used to fasten objects using screws. There are different types of screw drivers like Phillips Screw Driver etc. Allen Key Set is a set of tools that can fasten / unfasten special set of screws.
Spanners are tools that provides grip and mechanical advantage in applying torque/force to turn objects.
Image source: https://sites.google.com/view/master-training
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 10: Measurement Tools
Multimeter
A multimeter or a multi tester, also known as a VOM (volt ohm milli-ammeter), is an electronic measuring instrument that combines several measurement functions in one unit. A typical multimeter can measure voltage, current, and resistance.
Image source: https://sites.google.com/view/master-training
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 11: Measurement Tools
Digital Oscilloscope
A digital storage oscilloscope (often abbreviated DSO) is an oscilloscope which stores and analyses the signal digitally rather than using analog techniques It is now the most common type of oscilloscope in use because of the advanced trigger, storage, display and measurement features which it typically provides
Image source: https://sites.google.com/view/master-training
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 12: Power Tools
Power Drill
A power drill is an electrical motor that rotates a replaceable drill bit to make a hole in wood, plastic, or metal. Alternately, a screwdriver tip can be installed to turn screws. Corded or cordless drills can handle a wide variety of tasks, including drilling holes and driving screws in and out.
Image source: https://sites.google.com/view/master-training
Notes: A power drill is an electrical motor that rotates a replaceable drill bit to make a hole in wood, plastic, or metal. Alternately, a screwdriver tip can be installed to turn screws. Corded or cordless drills can handle a wide variety of tasks, including drilling holes and driving screws in and out.
Corded or cordless drills can be used in mobility, but the stationary drill or drill station has to be used on the surface bed of the stationary drill

## Slide 13: Power Tools
Hot Glue Gun
Hot glue guns use continuous heating elements to melt the adhesive The gun would heat the glue, and you could use the hot glue to adhere pieces of fabric together (or to make other craft projects).
Hot melt also has the advantage of not losing any thickness when drying.
Image source: https://sites.google.com/view/master-training
Notes: Hot glue guns use continuous heating elements to melt the adhesive The gun would heat the glue, and you could use the hot glue to adhere pieces of fabric together (or to make other craft projects).
Hot melt also has the advantage of not losing any thickness when drying.

## Slide 14: Crimping Tools and Types
Crimping tools
Crimp tools are a varied collection of devices used to join materials or components by pressing them together and creating a seal or crimp
Image source: https://sites.google.com/view/master-training
Notes: What is crimp tools?
Crimp tools are a varied collection of devices used to join materials or components by pressing them together and creating a seal or crimp

## Slide 15: Crimping Tools and Types
Types of Crimping tools
Bootlace Crimp Tool
RJ45 Crimp tool
RJ9 Crimp tool
Image source: https://www.computerhope.com/jargon/c/crimp.htm
Notes: Types of Crimp Tool
Crimp tools can be used for many different applications across a range of industries and environments. Here are some additional types of crimp tool:
Bootlace Crimp Tools
As the name suggests, bootlace crimp tools are specifically designed to work with bootlace ferrules, which require a different form of crimping to standard cabling. Precision must be combined with force to ensure a strong indent crimp.
RJ45 Crimping Tool
The RJ45 crimping tool is a flexible and powerful handheld crimper, compatible with CAT5e, CAT6, CAT6A and CAT7 terminals.
RJ9 Crimp Tool
The RJ9 is a widely used handheld crimp tool fitted with three dies (crimping heads) compatible with the standard connector types RJ45, RJ11 and RJ12. This adaptability means engineers require fewer items in their crimp toolsets when conducting repairs or installations.

## Slide 16: Safety hazards on basic hand tools
Image Source: https://nstidehradun.wordpress.com/2019/11/29/hand-tools-and-its-safety/
Hand Tool Safety Rules
Some basic hand tools safety hazards
Hammer Safety
Power Drill Safety
Power Saw Safety
Hand Files & Rasp Safety
Chisel Safety
Toolboxes, Tool Chests & Cabinets
Notes: Safety Precaution of Hand Tools:
Inspection should be done before use.
Always keep clean.
Always keep tools in box.
Use proper tool for the job doing.
Use bucket and leather bad to shift the tools at height.
Follow color coding.
Awareness among the workers for the safe using.
Carrying or transporting tools
Use a tool box, tool-holder, belt or pouch, this will protect the person and the tool
Carry pointed or sharp tools with the point or cutting edge away from the body
Do not carry tools by hand up ladders
Do not lay tools down where people can trip on them or they can fall on someone

## Slide 17: Soldering techniques
Image Source: https://svtronics.com/blog/wpcontent/uploads/2021/06/AdobeStock_130497973.jpg
What is Soldering
Soldering is a joining process used to join different types of metals together by melting solder.
Notes: Soldering is a joining process used to join different types of metals together by melting solder. Solder is a metal alloy usually made of tin and lead which is melted using a hot iron. The iron is heated to temperatures above 600 degrees Fahrenheit which then cools to create a strong electrical bond.
Overview: What is soldering and when should you use it?
Soldering is a process in which two or more metal items are joined together by melting and then flowing a filler metal into the joint—the filler metal having a relatively low melting point.
Soldering is used to form a permanent connection between electronic components.
The metal to be soldered is heated with a soldering iron and then solder is melted into the connection.
  Only the solder melts, not the parts that are being soldered.
  Solder is a metallic "glue" that holds the parts together and forms a connection that allows electrical current to flow.
You can use a solderless breadboard to make test circuits, but if you want your circuit to last for more than a few days, you will want to solder the components together.

## Slide 18: Soldering techniques
Image Source:https://www.sciencebuddies.org/science-fair projects/references/how-to-solder
Materials Required for soldering
Soldering Iron
Rosin core solder
Soldering iron stand
Sponge
Solder braid
Prototype board
Notes: Materials and Equipment
A soldering iron
  A soldering iron is used to heat the connections to be soldered.
  For electronic circuits, you should use a 25- to 40-watt (W) soldering iron.
  Higher wattage soldering irons are not necessarily hotter; they are just able to heat larger components. A 40-W soldering iron makes joints faster than a 25-W soldering iron does.
  A soldering iron can be purchased at hardware stores and at most large department stores.
Rosin core solder
  Solder has a lower melting point than the metals that are being connected do. The solder melts when it is heated by the soldering iron, but the metals being joined will not melt.
  The rosin core acts as a flux. It prevents oxidation of the metals that are being connected, and enhances the ability of the solder to "wet" the surfaces that are being joined.
  Solder that is used to join copper pipes has an acid core, which is appropriate for pipes, but will corrode electronic connections. Use solder that has a rosin core.
  For most electronics work, a solder with a diameter of 0.75 millimeters (mm) to 1.0 mm is best. Thicker solder might make soldering small joints difficult and also increases the chances of creating solder bridges between copper pads that are not meant to be connected.
  An alloy of 60/40 (60% tin, 40% lead) is used for most electronics work, but lead-free solders are available as well.
Stand on which to hold the hot soldering iron
  There are a variety of stands available. It is important to always keep the hot iron in its stand when not in use.
Sponge
  The damp sponge is used to clean the tip of the iron.
Solder braid
  This is used to remove solder.
  To use the braid, place it over the solder to be removed and heat it from above with the iron. The solder will flow into the braid.
  Solder braid is used to extract an electronic component that is soldered onto a board.
  It is also used to reduce the amount of solder on a connection.
Prototype board
  A prototype board is used to assemble the circuit. The board shown is from www.protostack.com, but Jameco Electronics also supplies prototype boards.
  Prototype boards have copper tracks or pads for connecting components.
Steel wool or fine sandpaper
  This is used to clean connections prior to soldering.
  Solder will not flow over a dirty connection.
Crocodile clips
  These can be used as heat sinks, if needed.

## Slide 19: Soldering techniques
Image Source:https://www.sciencebuddies.org/science-fair projects/references/how-to-solder
How to solder
Solder needs a clean surface on which to adhere
To solder, heat the connection with the tip of the soldering iron for a few seconds, then apply the solder.
Keep the soldering tip on the connection as the solder is applied
Don't move the connection while the solder is cooling.
Don't overheat the connection, as this might damage the electrical component you are soldering.
Notes: Soldering
Soldering
Solder needs a clean surface on which to adhere.
  Buff the copper foil of a PC board with steel wool before soldering.
  Remove any oil, paint, wax, etc. with a solvent, steel wool, or fine sandpaper.
To solder, heat the connection with the tip of the soldering iron for a few seconds, then apply the solder.
  Heat the connection, not the solder.
  Hold the soldering iron like a pen, near the base of the handle.
Both parts that are being soldered have to be hot to form a good connection. Keep the soldering tip on the connection as the solder is applied.
  Solder will flow into and around well-heated connections.
  Use just enough solder to form a strong connection.
Remove the tip from the connection as soon as the solder has flowed where you want it to be. Remove the solder, then the iron.
Don't move the connection while the solder is cooling.
Don't overheat the connection, as this might damage the electrical component you are soldering.
Transistors and some other components can be damaged by heat when soldering. A crocodile clip can be used as a heat sink to protect these components. Soldering a connection should take just a few seconds.
  If it is taking longer, see the troubleshooting section below.
Inspect the joint closely. It should look shiny (note: lead-free solder may appear dull, this is OK).
  If you are soldering a wire (called the lead) onto a PC board (on the track), it should have a volcano shape. See Figure 3.
  If the connection looks bad, reheat it and try again.
Wipe the tip of the iron on a damp sponge to clean it. The tip should now be shiny.
Unplug the soldering iron when it is not in use.

## Slide 20: Cables and Connectors
Image Source:https://contentgrid.homedepot-static.com/hdus/en_US/DTCCOMNEW/Articles/types-of-cables-and-connectors-for-networking-section-3-A.jpg
Cables
Cable is the medium through which information usually moves from one network device to another.
USB Cables
HDMI cables
Ethernet Cable
Cat 6 cable
VGA cable
Fiber optic cable
Notes: What is cable?
Cable is the medium through which information usually moves from one network device to another. There are several types of cable which are commonly used with LANs. In some cases, a network will utilize only one type of cable, other networks will use a variety of cable types. The type of cable chosen for a network is related to the network's topology, protocol, and size. Understanding the characteristics of different types of cable and how they relate to other aspects of a network is necessary for the development of a successful network.
Fiber Optic Cable
Fiber optic cabling consists of a center glass core surrounded by several layers of protective materials It transmits light rather than electronic signals eliminating the problem of electrical interference. This makes it ideal for certain environments that contain a large amount of electrical interference. It has also made it the standard for connecting networks between buildings, due to its immunity to the effects of moisture and lighting.
Fiber optic cable has the ability to transmit signals over much longer distances than coaxial and twisted pair. It also has the capability to carry information at vastly greater speeds. This capacity broadens communication possibilities to include services such as video conferencing and interactive services. The cost of fiber optic cabling is comparable to copper cabling; however, it is more difficult to install and modify. 10BaseF refers to the specifications for fiber optic cable carrying Ethernet signals.
Cat 6 cables
Category 6 cable (Cat 6) is a standardized twisted pair cable for Ethernet and other network physical layers that is backward compatible with the Category 5/5e and Category 3 cable standards.
Cat 6 must meet more stringent specifications for crosstalk and system noise than Cat 5 and Cat 5e. The cable standard specifies performance of up to 250 MHz, compared to 100 MHz for Cat 5 and Cat 5e
HDMI
The HDMI interface allows a port to send high-resolution digital video, theatre-quality sound and device commands through an HDMI connector and down a single HDMI cord, each designed to support a video resolution and features in the HDMI specification.
HDMI connectors are available in three sizes: standard, mini and micro.
There are also different types of HDMI cable (see the chart below). Not all cables use the logo but the cable specifications should indicate whether it is Standard, High Speed, Premium High Speed or Ultra High Speed. If the type is not indicated, assume Standard.
What is a USB Cable?
The term USB stands for "Universal Serial Bus". USB cable assemblies are some of the most popular cable types available, used mostly to connect computers to peripheral devices such as cameras, camcorders, printers, scanners, and more.

## Slide 21: Cables and Connectors
Image Source:https://5.imimg.com/data5/RO/XO/MY-3767981/rf-connectors-500x500.jpg
Connectors
A connector is the unique end of a plug, jack, or the edge of a card that connects to a port
AV ports
RF connectors
Notes: Connectors
A connector is the unique end of a plug, jack, or the edge of a card that connects to a port. For example, all desktop computer expansion cards have a connector that allows them to connect in a slot on the motherboard. When referring to cables, the connector is the end of the cable that connects into a port. For example, the end of a USB cable has a connector that allows it to connect to a USB port.
AV ports
The input/output paths on audio and video devices. Following are the major plugs and sockets.
RF Connectors
A coaxial RF connector (radio frequency connector) is an electrical connector designed to work at radio frequencies in the multi-megahertz range. RF connectors are typically used with coaxial cables and are designed to maintain the shielding that the coaxial design offers. Better models also minimize the change in transmission line impedance at the connection in order to reduce signal reflection and power loss.

## Slide 22: Able to Disassemble and assemble PC
(3 hours)
Notes: In this section we will learn about assembly and disassembly of personal computer
Assembling and Disassembling PC
Introduction
Computer assembly is an essential job of a computer installation technician. The technician has to work in a logical, methodical manner while handling various computer components and peripherals. The technician can improve the computer assembly skills with practice. Computer assembly is a process in which all the internal components required for the computer system are fitted so as to make the computer functional. There is a proper sequence of attachment of each and every component into the computer system. To establish proper connectivity, one has to use the tools. Proper handling of tools is also required by the technician. It is required that students learn the steps of installation of each component. The main component involves installing CPU, motherboard, drives, video, graphics card, sound card, modem and adapter, and connectors, and system panel connector. In this Chapter, we will understand the step by step process of assembling a computer. It also covers the need for adequate system resources to efficiently run the customer’s hardware and software.

## Slide 23: In this section, we will discuss:
Steps to asseble PC
Steps to deassemble PC
Notes: Mention the parent topics one by one. This particular learning outcome has 4 parent topics.
Steps to asseble PC
Steps to deassemble PC

## Slide 24: Computer assembly
Image Source: https://cdn2.vectorstock.com/i/1000x1000/30/51/assembling-pc-personal-computer-hardware-vector-13773051.jpg
Steps for assemble PC
As we know, computer assembly is a systematic process. First, arrange the computer parts. The sequence for assembly and working of the computer listed below is as:
Open the case.
Install the power supply.
Attach the components to the motherboard.
Install the motherboard.
Install internal drives.
Connect all internal cables.
Install motherboard power connections
Connect external cables to the computer.
Boot the computer for the first time.
Notes: Computer Assembly
As we know, computer assembly is a systematic process. First, arrange the computer parts. The sequence for assembly and working of the computer listed below is as:
Open the case.
Install the power supply.
Attach the components to the motherboard.
Install the motherboard.
Install internal drives.
Connect all internal cables.
Install motherboard power connections
Connect external cables to the computer.
Boot the computer for the first time.

## Slide 25: Computer assembly
Image Source: https://cdn3.vectorstock.com/i/1000x1000/30/67/assembling-pc-personal-computer-hardware-vector-13773067.jpg
Required Material
Computer case, with power supply installed
Motherboard
CPU
Heat sink/fan assembly
Thermal compound
RAM module(s)
Motherboard standoffs and screws
Anti‑static wrist strap and anti-static mat
Tool kit
Notes: Prepare the workspace before starting installation of the computer. There should be adequate lighting, good ventilation, and a comfortable room temperature. The workbench or table should be accessible from all sides. Avoid cluttering the surface of the workbench or table with tools and computer components. An anti‑static mat on the table will help to prevent physical and electrostatic discharge (ESD) damage to equipment. Small containers can be used to hold small screws and other parts as they are being removed.
Material Required
Computer case, with power supply installed
Motherboard
CPU
Heat sink/fan assembly
Thermal compound
RAM module(s)
Motherboard standoffs and screws
Anti‑static wrist strap and anti-static mat
Tool kit

## Slide 26: Computer assembly
Image Source: https://ncert.nic.in/vocational/pdf/keit104.pdf
Step 1 : Open the case
The first step in assembling a computer is to open the computer case.
There are different methods for opening cases.
The computer comes with various types of cabinets. The method for opening the case is different based on the manufacturer.
To open the case, first remove the screws of the left side cover and slide the side cover.
Notes: The first step in assembling a computer is to open the computer case (see Figure 1.1). There are different methods for opening cases.
The computer comes with various types of cabinets. The method for opening the case is different based on the manufacturer.
To open the case, first remove the screws of the left side cover and slide the side cover (see Figure 1.2).

## Slide 27: Computer assembly
Image Source: https://ncert.nic.in/vocational/pdf/keit104.pdf
Step 2 : Install Power Supply
Insert the power supply into the case.
Align the holes in the power supply with the holes in the case.
Secure the power supply to the case using the proper screws
Notes: Install the power supply The next step is to install a power supply (see Figure 1.3). There are usually four screws that attach the power supply to the case. Power supplies have fans that can vibrate and loosen screws that are not secured. When installing a power supply, make sure that all of the screws are used and that they are properly tightened.
Insert the power supply into the case.
Align the holes in the power supply with the holes in the case.
Secure the power supply to the case using the proper screws

## Slide 28: Computer assembly
Image Source: https://i.ytimg.com/vi/H3yTF6wqTbg/maxresdefault.jpg
Step 3 : Assemble motherboard
The motherboard has to be prepared before its installation. To prepare the motherboard, you first need to install the CPU, then the heat sink on the CPU and CPU fan.
Notes: The motherboard has to be prepared before its installation. To prepare the motherboard, you first need to install the CPU, then the heat sink on the CPU and CPU fan.
CPU
The CPU and motherboard are sensitive to electrostatic discharge. So place them on a grounded anti-static mat and wear an anti-static wrist strap while handling the CPU. When handling a CPU, do not touch the CPU contacts at any point. The CPU is secured to the socket on the motherboard with a locking assembly.
Thermal compound which is used to conduct heat away from the CPU is applied on the top of CPU. In case of an old CPU, first clean the top of the CPU, and then apply the thermal compound. Clean the top of the CPU and the base of the heat sink with isopropyl alcohol and a lint‑free cloth. This removes the old thermal compound. Then apply a new layer of thermal compound

## Slide 29: Computer assembly
Image Source: https://content.instructables.com/ORIG/F97/Y4PB/KKCKYS94/F97Y4PBKKCKYS94.jpg?auto=webp&fit=bounds&frame=1&auto=webp&frame=1&height=300
Step 3 : Assemble motherboard
Heat sink and fan assembly
Notes: The motherboard has to be prepared before its installation. To prepare the motherboard, you first need to install the CPU, then the heat sink on the CPU and CPU fan.
Heat sink and fan assembly
Heat sink and fan assembly is a two-part cooling device. The heat sink draws heat away from the CPU. The fan moves the heat away from the heat sink. The assembly has a 3-pin power connector.
To install a CPU and heat sink and fan assembly, follow these steps:
First, open the CPU load plate. Align the CPU orientation so that the notches on the CPU are aligned with the orientation keys on CPU socket.
Place the CPU gently into the socket. Close the CPU load plate.
Close the load lever.
Apply a small amount of thermal compound to top of the CPU (see Figure)
Screw the CPU fan on the heat sink.
Align the heat sink and fan assembly with the holes on the motherboard.
Place the assembly onto the CPU socket carefully.
Screw the assembly on the motherboard (see Figure 1.7).
Connect the assembly power cable to the CPU fan connector on the motherboard.

## Slide 30: Computer assembly
Image Source: https://encrypted-tbn0.gstatic.com/images?q=tbn:ANd9GcREsFBYn_au89zChyMMDNg4OMhdNcJs4GXYtg&usqp=CAU
Step 3 : Assemble motherboard
RAM Installation
Notes: The motherboard has to be prepared before its installation. To prepare the motherboard, you first need to install the CPU, then the heat sink on the CPU and CPU fan.
Installation of RAM
It is better to install the RAM first on the motherboard and then fix the motherboard in the case. To install RAM, first ensure its compatibility with the motherboard. If DDR3 is mentioned on the motherboard, then DDR3 RAM may be fixed in the memory slot. To install RAM, follow these steps.
Press down the side locks of the memory slot (see Figure 1.8). Align the notches on the RAM module to the keys in the slot and press down on both ends of RAM module until the side lock gets locked.
Make sure that the side tabs have locked the RAM module.
Repeat the above steps to install additional RAM modules.

## Slide 31: Computer assembly
Image Source: https://icdn.digitaltrends.com/image/digitaltrends/installmotherboard01.jpg
Step 4 : Install motherboard
Lay the motherboard over the standoffs to mount it on the holes.
Align the screw holes of the motherboard with the standoffs.
Then screw the board using a standard screwdriver.
Tighten all the motherboard screws.
Connect the 4-pin ATX power connector from the power supply to the motherboard.
Notes: After preparing the motherboard, you can install the computer case, as shown in Figure 1.9. Plastic and metal standoffs are used to mount the motherboard and to prevent it from touching the metal portions of the case. To install the motherboard, follow these steps:
Lay the motherboard over the standoffs to mount it on the holes.
Align the screw holes of the motherboard with the standoffs.
Then screw the board using a standard screwdriver.
Tighten all the motherboard screws.
Connect the 4-pin ATX power connector from the power supply to the motherboard.

## Slide 32: Computer assembly
Image Source: https://www.deskdecode.com/wp-content/uploads/2020/05/installing-hard-drive-min.jpg
Step 5 : Install Internal Drives
Hard Drive
Position the HDD so that it aligns with the 3.5-inch drive bay.
Insert the HDD into the drive bay so that the screw holes in the drive line up with the screw holes in the case
Secure the HDD to the case using proper screws.
Notes: Hard drive
The hard drive is the device which stores all the data. It is 3.5 inch wide and needs to be mounted so that access to the cable connections on the back is gained. Drives that are installed in internal bays are called internal drives. A hard disk drive (HDD) is an example of an internal drive. To install HDD, follow these steps:
Position the HDD so that it aligns with the 3.5-inch drive bay.
Insert the HDD into the drive bay so that the screw holes in the drive line up with the screw holes in the case (see Figure 1.10)
Secure the HDD to the case using proper screws.

## Slide 33: Computer assembly
Image Source: https://docs.oracle.com/cd/E19127-01/ultra27.ws/820-6776/images/126223new.gif
Step 5 : Install Internal Drives
Optical Drive
Position the optical drive so that it aligns with the 5.25 inch drive bay.
Insert the optical drive into the drive bay so that the optical drive screw holes align with the screw holes in the case (see Figure 1.11).
Secure the optical drive to the case using the proper screws.
Connect the power cable coming from the SMPS to the power socket of optical drive.
Connect SATA data cable from optical drive socket to the motherboard socket.
Notes: Optical drive
Position the optical drive so that it aligns with the 5.25 inch drive bay.
Insert the optical drive into the drive bay so that the optical drive screw holes align with the screw holes in the case (see Figure 1.11).
Secure the optical drive to the case using the proper screws.
Connect the power cable coming from the SMPS to the power socket of optical drive.
Connect SATA data cable from optical drive socket to the motherboard socket.

## Slide 34: Computer assembly
Image Source: https://docs.oracle.com/cd/E19127-01/ultra27.ws/820-6776/images/126223new.gif
Step 6 : Connect all internal cables
Power cables are used to distribute electricity from the power supply to the motherboard and other components. Data cables transmit data between the motherboard and storage devices, such as hard drives.
Notes: Step 6: Connect all internal cables
Power cables are used to distribute electricity from the power supply to the motherboard and other components. Data cables transmit data between the motherboard and storage devices, such as hard drives.

## Slide 35: Computer assembly
Image Source: https://ncert.nic.in/vocational/pdf/keit104.pdf
Step 7 : Install motherboard power connections
Align the 20-pin ATX power connector with the socket on the motherboard.
Gently press down on the connector until the clip clicks into place.
Align the 4-pin AUX power connector with the socket on the motherboard.
Gently press down on the connector until the clip clicks into place.
Notes: Just like other components, motherboards require power to operate. The Advanced Technology eXtended (ATX) main power connector will have either 20 or 24 pins. The power supply may also have a 4-pin or 6-pin auxiliary (AUX) power connector that connects to the motherboard. A 20-pin connector will work in a motherboard with a 24-pin socket. Follow these steps for motherboard power cable installation:

## Slide 36: Computer assembly
Image Source: https://ncert.nic.in/vocational/pdf/keit104.pdf
Step 8 : Connect External cables to computers
Connect Monitor
Connect one end of the cable to the monitor port on the back of the computer case and the other end to the monitor. In case of VGA cable as shown in Figure 12.22 tighten the screws on the monitor cable to secure it.
Notes: Setting up the computer system involves the complete process of establishing the proper connectivity of various parts of the computer system — input and output devices, connectivity of computer with the surge power supply. Reattach the side panels to the case. The process of connecting the external cables given below:
Locate the monitor cable
Locate the two power cable and one VGA cable or monitor cable (see Figure 1.14). The VGA cable is used to connect to monitor and another point on to the back side of the cabinet. If you are having trouble finding these, refer to the instruction manual of or the computer. You can skip to ‘Step 3’, in case of all-in-one computer that is built into the monitor.
Connecting monitor
Connect one end of the cable to the monitor port on the back of the computer case and the other end to the monitor. In case of VGA cable as shown in Figure 12.22 tighten the screws on the monitor cable to secure it.
The cables will only fit in a specific way. If the cable does not fit, do not force it, otherwise the connectors might get damaged. Make sure the plug aligns with the port, then connect it. So, first identify all the cables, ports, and connectors. The cables will only fit in a specific way. If the cable does not fit, do not force it, otherwise the connectors might get damaged. Make sure the plug aligns with the port, then connect it. So, first identify all the cables, ports, and connectors

## Slide 37: Computer assembly
Image Source: https://ncert.nic.in/vocational/pdf/keit104.pdf
Step 8 : Connect External cables to computers
Connect Keyboard and mouse
As shown in image make proper connection with keyboard and mouse
Notes: Connecting keyboard and mouse
Unpack the keyboard and determine whether it uses a USB (rectangular) connector or a PS/2 (round) connector. If they have colour coded plugs that are light green and lavender, plug them into the corresponding colour-coded ports, it is more likely if they use round PS/2 connectors. If it uses a USB connector, plug it into any of the USB ports on the back of the computer. The following Figures 1.16 and 1.17 shows connecting keyboard in PS/2 connector and USB connector.
Connecting mouse
Unpack the mouse and determine whether it uses a USB or PS/2 connector. If it uses a USB connector, plug it into any of the USB ports on the back of the computer. If it uses a PS/2 connector, plug it into the green mouse port on the back of the computer. In case of wireless mouse or keyboard, connect a Bluetooth dongle (USB adapter) in one of the USB ports of the computer. However, it is not necessary to connect an adapter for the modern computers which have built-in Bluetooth.

## Slide 38: Computer assembly
Image Source: https://ncert.nic.in/vocational/pdf/keit104.pdf
Step 8 : Connect External cables to computers
Checklist the following before starting the computer
VGA cable of monitor is connected to the cabinet or not.
Power cable of monitor and cabinet has been plugged into the UPS power output socket. Make sure monitor is connected to the power supply or not.
Keyboard and mouse both are connected to their proper ports
Notes: Checklist the following before starting the computer :
VGA cable of monitor is connected to the cabinet or not.
Power cable of monitor and cabinet has been plugged into the UPS power output socket. Make sure monitor is connected to the power supply or not.
Keyboard and mouse both are connected to their proper ports.

## Slide 39: Computer assembly
Image Source: https://ncert.nic.in/vocational/pdf/keit104.pdf
Step 9 : Starting the Computer
To start the computer, it is necessary to follow the correct sequence to start up. Now push the power button on the CPU to start the computer
Notes: Step 9: Starting the computer
To start the computer, it is necessary to follow the correct sequence to start up. Now push the power button on the CPU to start the computer. Practically when we start our vehicle, we always check that the light or air conditioner (AC) is off. Otherwise, it will consume more power compared to normal start up.
Always remember that the first step is to push power button of the CPU than the monitor’s. Because the monitor consumes more electricity when powered. An operating system or system software like Window or Linux will start.

## Slide 40: Computer Disassembly
Image Source: https://www.researchgate.net/profile/Sagar-Kamarthi/publication/45061936/figure/fig1/AS:669091685728257@1536535297037/Disassembly-of-Personal-Computer.png
Steps for Disassemble PC
Disassembly is the process of breaking down a device into separate parts. Disassembly of any device is required to determine a problem, to replace a part, or take the parts and use them in another device
Unplugging
Open the case
Disconnect all connectors
Remove the Fan
Remove the Power Supply
Remove HDD and Optical Drive
Remove RAM
Remove Motherboard
Notes: Computer Disassembly
Disassembly is the process of breaking down a device into separate parts. Disassembly of any device is required to determine a problem, to replace a part, or take the parts and use them in another device. A computer is also an electronic device which requires disassembly for such issues. For example, if a RAM gets dysfunctional in a computer, then it requires disassembling the computer to take out the dysfunctional RAM and replace it with new RAM chips. As we know, computers have standard internal components, but the way of placement may vary as per the PC tower case and different brands of computer. The best way is to refer to the manufacturer instructions manual. But in general there is a standard process of computer disassembly, which is demonstrated in this session. Just like computer assembly, the disassembly is a standard process. The process involves unplugging of all the cords and cables connecting a component to other components, then removing the part from the case or frame. Components can be attached to the case with special clips, screws, or by insertion into a holder. A small amount of force is required to remove each part of the computer system.

## Slide 41: Computer Disassembly
Image Source: https://www.researchgate.net/profile/Sagar-Kamarthi/publication/45061936/figure/fig1/AS:669091685728257@1536535297037/Disassembly-of-Personal-Computer.png
Required Material
One working PC
An anti‑static wrist strap
An anti‑static mat
Anti-static bags of various sizes
Technician’s toolkit
A plastic cup or box to organise screws, nuts, and bolts
Notes: Material Required
One working PC
An anti‑static wrist strap
An anti‑static mat
Anti-static bags of various sizes
Technician’s toolkit
A plastic cup or box to organise screws, nuts, and bolts

## Slide 42: Computer Disassembly
Image Source: https://awesomerajaaida.files.wordpress.com/2015/02/lab-3-how-to-install-a-hard-drive.jpg
Step 1 : Unplugging
Unplug the power cord from the PC and from the wall socket to prevent any injuries and damage of the PC from electrostatic discharge (ESD).
Unplug all the peripherals attached to the computer, such as the keyboard, mouse, monitor, headphones, and any external drives.
Wear a grounding strap to discharge any static electricity.
Notes: Step 1: Unplugging
Unplug the power cord from the PC and from the wall socket to prevent any injuries and damage of the PC from electrostatic discharge (ESD).
Unplug all the peripherals attached to the computer, such as the keyboard, mouse, monitor, headphones, and any external drives.
Wear a grounding strap to discharge any static electricity.

## Slide 43: Computer Disassembly
Image Source: https://ncert.nic.in/vocational/pdf/keit104.pdf
Step 2 : open the case
To open the case, first remove the screws of the left side cover and slide the side cover.
Pull the latch to release the side panel. Then lift the side cover out from the chassis.
Notes: Step 2: Open the case
The computer comes with various types of cabinets. The methods of opening the case are different based on the manufacturer.
To open the case, first remove the screws of the left side cover and slide the side cover.
Pull the latch to release the side panel. Then lift the side cover out from the chassis.
To remember connectivity of internal cables, take the photographs of internal circuitry. It will help to assemble back the system.

## Slide 44: Computer Disassembly
Image Source: https://ncert.nic.in/vocational/pdf/keit104.pdf
Step 3 : Disconnect all Connectors
Disconnect all the connectors connected to the motherboard. These include SATA power cable and data cable of HDD as well as SATA cable of optical drive.
Notes: Step 3: Disconnect all the connectors
Disconnect all the connectors connected to the motherboard. These include SATA power cable and data cable of HDD as well as SATA cable of optical drive.

## Slide 45: Computer Disassembly
Image Source: https://ncert.nic.in/vocational/pdf/keit104.pdf
Step 4 : Remove the Fan
Remove the fan now. Most computers have two fans — the system fan and CPU fan. The system fan is located at the back side of the computer to blow air into the computer. The CPU fan is located on top of the CPU heat sink. The fans and its connectors are labelled with their names.
Notes: Remove the fan now. Most computers have two fans — the system fan and CPU fan. The system fan is located at the back side of the computer to blow air into the computer. The CPU fan is located on top of the CPU heat sink. The fans and its connectors are labelled with their names.
To remove the system fan, first, disconnect its connector from the motherboard. Then, unscrew it from the outside of the back of the case and lift the fan out of the system.
To remove the CPU fan from the heat sink, first, disconnect its connector from the motherboard. Then remove the four screws securing it

## Slide 46: Computer Disassembly
Image Source: https://ncert.nic.in/vocational/pdf/keit104.pdf
Step 5 : Remove Power supply
Disconnect the power cable of the hard disk and optical drive which connects to the SMPS
Remove the screws that secure the power supply unit to the chassis
Carefully lift the power supply out of the chassis
Notes: The power supply is connected to the motherboard by a 20-pin connector and 4-pin connector. It is also connected to hard disk drive and the optical drive. Firstly, disconnect hard disk drive and the optical drive connectors from the motherboard
Disconnect the power cable of the hard disk and optical drive which connects to the SMPS
Remove the screws that secure the power supply unit to the chassis
Carefully lift the power supply out of the chassis

## Slide 47: Computer Disassembly
Image Source: https://docs.oracle.com/cd/E19127-01/ultra27.ws/820-6776/images/23967.gif
Step 6 : Remove RAM
RAM allows for the transfer of information to and from the CPU. Computer runs fast with more RAM. Most computers have four RAM slots, and two RAM chips. To remove the RAM, push down on both tabs holding the RAM in place, which are located at both ends of the RAM. It will cause the module to pop up for easy removal.
Notes: RAM allows for the transfer of information to and from the CPU. Computer runs fast with more RAM. Most computers have four RAM slots, and two RAM chips. To remove the RAM, push down on both tabs holding the RAM in place, which are located at both ends of the RAM. It will cause the module to pop up for easy removal.

## Slide 48: Computer Disassembly
Image Source https://ncert.nic.in/vocational/pdf/keit104.pdf
Step 7 : Remove Expansion Cards
The modern motherboards are integrated with the audio, video and network cards. However, if your computer has the expansion card as shown in Figure , insert into the expansions slot to increase the functionality. The expansion card is screwed with a single screw on top of expansion card slot.
Notes: Step 7: Remove expansion cards
The modern motherboards are integrated with the audio, video and network cards. However, if your computer has the expansion card as shown in Figure 1.31, insert into the expansions slot to increase the functionality. The expansion card is screwed with a single screw on top of expansion card slot.
To remove the expansion cards, disconnect the cables attached to it.
Remove the screws securing the card in the slot.
Carefully take out the card from the slot

## Slide 49: Computer Disassembly
Image Source https://i.ytimg.com/vi/i3afSFfCmH4/maxresdefault.jpg
Step 8 : Remove Mother board
Every part of the computer is attached to the motherboard. The CPU, RAM, and expansion cards are directly attached to the motherboard.
To remove the motherboard, disconnect all the cables from the motherboard. It has seven screws holding it to the frame. Remove these screws and then lift the motherboard out of the frame.
Notes: Step 8: Remove motherboard
Every part of the computer is attached to the motherboard. The CPU, RAM, and expansion cards are directly attached to the motherboard.
To remove the motherboard, disconnect all the cables from the motherboard. It has seven screws holding it to the frame. Remove these screws and then lift the motherboard out of the frame.

## Slide 50: Able to install and maintain software’s for a PC
(1 hours)
Notes: In this section we will discuss the different type of software and file system of PC

## Slide 51: In this section, we will discuss:
Distinguish between System Software and Application Software
Differentiate between Linux and Windows OS
Windows 32 bit, and 64 bit System
FDISK, Format, Scandisk, FAT System, NTFS and Directories, Fragmentation and defragmentation disk
Notes: We will discuss following things in this section
Distinguish between System Software and Application Software
Differentiate between Linux and Windows OS
Windows 32 bit, and 64 bit System
FDISK, Format, Scandisk, FAT System, NTFS and Directories, Fragmentation and defragmentation disk

## Slide 52: Distinguish between System Software and Application Software
Image Source : https://eportfolio.utm.my/user/choy-wan-ling/chapter-5-system-software
System Software
What is System Software?
Types of System Software
Features of System Software
Notes: We will discuss following in this section
What is software?
Types of Software
System Software
Features of system software:
Types of system software:

## Slide 53: System Software
Image Source : https://eportfolio.utm.my/user/choy-wan-ling/chapter-5-system-software
What is System Software
System Software is a set of programs that control and manage the operations of computer hardware.
It also helps application programs to execute
correctly.
Example: Operating system, programming language, Communication software, etc.
Notes: What is software?
Software is the collection of data, programs, procedures, routines and instructions that tell a computer or electronic device how to run, work and execute specific tasks. This is in contrast to hardware, which is the physical system and components that perform the work.
System software is software that directly operates the computer hardware and provides the basic functionality to the users as well as to the other software to operate smoothly. Or in other words, system software basically controls a computer’s internal functioning and also controls hardware devices such as monitors, printers, and storage devices, etc. It is like an interface between hardware and user applications, it helps them to communicate with each other because hardware understands machine language(i.e. 1 or 0) whereas user applications are work in human-readable languages like English, Hindi, German, etc. so system software converts the human-readable language into machine language and vice versa.

## Slide 54: System Software
Types of System Software
Operating system
Device Driver
Language processors
System Software
Operating System
Device Driver
Language Processors
Notes: Types of system software:
It has two subtypes which are:
Operating System: It is the main program of a computer system. When the computer system ON it is the first software that loads into the computer’s memory. Basically, it manages all the resources such as memory, CPU, printer, hard disk, etc., and provides an interface to the user, which helps the user to interact with the computer system. It also provides various services to other computer software. Examples of operating systems are Linux, Apple macOS, Microsoft Windows, etc.
Language Processor: As we know that system software converts the human-readable language into a machine language and vice versa. So, the conversion is done by the language processor. It converts programs written in high-level programming languages like Java, C, C++, Python, etc(known as source code), into sets of instructions that are easily readable by machines(known as object code or machine code).
Device Driver: A device driver is a program or software that controls a device and helps that device to perform its functions. Every device like a printer, mouse, modem, etc. needs a driver to connect with the computer system eternally. So, when you connect a new device with your computer system, first you need to install the driver of that device so that your operating system knows how to control or manage that device.

## Slide 55: System Software
Features of System Software
System Software is closer to the system
Generally written in a low-level language
The system software is difficult to design and understand
Fast in speed
Less interactive
Smaller in size
Hard to manipulate
Image Source : https://eportfolio.utm.my/user/choy-wan-ling/chapter-5-system-software
Notes: Features of system software:
Let us discuss some of the features of System Software:
  System Software is closer to the computer system.
  System Software is written in a low-level language in general.
  System software is difficult to design and understand.
  System software is fast in speed(working speed).
  System software is less interactive for the users in comparison to application software.

## Slide 56: Distinguish between System Software and Application Software
https://www.technoganpat.in/2018/08/difference-between-systems-software-and-application
Application Software
What is Application Software?
Types of Application Software
Features of Application Software
Notes: In this section you learn about
What is Application Software?
Types of Application Software
Features of Application Software

## Slide 57: Application Software
Image source: https://images.saymedia-content.com/.image/ar_16:9%2Cc_fill%2Ccs_srgb%2Cq_auto:eco%2Cw_1200/MTc2NDU0MjY4MDgwNDMzMTE0/three-categories-of-application-software.png
what is Application Software ?
Application Software is a program that does real work for the user. It is mostly created to perform a specific task for a user.
Application Software acts as a mediator
between the end-user and System Software. It is also known as an application package.
This type of software is written using a high- level language like C, Java, VB. Net, etc.
Example: Word-processing, Spreadsheet, Database,
etc.
Notes: Application Software
Software that performs special functions or provides functions that are much more than the basic operation of the computer is known as application software. Or in other words, application software is designed to perform a specific task for end-users. It is a product or a program that is designed only to fulfill end-users’ requirements. It includes word processors, spreadsheets, database management, inventory, payroll programs, etc.

## Slide 58: Application Software
Types of Application Software ?
General Purpose Software E.g. MS word, Ms-Excel, Power Point
Customized Software E.g. railway reservation system, airline reservation system
Utilities software E.g. Antivirus, disk fragmented, memory tester, disk repair
Application Software
General purpose software
Customized software
Utilities software
Notes: Types of application software:
There are different types of application software and those are:
General Purpose Software: This type of application software is used for a variety of tasks and it is not limited to performing a specific task only. For example, MS-Word, MS-Excel, PowerPoint, etc.
Customized Software: This type of application software is used or designed to perform specific tasks or functions or designed for specific organizations. For example, railway reservation system, airline reservation system, invoice management system, etc.
Utility Software: This type of application software is used to support the computer infrastructure. It is designed to analyze, configure, optimize and maintains the system, and take care of its requirements as well. For example, antivirus, disk fragmenter, memory tester, disk repair, disk cleaners, registry cleaners, disk space analyzer, etc.

## Slide 59: Application Software
Feature of Application Software ?
An important feature of Application Software:
Perform more specialized tasks like word
processing, spreadsheets, email, photo editing, etc.
It needs more storage space as it is bigger in
size
Easy to design and more interactive for the user
Generally written in a high-level language
Image source: https://www.goodcore.co.uk/blog/wp-content/uploads/2019/08/types-of-software.png
Notes: Features of application software:
Let us discuss some of the features of Application Software:
An important feature of application software is it performs more specialized tasks like word processing, spreadsheets, email, etc.
Mostly, the size of the software is big, so it requires more storage space.
Application software is more interactive for the users, so it is easy to use and design.
The application software is easy to design and understand.
Application software is written in a high-level language in general.

## Slide 60: Distinguish between System Software and Application Software
System Software | Application Software
It is designed to manage the resources of the computer system, like memory and process management, etc | It is designed to full fill the requirements of the user for performing specific tasks.
Written in a low-level language | Written in a high-level language
Less interactive for the users | More interactive for the users
System software plays vital role for the effective functioning of a system | Application software is not so important for the functioning of the system, as it is task specific.
Notes: System Software
It is designed to manage the resources of the computer system, like memory and process management, etc
Written in a low-level language
Less interactive for the users
System software plays vital role for the effective functioning of a system
Application Software
It is designed to full fill the requirements of the user for performing specific tasks.
Written in a high-level language
More interactive for the users
Application software is not so important for the functioning of the system, as it is task specific.

## Slide 61: Operating System
Operating system
What is operating System
Types of Operating System
https://www.howtogeek.com/wp-content/uploads/2018/08/img_5b68e80f77e33.png?width=1198&trim=1,1&bg-color=000&pad=1,1
Notes: In this section we will discuss about the operating system and types of operating system
What is OS
Types of OS

## Slide 62: Operating System
What is Operating system
An operating system is a program that controls the execution of application programs and acts as an interface between the user of a computer and the computer hardware.
A more common definition is that the operating system is the one program running at all times on the computer (usually called the kernel), with all else being application programs.
https://www.howtogeek.com/wp-content/uploads/2018/08/img_5b68e80f77e33.png?width=1198&trim=1,1&bg-color=000&pad=1,1
Notes: Introduction to Operating system
An operating system acts as an intermediary between the user of a computer and computer hardware. The purpose of an operating system is to provide an environment in which a user can execute programs conveniently and efficiently.
An operating system is a software that manages computer hardware. The hardware must provide appropriate mechanisms to ensure the correct operation of the computer system and to prevent user programs from interfering with the proper operation of the system.
Operating System – Definition:
An operating system is a program that controls the execution of application programs and acts as an interface between the user of a computer and the computer hardware.
A more common definition is that the operating system is the one program running at all times on the computer (usually called the kernel), with all else being application programs.
An operating system is concerned with the allocation of resources and services, such as memory, processors, devices, and information. The operating system correspondingly includes programs to manage these resources, such as a traffic controller, a scheduler, a memory management module, I/O programs, and a file system.

## Slide 63: Operating System
Types of Operating system
Operating system
Batch operating system
Time Sharing OS
Network OS
RTOS
Notes: Types of Operating Systems: Some widely used operating systems are as follows-
Batch Operating System – This type of operating system does not interact with the computer directly. There is an operator which takes similar jobs having the same requirement and group them into batches. It is the responsibility of the operator to sort jobs with similar needs.
Examples of Batch based Operating System: Payroll System, Bank Statements, etc.
2. Time-Sharing Operating Systems – Each task is given some time to execute so that all the tasks work smoothly. Each user gets the time of CPU as they use a single system. These systems are also known as Multitasking Systems. The task can be from a single user or different users also. The time that each task gets to execute is called quantum. After this time interval is over OS switches over to the next task.
Examples of Time-Sharing OSs are: Multics, Unix, etc.
3. Network Operating System These systems run on a server and provide the capability to manage data, users, groups, security, applications, and other networking functions. These types of operating systems allow shared access of files, printers, security, applications, and other networking functions over a small private network. One more important aspect of Network Operating Systems is that all the users are well aware of the underlying configuration, of all other users within the network, their individual connections, etc. and that’s why these computers are popularly known as tightly coupled systems.
Examples of Network Operating System are: Microsoft Windows Server 2003, Microsoft Windows Server 2008, UNIX, Linux, Mac OS X, Novell NetWare, and BSD, etc.
4. Real-Time Operating System – These types of OSs serve real-time systems. The time interval required to process and respond to inputs is very small. This time interval is called response time.
Real-time systems are used when there are time requirements that are very strict like missile systems, air traffic control systems, robots, etc.

## Slide 64
Differentiate between Linux and Windows OS
Linux | Windows OS
Linux Is a open source operating system | While windows is licenced operating system
Linux is free of cost | While windows is paid and costly
Monolithic kernel used | Micro kernel used
Linux is more efficient compared to windows | Less efficient compared to linux
Provide more security than windows | While it provide less security than linux
Notes: Linux could be a free and open supply OS supported operating system standards. It provides programming interface still as programme compatible with operating system primarily based systems and provides giant selection applications. A UNIX operating system system additionally contains several severally developed parts, leading to UNIX operating system that is totally compatible and free from proprietary code.
Windows may be a commissioned OS within which ASCII text file is inaccessible. it’s designed for the people with the angle of getting no programming information and for business and alternative industrial users. it’s terribly straightforward and simple to use.
The distinction between Linux and Windows package is that Linux is completely freed from price whereas windows is marketable package and is expensive. Associate operating system could be a program meant to regulate the pc or computer hardware Associate behave as an treater between user and hardware.
Linux is a open supply package wherever users will access the ASCII text file and might improve the code victimisation the system. On the opposite hand, in windows, users can’t access ASCII text file, and it’s a authorized OS.

## Slide 65
Differentiate between 32 bit and 64 bit OS
32 bit OS | 64 bit OS
32 bit system can access 2^32 memory address. | 64 bit system can access 2^64 memory address.
Can Handle upto 4GB RAM data | Can Handle more than 4GB RAM data
A 32-bit processor system could properly run a 32-bit OS, but it cannot run the 64-bit OS at its full capability. | A 64-bit processor system can run either a 32-bit or 64-bit version of an installed operating system (OS).
The 64-bit programs and applications won't work. | The 32-bit programs and applications will work with no hassle.
It needs a 32-bit operating system. | This one can run on both 32-bit and the 64-bit operating system.
https://static.javatpoint.com/operating-system/images/32-bit-vs-64-bit-operating-system.png
Notes: Difference between 32-bit and 64-bit operating systems
In computing, there are two types of processors existing, i.e., 32-bit and 64-bit processors. These types of processors tell us how much memory a processor can access from a CPU register. For instance,
Most computers made in the 1990s and early 2000s were 32-bit machines. The CPU register stores memory addresses, which is how the processor accesses data from RAM. One bit in the register can reference an individual byte in memory, so a 32-bit system can address a maximum of 4 GB (4,294,967,296 bytes) of RAM. The actual limit is often less than around 3.5 GB since part of the register is used to store other temporary values besides memory addresses. Most computers released over the past two decades were built on a 32-bit architecture, hence most operating systems were designed to run on a 32-bit processor.
A 64-bit register can theoretically reference 18,446,744,073,709,551,616 bytes, or 17,179,869,184 GB (16 exabytes) of memory. This is several million times more than an average workstation would need to access. What’s important is that a 64-bit computer (which means it has a 64-bit processor) can access more than 4 GB of RAM. If a computer has 8 GB of RAM, it better has a 64-bit processor. Otherwise, at least 4 GB of the memory will be inaccessible by the CPU.
A major difference between 32-bit processors and 64-bit processors is the number of calculations per second they can perform, which affects the speed at which they can complete tasks. 64-bit processors can come in dual-core, quad-core, six-core, and eight-core versions for home computing. Multiple cores allow for an increased number of calculations per second that can be performed, which can increase the processing power and help make a computer run faster. Software programs that require many calculations to function smoothly can operate faster and more efficiently on the multi-core 64-bit processors, for the most part.
Advantages of 64-bit over 32-bit
Using 64-bit one can do a lot in multi-tasking, user can easily switch between various applications without any windows hanging problems.
Gamers can easily play High graphical games like Modern Warfare, GTA V, or use high-end software like Photoshop or CAD which takes a lot of memory since it makes multi-tasking with big software, easy and efficient for users. However, upgrading the video card instead of getting a 64-bit processor would be more beneficial.

## Slide 66: FDISK, Format, Scandisk commands
Disk Part command in windows 10 – fdisk command
The diskpart command interpreter helps you manage your computer's drives (disks, partitions, volumes, or virtual hard disks).
Disk Part, replacing its predecessor - fdisk, is a command-line utility that provides the ability to manage disks, partitions or volumes in your computer running all versions of the operating system since Windows 2000, also including the latest Windows 10.
Notes: The diskpart command interpreter helps you manage your computer's drives (disks, partitions, volumes, or virtual hard disks).
Disk Part, replacing its predecessor - fdisk, is a command-line utility that provides the ability to manage disks, partitions or volumes in your computer running all versions of the operating system since Windows 2000, also including the latest Windows 10.
FDISK
The fdisk command is used to create and delete partitions on the hard drive in earlier versions of MS-DOS and Windows.

## Slide 67: FDISK, Format, Scandisk commands
Using Disk management create partition
Disk Management is not as powerful as MiniTool Partition Wizard Free Edition, but as a Windows built-in partition manager, it can complete most simple and basic partition managements like create partition, delete partition, format partition, etc.
Notes: Disk Management is not as powerful as MiniTool Partition Wizard Free Edition, but as a Windows built-in partition manager, it can complete most simple and basic partition managements like create partition, delete partition, format partition, etc.

## Slide 68: FDISK, Format, Scandisk commands
Scandisk Command
Scandisk can improve the performance of your hard drive and help maintain the Windows file system.
Command Prompt, follow these steps:
Boot your computer.
Go to Start.->Run.->cmd in the box:
You can now type chkdsk to open the utility in a read-only mode. Press Enter.
To repair errors
Notes: Scandisk can improve the performance of your hard drive and help maintain the Windows file system.
Command Prompt, follow these steps:
Boot your computer.
Go to Start.->Run.->cmd in the box:
You can now type chkdsk to open the utility in a read-only mode. Press Enter.
To repair errors

## Slide 69: FDISK, Format, Scandisk commands
Format Command
The format command is used to erase information from a computer diskette or fixed drive.
Format
C:\WINDOWS\system32>format E:
E: is the drive letter
Notes: The format command is used to erase information from a computer diskette or fixed drive.
Format
C:\WINDOWS\system32>format E:
E: is the drive letter

## Slide 70: FAT System, NTFS and Directories, Fragmentation and defragmentation disk
What is directories
A directory is a location for storing files on your computer. Directories are found in a hierarchical file system such as Linux, DOS, and Unix
Pictured is an example of output from the Windows/DOS tree command. It shows all the local and subdirectories.
Reference: https://www.computerhope.com/jargon/d/director.htm
Notes: What is directories in operating system?
A directory is a location for storing files on your computer. Directories are found in a hierarchical file system, such as Linux, MS-DOS, OS/2, and Unix.
Pictured is an example of output from the Windows/DOS tree command. It shows all the local and subdirectories (e.g., the "big" directory in the "cdn" directory). When looking at this overview, the current directory is the root directory of the C: drive. It's called the "root" directory because there is nothing beneath it, and the other directories "branch" from it. If you are using an operating system with multiple user accounts, the directory may also be referred to as a home directory.

## Slide 71: FAT System, NTFS and Directories, Fragmentation and defragmentation disk
FAT File System
A disk formatted with FAT is allocated in clusters, whose size are determined by the size of the volume. When a file is created, an entry is created in the directory and the first cluster number containing data is established.
It is only used with FAT12 and FAT16, and imposes on the root directory a fixed maximum size which is pre-allocated at creation of this volume.
Image Source: http://www.c-jump.com/CIS24/Slides/FAT/lecture.html
Notes: A disk formatted with FAT is allocated in clusters, whose size are determined by the size of the volume. When a file is created, an entry is created in the directory and the first cluster number containing data is established.
1. FAT32 : FAT32 stands for File Allocation Table. FAT32 is an extension of previous file systems in which the data is stored in chunks of 32 bits. FAT32 is an upgraded version of FAT16 designed to overcome the limitations of FAT16 and add support for larger media. FAT32 was used in older versions of operating systems like Windows 95 up until Windows XP.
Advantages of FAT32 –
FAT32 efficiently work under partitions of 200 MB.
FAT32 provides compatibility with different operating systems.
FAT32 is frequently used as a primary partition on multiboot systems.
Disadvantages of FAT32 –
The partitions in FAT32 of size over 200 MB can degrade the performance.
FAT32 is insecure because of lack of encryption.
FAT32 is susceptible to fragmentation.

## Slide 72: FAT System, NTFS and Directories, Fragmentation and defragmentation disk
FAT File System
FAT32 stores the root directory in the Data Region, along with files and other directories, allowing it to grow without such a constraint.
Image Source: http://www.c-jump.com/CIS24/Slides/FAT/lecture.html
Notes: A disk formatted with FAT is allocated in clusters, whose size are determined by the size of the volume. When a file is created, an entry is created in the directory and the first cluster number containing data is established.
1. FAT32 : FAT32 stands for File Allocation Table. FAT32 is an extension of previous file systems in which the data is stored in chunks of 32 bits. FAT32 is an upgraded version of FAT16 designed to overcome the limitations of FAT16 and add support for larger media. FAT32 was used in older versions of operating systems like Windows 95 up until Windows XP.
Advantages of FAT32 –
FAT32 efficiently work under partitions of 200 MB.
FAT32 provides compatibility with different operating systems.
FAT32 is frequently used as a primary partition on multiboot systems.
Disadvantages of FAT32 –
The partitions in FAT32 of size over 200 MB can degrade the performance.
FAT32 is insecure because of lack of encryption.
FAT32 is susceptible to fragmentation.

## Slide 73: FAT System, NTFS and Directories, Fragmentation and defragmentation disk
NTFS
NT file system (NTFS), which is also sometimes
called the New Technology File System, is a process that the Windows NT operating system uses for storing, organizing, and finding files on a hard disk efficiently.
Image Source:https://www.kencorner.com/wp-content/uploads/2018/03/NTFSFileSystem.png
Notes: 2. NTFS : NTFS stands for New Technology File System. First introduced in 1993, it is used in newer versions of operating systems such as Windows NT and 2000 and later versions of Windows. NTFS is a more robust, high-performance logging file system with multi-user access control, ACLs, and many other things that make it appropriate to work with an Operating System that has protection. NTFS includes characteristics such as data recovery, multi-streaming, fault tolerance, security, extended file size, and file systems, UNICODE names. exFAT is used where NTFS is not feasible, due to its data-structure overhead, but a greater file-size limit than the standard FAT32 file system is needed.
Advantages of NTFS –
NTFS is highly secure because it prevents unauthorized access to file contents by enforcing Encryption File System(EFS).
NTFS performs well even in the partitions of size over 400 MB.
NTFS is less susceptible to fragmentation.
Disadvantages of NTFS –
NTFS is not extensively supported.
Performance in NTFS file system degrades under partitions of 400 MB.

## Slide 74: FAT System, NTFS and Directories, Fragmentation and defragmentation disk
Fragmentation and Defragmentation
Disk fragmentation occurs when a file is broken up into pieces to fit on the disk. Because files are constantly being written, deleted and resized, fragmentation is a natural occurrence.
When a file is spread out over several locations, it takes longer to read and write.
Image Source: https://windowsreport.com/windows-10-defrag-tools
Notes: Fragmentation
Fragmentation commonly occurs when old files are opened, modified and subsequently saved.
One example of this, would be where a previously saved file, let's say, a document, is opened and added to. This will cause the file to be larger in physical space than when it was first saved. The operating system will then break the file into 2 or more pieces, and store those pieces (fragments) in different parts of the storage area.
The file system, such as File Allocation Table (FAT) or NTFS, would then keep a record of where the different fragments of the file are stored.
When the operating system requires the file again, it will query the file system to find out where the different fragments of the file are located on the partition (drive).

## Slide 75: FAT System, NTFS and Directories, Fragmentation and defragmentation disk
Fragmentation and Defragmentation
the process of defragmentation rejoins the fragmented parts of a file. It loads the file fragments and then saves them in consecutive parts of the storage.
The process of defragmenting can be time consuming, but it is one of the easiest ways to increase the performance of your computer. The frequency at which a PC should be defragmented will directly depend on the amount of usage area.
Notes: Defragmentation
As noted above, the process of defragmentation rejoins the fragmented parts of a file. It loads the file fragments and then saves them in consecutive parts of the storage.
The process of defragmenting can be time consuming, but it is one of the easiest ways to increase the performance of your computer. The frequency at which a PC should be defragmented will directly depend on the amount of usage area.
Disk Defragmentation : In this process, all scattered fragments (data) rearrange in such that they come in sequence form with further utility program available in Windows. In this process program first, check percentage of the fragment available in disk then Defragment all disk as can as possible.

## Slide 76: Able to manage files effectively in Windows and Linux environment
(6 hours)
Notes: Title - The learning outcome
Subtitle - Duration

## Slide 77: In this section, we will discuss:
Functions of Key board and Mouse
Applications MS Paint/Note pad
Different text formats
Different image file formats
Advantages of compressing files
Distinguish between backup and cloning
Notes: Mention the parent topics one by one. This particular learning outcome has 6 parent topics.

## Slide 78: Functions of Key board and Mouse
What is a Computer Keyboard?
A keyboard is a peripheral device that enables a user to input text into a computer or any other electronic machinery.
It is a peripheral device that is the most basic way for the user to communicate with a computer.
Image Source:
https://www.ign.com/articles/best-keyboard
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
A keyboard is a peripheral device that enables a user to input text into a computer or any other electronic machinery. It is a peripheral device that is the most basic way for the user to communicate with a computer. It consists of multiple buttons, which create numbers, symbols, and letters, and special keys like the Windows and Alt key, including performing other functions.
A keyboard is connected to a computer system using a cable or a wireless connection.
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Reference:
https://www.ign.com/articles/best-keyboard

## Slide 79: Functions of Key board and Mouse
Categories of Keys on a Keyboard
Typing(alphanumeric) keys
Control keys
Function keys
Navigation keys
Numeric keypad
Other Keys( Shift, Caps Lock, Tab, Enter, spacebar, Backspace)
Image Source:
https://www.javatpoint.com/keyboard
Notes: This slide talks about the case if we have to divide a subtopic further.
Title Box - Parent Topic
Subtitle box - Sub Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Categories of keys:
Typing (alphanumeric) keys. These keys include the same letter, number, punctuation, and symbol keys found on a traditional typewriter.
Control keys. These keys are used alone or in combination with other keys to perform certain actions. The most frequently used control keys are Ctrl, Alt, the Windows logo key﻿ Picture of the Windows logo key, and Esc.
Function keys. The function keys are used to perform specific tasks. They are labeled as F1, F2, F3, and so on, up to F12. The functionality of these keys differs from program to program.
Navigation keys. These keys are used for moving around in documents or webpages and editing text. They include the arrow keys, Home, End, Page Up, Page Down, Delete, and Insert.
Numeric keypad. The numeric keypad is handy for entering numbers quickly. The keys are grouped together in a block like a conventional calculator or adding machine.
Reference:
https://www.javatpoint.com/keyboard

## Slide 80: Functions of Key board and Mouse
What are the Uses of Keyboard in Computer?
Input Date
Type Numbers
Text Chatting
Type Special Character
Types computer short cut Keys
Image Source:
https://www.computerhope.com/issues/ch001689.htm
Notes: Title Box - Parent Topic
Subtitle box - Sub Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
There are five uses of a keyboard in a computer, which are given below.
Input Date
Type Numbers
Text Chatting
Type Special Character
Types computer short cut Keys
Reference:
https://www.computerhope.com/issues/ch001689.htm

## Slide 81: Introduction to Internet, Browsing, and Emailing
Types of Keyboards
Gaming Keyboard
Mechanical Keyboard
Ergonomic Keyboard
Multimedia Keyboard
Hand Keyboard
Flexible Keyboards
Image Source:
https://www.computerhope.com/jargon/k/keyboard.htm
Notes: Title Box - Parent Topic
Subtitle box - Sub Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Type of Keyboards
Gaming keyboards are built with gamers in mind and come with extra features that are rare in normal keyboards
Mechanical keyboards are one of the types of important keyboards. They are expensive and require a little learning to understand how they work.
Ergonomic keyboards are not really a normal type of computer keyboard on their own, but rather refer to any keyboard that is designed to minimize stress and pain on your body and enhance comfort.
Multimedia keyboards are very similar to common keyboards but with the addition of a series of keys that allow you to control directly the most common functions of multimedia content players, such as Play, Stop, Resume, Rewind, Mute, Volume, etc.
Some keyboards look so unconventional cause they create a whole new category. Such as the AlphaGrip handheld keyboard, which combines the design of a game controller with the functions of a basic keyboard and ergonomic keyboard too.
Flexible Keyboard-These keyboards are very eye-catching for those who see them for the first time, stand out for their appearance and the material with which they are built by rubber, silicon and plastic
Reference:
https://www.computerhope.com/jargon/k/keyboard.htm

## Slide 82: Introduction to Internet, Browsing, and Emailing
Types of Keyboards
Wireless Keyboard
Laptop Keyboard
Laser virtual Keyboard
Image Source:
https://www.computerhope.com/jargon/k/keyboard.htm
Notes: Continuing from the last slide:
Title Box - Parent Topic
Subtitle box - Sub Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
A wireless keyboard works just like a wireless mouse; you plug a receiver into one of the USB ports on your computer.
The keyboard used in a laptop is called a laptop keyboard or QWERTY keyboard. The layout of the laptop keyboards is designed according to the size of the laptop slightly different from normal keyboards
A virtual keyboard is a computer keyboard that a user operates by typing on or within a wireless- or optical-detectable surface or area rather than by depressing physical keys
Reference:
https://www.computerhope.com/jargon/k/keyboard.htm

## Slide 83: Introduction to Internet, Browsing, and Emailing
Five Functions of Keyboard
Built-in functions
Boot sequence functions
Operation keystrokes
Shortcut commands
Specialty keys
Image Source:
https://www.advance-africa.com/images/xwindows1.png.pagespeed.ic.bg4V5WeD6K.jpg
Notes: Title Box - Parent Topic
Subtitle box - Sub Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Reference:
https://www.advance-africa.com/images/xwindows1.png.pagespeed.ic.bg4V5WeD6K.jpg
Functions of Keyboard
Built-in functions
Two common built-in functions are the Home and End keys. Pressing "Home" in any type of edit window will cause the cursor to jump to the beginning of the line you are editing, and pressing "End" will move the cursor to the end of the line. These functions are built into most every PC keyboard.
Boot sequence functions
When your PC is first booted up, the keyboard has a few important functions built into the BIOS, the interface between you and your computer. Commonly, the boot functions are F1 to continue, ESC to exit the current command, and F2 to enter the system setup. Keep in mind that the BIOS setup deals exclusively with the computer hardware and changes made to the BIOS could make the computer inoperable without major repairs.
Operation keystrokes.
A large number of computer programs use the F1 key as a universal help key. Likewise, pressing the ESC key will usually take you back to the previous step. Other function keys--F1 through F12--have typical functions, such as F8 saving a document. It is important to note that these functions are set by individual programs, and will vary from one application to the next.
Shortcut commands
Almost all programs allow basic keyboard commands. These commands include Ctrl+A to select and highlight all content, Ctrl+C to copy highlighted text, and Ctrl+V to paste text you have copied. You may be surprised to find out that more than half of your keys have functions associated with the CTRL key combination, and the help files of your software program will offer a complete list.
Specialty keys
Some keyboards now have specialty keys that give the user the ability to launch Internet functions or common computer programs. Your keyboard may have specialty keys that will launch your web browser, an email program or a chat program. You also may have keys that will launch your computer's calculator or shutdown your computer.

## Slide 84: Introduction to Internet, Browsing, and Emailing
Other Functions of Keyboard
Print Screen
Scroll Lock
Pause
Brightness UP & Down
Volume UP & Down
Image Source:
https://www.digitalcitizen.life/7-ways-change-volume-windows-both-pcs-tablets/
Notes: Title Box - Parent Topic
Subtitle box - Sub Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Other functions of keyboard
Print Screen
The Print Screen button is on every computer keyboard that is used to take a screenshot of the monitor screen.Screenshot means taking a photo of whatever is on the screen or whatever is going on the screen.
Scroll Lock
The Scroll Lock button is also on the keyboard of every computer, which is used to temporarily turn off the scrolling features.
Pause Button
The Pause button is also on the keyboard of every computer, which is used to pause something.
Brightness UP & Down
The Brightness Up & Down button is also on the keyboard of every computer, which is used to decrease or increases the light of the screen.
Volume UP & Down
Volume UP & Down button is also on the keyboard of every computer, which is used to increase or decrease the volume of the computer.
Reference:
https://www.digitalcitizen.life/7-ways-change-volume-windows-both-pcs-tablets/

## Slide 85: Functions of Key board and Mouse
How does Keyboard Works in Computer?
A keyboard contains many mechanical switches or push-buttons called "keys".
When one of these are pushed, an electrical circuit is closed, and the keyboard sends a signal to the computer that tells it what letter, number or symbol it would like to be shown on the screen.
Image Source:
https://www.engineersgarage.com/insight-how-computer-keyboard-works/
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Computer keyboard is an device used to convert the keystrokes in to the electrical signals that a computer can understand. There are special types of switches and circuits to do this. When we press a key, it completes its corresponding circuit and an electrical signal goes to keyboard’s internal processor which detects the key which is pressed.
Reference:
https://www.engineersgarage.com/insight-how-computer-keyboard-works

## Slide 86: Introduction to Internet, Browsing, and Emailing
Keyboard Advantages and Disadvantages
Advantages
User Friendly
Security
Visual Representation
Water Proof
Typing Errors
Image Source:
https://www.esis.com.au/computer-products/keyboards-pointing-devices/keyboards-mice-etc-industrial/waterproof-keyboards-plastic/
Notes: Title Box - Parent Topic
Subtitle box - Sub Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Advantages of Keyboard
User Friendly
A concept keyboard typically takes less time to learn compared to a standard keyboard.
Security
A concept keyboard makes sure that it is free of tampering. Whatever the information that is offered cannot be corrupted easily. Thus, customers information which are meant to be kept private are secured to a very high extent.
Visual Representation
Visual representations used in a concept keyboard is able to bring instant responses more than a traditional keyboard.
Water Proof
A concept keyboard on default is designed to withstand any environmental constraints. This includes water proof technology as well.
Typing Errors
Concept keyboards are also less vulnerable to typing errors.
Reference:
https://www.esis.com.au/computer-products/keyboards-pointing-devices/keyboards-mice-etc-industrial/waterproof-keyboards-plastic/

## Slide 87: Introduction to Internet, Browsing, and Emailing
Keyboard Advantages and Disadvantages
Disadvantages
Cost
Maintenance
Cleanliness
Text/Numeric Input
Health Risks
Image Source:
https://slidetodoc.com/lis-508-lecture-4-looking-at-a-computer/
Notes: Continuing from the last slide:
Title Box - Parent Topic
Subtitle box - Sub Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Disadvantages of Keyboard
Cost
The initial cost involved in a concept keyboard is much higher than a regular keyboard.
Maintenance
A concept keyboard uses pre-programmed icons to depict products of an organization. Therefore, whenever a new product is added or existing product is upgraded, the programming needs to be done accordingly. As a result, it could increase the long-term maintenance costs of an organization.
Cleanliness
It is difficult to maintain cleanliness when using a concept keyboard. A concept keyboard is used similar to a touchscreen.
Text/Numeric Input
A concept used according to a command line basis. Thus, a numeric or textual input keyboard is absent in a concept keyboard.
Reference:
https://slidetodoc.com/lis-508-lecture-4-looking-at-a-computer/

## Slide 88: Functions of Key board and Mouse
What is Computer Mouse?
A mouse is a pointing input device that controls the movement of the cursor or pointer on a display screen.
It controls the movement of the cursor on the computer screen and allows users to move and select folders, text, files, and icons on a computer.
Image Source:
https://www.uow.edu.au/student/learning-co-op/technology-and-software/mouse-buttons/
Notes: Left (White Color space):
Subtitle box - Sub Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
A mouse is a pointing input device that controls the movement of the cursor or pointer on a display screen
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Reference:
https://www.uow.edu.au/student/learning-co-op/technology-and-software/mouse-buttons/

## Slide 89: Functions of Key board and Mouse
What are the uses of a Mouse?
Move the mouse pointer
Select
Open or execute a program
Drag-and-drop
Hovering
Image Source:
https://www.barhamprimary.co.uk/page/?title=Computer+Mouse+and+Keyboard+Skills&pid=135
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Uses of Mouse:
Move the mouse pointer:
The main function of a mouse is to move the mouse cursor on the screen in the desired direction.
Select:
A mouse provides users the option to select the text, file, or folder and many files at once. For example, if you want to send multifile to anyone, you can select many files at once and can send them.
Open or execute a program:
You can open a folder, icon, or other objects by a mouse. You are required to move the cursor to a file, folder, or an icon, then double click on the object that you want to open or execute.
Drag-and-drop:
When you select something, it can also be moved from one location to another by using the drag-and-drop method. In this method, first, you need to highlight the file or an object that you want to move. Then, move this file while pressing the mouse button and drop it on the desired location.
Hovering:
When you move the mouse pointer on any object, hover changes the Color of links, and by clicking on that link, you can go on the destination page.
Reference:
https://www.barhamprimary.co.uk/page/?title=Computer+Mouse+and+Keyboard+Skills&pid=135

## Slide 90: Functions of Key board and Mouse
What are the uses of a Mouse?
Scroll Up & Down
Perform other functions
Playing Game
Combination Activities
Image Source:
http://lazplanet.blogspot.com/2017/05/make-simple-image-zoomer-in-5-minutes.html
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Scroll Up & Down:
If you are viewing a long web page or working with a large document, you need to scroll up or down a page. The mouse's scroll button helps to up and down your document page; otherwise, you can also click and drag the scroll bar.
Perform other functions:
Most of the desktop mouse contains buttons, which can perform any function by programming them according to the requirement. For instance, on the thumb portion, many mouses have two side buttons that can be programmed to go back on web pages.
Playing Game:
A mouse provides users the option to play various games like chase games, in which a mouse is used to select any particular objects.
Combination Activities:
A mouse can be used in many combination activities like, Ctrl + Mouse click can be used for the hyperlink in new windows.
Reference:
http://lazplanet.blogspot.com/2017/05/make-simple-image-zoomer-in-5-minutes.html

## Slide 91: Functions of Key board and Mouse
Computer Mouse Parts with their Functions
Buttons
Ball/laser/LED
Mouse Wheel
Printed Circuit Board
Cable/Wireless Receiver
Battery
Microprocessor
Image Source:
https://www.nidirect.gov.uk/articles/keyboard-and-mouse-basics
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Computer parts and therir functions
Buttons:
Now these days, every mouse has two buttons, one is left and other right. With the help of these buttons, users can be manipulating any objects and text as well.
Ball/laser/LED:
In mechanical mouse have rubber ball that roll on the surface things such as table. In the optical mouse have laser or LED, these parts allow to mouse for movement on x-axis and y-axis directions, and its parallel move the mouse cursor on the computer screen.
Mouse Wheel:
Main objective of wheel in mouse for scroll your document page up and down direction.
Printed Circuit Board:
This board is placed inside of mouse chasses, in that board all electronics components embedded such as capacitor, diode, and register etc. This board takes input in the form of electronics signals when user given instructions by mouse such as clicking, scrolling, and more.
Cable/Wireless Receiver:
Corded mouse have cable for plugging with computer. If your mouse is wireless then require the USB receiver for getting the broadcasted signals such as (Infrared, Bluetooth, Radio signals), and then give input to computer.
Battery:
This component is used in the wireless mouse for running stages. if its battery get down then mouse will not working properly.
Microprocessor:
This is a processor that is embedded on the circuit board of mouse. Microprocessor is the brain of mouse, because without microprocessor all components of mouse are workless.
Reference:
https://www.nidirect.gov.uk/articles/keyboard-and-mouse-basics

## Slide 92: Functions of Key board and Mouse
Types of Mouse
Optical Mouse
Gaming Mouse
Wireless Mouse
Laser Mouse
Trackball Mouse
Ergonomic Mouse
Image Source:
https://scoopten.com/what-is-computer-mouse-types/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Types of Mouse
An optical mouse is a computer mouse which uses a light source, typically a light-emitting diode, and a light detector, such as an array of photodiodes, to detect movement relative to a surface
A gaming mouse is essentially, from one angle, just a desktop mouse with a few additional functions which make it suited to computer gaming or high intensity programming.
A Wireless mouse that connects to the computer without a cord. They can also be used with a computer that has Bluetooth from the factory or via an adapter. Wireless mice that use other radio frequencies (RF) come with their own transceiver that plugs into the USB port of the computer.
A laser mouse is a type of optical mouse that uses laser light to detect mouse movement.
A trackball is a computer cursor control device used in many notebook and laptop computers. The trackball is usually located in front of the keyboard toward the user.
The ergonomic mouse model is ideal for people who feel pain in their posture while using the mouse in front of the computer. It is known as a vertical mouse due to its ergonomic posture.
Reference:
https://scoopten.com/what-is-computer-mouse-types/

## Slide 93: Functions of Key board and Mouse
Types of Mouse
3D Mouse
Mechanical Mouse
Roller Bar Mouse
Finger Mouse
Pen Mouse (Stylus)
Image Source:
https://scoopten.com/what-is-computer-mouse-types/
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
A 3D mouse is a pointing and control device specialized for movement in virtual 3D (three-dimensional) environments. 3D mouse devices have used a number of different means to control 3D movement as well as 2D pointing, including multi-axis sensors, accelerometers, IR lights and IR sensors.
The mechanical mouse is also known as a ball mouse because it contains a plastic sphere in its lower part. This computer mouse works through a ball located at the bottom, and when it turns, it activates small rollers in charge of transmitting the movement to the computer.
A Roll Bar Mouse sits directly in front of your keyboard allowing you to use either or both hands together to point, click and scroll.
The Finger mouse is very small in size with an optical LED light for functioning. One can use finger mice by wearing its band for any finger size since it is adjustable. They can wireless or wired USB and needs a AAA battery
A stylus is a small pen-like shaped device. These types of mice are also known as stylus pens or GStick mice
Reference:
https://scoopten.com/what-is-computer-mouse-types/

## Slide 94: Functions of Key board and Mouse
How does Mouse Works in Computer?
Able to work on almost any surface, the mouse has a small, red light-emitting diode (LED) that bounces light off that surface onto a (CMOS) sensor.
The computer moves the cursor on the screen based on the coordinates received from the mouse.
Image Source:
https://www.quora.com/What-are-the-different-types-of-mouse
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
The LED installed at the bottom of the mouse emits a bright light in the downward direction. Since a mouse is usually used on plain surfaces, the light bounces back from the surface and enters a photocell that’s also mounted on the bottom, almost next to the LED
Reference:
https://www.quora.com/What-are-the-different-types-of-mouse

## Slide 95: Functions of Key board and Mouse
Mouse Advantages and Disadvantages
Advantages
It is easier to use and handle a mouse as compared to the keyboard.
Mouse requires less space.
Mouse can be used to draw graphics.
Mouse is light to carry. Therefore it is portable.
They can be easily connected to any devices with USB port.
Image Source:
https://slideplayer.com/slide/7606416/25/images/9/Mouse+Advantages+Disadvantages.jpg
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Advantages of Mouse:
Mostly use with desktop computer systems.
When buy new brand computer then get mouse with computer.
No need more training for using it.
Solve many problems when use mouse while keyboard’s keys.
Freedom for movement flexibility.
Freedom for selection of mouse according user’s comfortable because mouse have huge varieties are available in the market.
Portability- Easy to carry one place to another place.
Most preferred device for graphic applications areas.
Some multi-function mouse provides to users more flexibilities for cursor movement.
Having faster to traditional mouse.
No need more space for using it.
Low cost.
Easy to operate indoor and outdoor areas
Reference:
https://slideplayer.com/slide/7606416/25/images/9/Mouse+Advantages+Disadvantages.jpg

## Slide 96: Functions of Key board and Mouse
Mouse Advantages and Disadvantages
Disadvantages
The wired mouse is delicate in nature and must be used carefully as it can be damaged easily
If the batteries are low they tend to lose their accuracy and speed.
Wireless mouse can sometimes face connectivity issues.
Mouse cannot enter text data into the computer.
Image Source:
https://www.shutterstock.com/image-photo/inside-laptop-mouse-damaged-1905599818
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Disadvantages of Mouse:
Need flat surface.
Need services regular basis.
More dust sensitive.
Some time, dragging operations is difficult by user.
Mouse can be damaged easily.
May be, can be eye sight problems due to more use of mouse rotation.
Need little space for using.
Palm can be getting pain due to use mouse long time.
Not easy task for giving text input to computer.
Getting very low performance due to virus infection.
Reference:
https://www.shutterstock.com/image-photo/inside-laptop-mouse-damaged-1905599818

## Slide 97: Applications MS Paint/Notepad
What is MS Paint?
MS Paint is a simple program that allows users to create basic graphic art on a computer.
Images created within MS Paint are typically saved as GIF, Windows bitmap, PNG, TIFF or JPEG files.
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 2
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
MS Paint is a simple program that allows users to create basic graphic art on a computer
Reference:

## Slide 98: Applications MS Paint/Notepad
Tools of MS Paint
Free-Form Select and Select Tool
Eraser/Colour Eraser
Pick Colour
Pencil
Airbrush
Fill With Colour
Image Source:
https://www.electronicsandcommunications.com/2020/08/microsoft-paint-tutorial-for-beginners.html
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Ms Paint Tools:
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Free Form Tool:
The free form select tool allows you to select part of the picture (to move, copy or edit it). After selecting this tool, you can drag the free form shape around the picture to select any portion of it.
Select Tool:
The select tool selects rectangular parts of the picture. You first click on this and then drag a rectangle around the picture part.
Eraser Tool:
The Eraser tool when picked allows you to erase the portion of the picture over which it is dragged.
Fill with Colour:
The fill with colour tool fills part of the picture with foreground colour. To fill an object, it should be a closed figure with no gaps.
Pick Colour:
The pick colour tool allows you to select foreground or background colour from the picture itself. Select pick colour tool. To select foreground colour left click on colour in picture. To select background colour right click on colour in the picture.
Reference:
https://www.electronicsandcommunications.com/2020/08/microsoft-paint-tutorial-for-beginners.html

## Slide 99: Applications MS Paint/Notepad
Tools of MS Paint
Magnifier
Brush
Text
Curve Tool
Shapes(Line,Rectangle,Ellipse,Polygon)
Image Source:
https://www.electronicsandcommunications.com/2020/08/microsoft-paint-tutorial-for-beginners.html
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Magnifier
The magnifier tool when selected and clicked on the picture will magnify it.
Pencil
The pencil tool can be used to draw free form lines.
Brush
The brush tool can be used to draw with brush.
Text Tool
The text tool allows you to add text in picture. After selecting text tool, select foreground colour, drag rectangle in drawing area to hold the text. You can type a text in this box.
Line Tool:
For drawing a line. To make your line straight, hold down the Shift key and then drag your mouse holding the left button. Select the thickness of the line below the toolbox.
Rectangle Tool:
For making rectangles. You can also draw a square by holding the Shift key.
Polygon Tool: For drawing a polygon, but still you can draw a lot of other objects.
Rounded Rectangle: This tool helps you to draw a rectangle with rounded corners.
Reference:
https://www.electronicsandcommunications.com/2020/08/microsoft-paint-tutorial-for-beginners.html

## Slide 100: Applications MS Paint/Notepad
What is Notepad?
Notepad is a generic text editor included with all versions of Microsoft Windows that allows you to create, open, and read plaintext files.
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Notepad is a generic text editor included with all versions of Microsoft Windows that allows you to create, open, and read plaintext files
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 101: Applications MS Paint/Notepad
How to use Notepad?
Create, open, and save text files with Notepad
simple text edits
Turn Word Wrap on or off
Change the font of the text document
Print text files
Image Source:
https://www.howtogeek.com/258545/how-to-use-notepad-to-create-a-dated-log-or-journal-file/
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Ways to Open Notepad on Your Windows 10
Turn Notepad on in the Start menu. Select the Start button on the taskbar and then choose Notepad.
Find it by searching.
Open Notepad by right-clicking a blank area.
Press Windows(logo)+R, type notepad and then select OK.
Select Start.
Reference:
https://www.howtogeek.com/258545/how-to-use-notepad-to-create-a-dated-log-or-journal-file/

## Slide 102: Different text formats
What is the text-based formats?
Text based also refers to documents that contain only text, such as program source code, batch and shell scripts as well as HTML and XML files.
Text-based documents are readable in any text editor and most word processors.
Image Source:
https://www.bleepingcomputer.com/news/microsoft/windows-10-notepad-is-getting-better-utf-8-encoding-support/
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 3
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Text based also refers to documents that contain only text, such as program source code, batch and shell scripts as well as HTML and XML files
Reference:
https://www.bleepingcomputer.com/news/microsoft/windows-10-notepad-is-getting-better-utf-8-encoding-support/

## Slide 103: Different text formats
File format extensions for text files
.doc and .docx - Microsoft Word file
.odt - OpenOffice Writer document file
.pdf - PDF file
.rtf - Rich Text Format
.tex - A LaTeX document file
.txt - Plain text file
.wpd - WordPerfect document
Image Source:
https://filesconverter.com/text-formats
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
File format extensions for text files
TXT is a typical plain text file.
RTF is a common, convertible rich text format, with selection of captions, font types and sizes, page layout etc.
DOC/DOCX are binary rich formats for office text files supported primarily by Microsoft Office Word and other Word-compatible text editors.
ODT is a freeware alternative for DOC, provided by OpenOffice.org software and its clones such as LibreOffice. It is also a binary formatted rich text document.
PDF is a “physical” layout format for electronic documents, with a standard for its tags and properties. You can either view PDF files as documents or print these files as physical pages.
XML is a tag-based format that is like HTML. Its primary purpose is to create configuration files and text documentation for different software.
Reference:
https://filesconverter.com/text-formats

## Slide 104: Different image formats
What is the image-based formats?
Image Format describes how data related to the image will be stored.
Data can be stored in compressed, Uncompressed or vector format.
Image Source:
https://dlpng.com/png/6589946
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 4
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Image Format describes how data related to the image will be stored. Data can be stored in compressed, Uncompressed or vector format
Reference:
https://dlpng.com/png/6589946

## Slide 105: Different text formats
File format extensions for image files
.ai - Adobe Illustrator file
.bmp - Bitmap image
.gif - GIF image
.ico - Icon file
.jpeg or .jpg - JPEG image
Image Source:
https://99designs.com/blog/tips/image-file-types/
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
File format extensions for image files
JPEG (.jpg, .jpeg)
Joint Photographic Experts Group is a loss-prone (lossy) format in which data is lost to reduce size of image. Due to compression, some data is lost but that loss is very less. It is a very common format and are good for digital cameras, nonprofessional prints, E-Mail, PowerPoint etc., making it ideal for web use.
GIF (.gif)
GIF or Graphics Interchange Format files are used for web graphics. They can be animated and are limited to only 256 colors, can allow for transparency. GIF files are typically small is size and are portable.
Bitmap (.bmp)
Bit Map Image file is developed by Microsoft for windows. It is same as TIFF due lossless, no compression property. Due to BMP being a proprietary format, it is generally recommended to use TIFF files.
EPS (.eps)
Encapsulated PostScript file is a common vector file type. EPS files can be opened in applications such as Adobe Illustrator or CorelDRAW.
RAW Image Files (. raw, .cr2, .nef, .orf, .sr2)
These Files are unprocessed created by a camera or scanner.
Reference:
https://99designs.com/blog/tips/image-file-types/

## Slide 106: Different text formats
File format extensions for image files
.png - PNG image
.ps - PostScript file
.psd - PSD image
.svg - Scalable Vector Graphics file
.tif or .tiff - TIFF image
Image Source:
https://www.firevista.com/list-of-all-image-formats/
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
TIFF(.tif, .tiff)
Tagged Image File Format this format store image data without losing any data. It do not perform any compression on images have a high-quality image is obtained but size of image is also large, which is good for printing, professional printing.
PNG (.png)
PNG or Portable Network Graphics files are a lossless image format. It was designed to replace gif format as gif supported 256 colors unlike PNG which support 16 million colors.
SVG:
Scalable Vector Graphics is an XML-based vector image format for two-dimensional graphics with support for interactivity and animation.
Reference:
https://www.firevista.com/list-of-all-image-formats/

## Slide 107: Advantages of compressing files
What Is a Compressed File?
A compressed file is any file containing one or more files or directory that is smaller than their original file size.
Image Source:
https://www.howtogeek.com/178146/htg-explains-everything-you-need-to-know-about-zipped-files/
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 5
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
A compressed file is any file which is smaller than its original size and could contain one or more files, or even a directory
Reference:
https://www.howtogeek.com/178146/htg-explains-everything-you-need-to-know-about-zipped-files/

## Slide 108: Advantages of compressing files
Why Compress Files?
A compressed file takes up less storage space
Several files and folders are combined into one package that is easy to manage
Image Source:
https://www.khanacademy.org/computing/computers-and-internet/
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Compressing is mainly used for the following purposes:
A compressed file takes up less storage space. A smaller file can be transferred faster between locations e.g., on the Internet.
Several files and folders are combined into one package that is easy to manage; it is usually easier to handle one file than a set of, say, 10,000 files.
Reference:
https://www.khanacademy.org/computing/computers-and-internet/

## Slide 109: Advantages of compressing files
How Does Compression Work?
Data compression is a means of altering or encoding structured data to take up less disk space when stored on a computer-based system.
Types of Compression
Lossless Compression
Lossy Compression
Image Source:
https://developer.apple.com/documentation/compression
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Data compression is a means of altering or encoding structured data to take up less disk space when stored on a computer-based system.
Lossless compression is a class of data compression that allows the original data to be perfectly reconstructed from the compressed data.
Lossy compression is a method of data compression in which the size of the file is reduced by eliminating data in the file.
Reference:
https://developer.apple.com/documentation/compression

## Slide 110: Advantages of compressing files
Common Compression and Extraction Methods
zip
rar
gz
7z
Image Source:
https://www.maketecheasier.com/7-zip-vs-winrar-vs-winzip/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
ZIP is an archive file format that supports lossless data compression. A ZIP file may contain one or more files or directories that may have been compressed.
A RAR file (short for a Roshal Archive Compressed file) is a compressed file, or data container, that holds one or more other files and folders inside of it.
gzip is a file format and a software application used for file compression and decompression.
7z is a compressed archive file format that supports several different data compression, encryption and pre-processing algorithms..
Reference:
https://www.maketecheasier.com/7-zip-vs-winrar-vs-winzip

## Slide 111: Advantages of compressing files
Advantages & Disadvantages of Using File Compression
Advantages
Increased computing efficiency
Quicker transfers
Improved file integrity
Email/webpage accessibility
Image Source:
https://www.rfwireless-world.com/Terminology/Advantages-and-Disadvantages-of-Data-Compression.html
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Advantages of File Compression
Increased computing efficiency
Compressed data permits users to back-up and store data faster, especially when dealing with larger files. Note: The advantage of compressing digital video is becoming more useful as video sales letters (VSLs) and personalized videos become more prevalent.
Quicker transfers
Not only does file compression enable you to move files around on a local device more efficiently, it also enables you to send large documents and data faster over the internet.
Improved file integrity
Uncompressed files can often become corrupt when sent over the web. Zipped files serve to preserve the integrity of your files and make sure your data goes uncorrupted.
Email/webpage accessibility
It’s easier to compress larger files when uploading them to a webpage or sending them via email. Also, as previously mentioned, the most common email systems restrict the size of attachments. So, compression offers a way to send multiple files collectively, instead of one by one.
Reference:
https://www.rfwireless-world.com/Terminology/Advantages-and-Disadvantages-of-Data-Compression.html

## Slide 112: Advantages of compressing files
Advantages & Disadvantages of Using File Compression
Disadvantages
Memory Issue
Speed
File Size
Viruses and Malware
File Transfer
Image Source:
https://image.slidesharecdn.com/final-302-181124182547/95/file-compression-zip-file-15-638.jpg?cb=1543084052
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Disadvantage of File Compression
Memory Issue
When uncompressing a file for reading, your computer uses more memory to complete the task. During the uncompressing process, your computer will pause and allocate any free memory to complete the task. You may encounter one or more "Low Resources" or "Out of Memory" errors if your computer doesn't have enough memory. The errors also occur if you have multiple applications running at the same time while your computer is processing the compressed file.
Speed
The uncompressing process not only uses memory but also processor time. The process is slow and is a disadvantage when you are trying to access a file quickly. The processing time varies due to file size and the method used to compress the file. Also, running multiple applications on your system during the uncompressing process makes the task run longer.
File Size
An increase in file size is another disadvantage of compressing files. In some situations including compressing video and audio files, the file you are compressing cannot be made smaller, resulting in a compressed file that is larger in size than the original file.
Viruses and Malware
Your computer's anti-virus program may not be able to scan a compressed file for viruses and other malware, resulting in your computer being exposed to files that may contain viruses, Trojans, spyware and other harmful programs. These types of programs can destroy your computer. Compressed files from unknown sources should be uncompressed only after a complete scan with an anti-virus program that is capable of scanning the compact files.
File Transfer
If you send a compressed file to someone else via the Internet, email or on a computer network, that person may not be able to open the file if they don't have a program to uncompress it. This disadvantage is easily resolved by including a link to download a free or shareware program to uncompressed the file
Reference:
https://image.slidesharecdn.com/final-302-181124182547/95/file-compression-zip-file-15-638.jpg?cb=1543084052

## Slide 113: Advantages of compressing files
Difference between the Zip and Rar format
ZIP and RAR are widely used file formats for data compression and archive.
ZIP supports lossless data compression. Whereas, RAR supports data compression, error recovery and file spanning.
Image Source:
https://tech-blogs.com/the-little-known-difference-between-rar-and-zip/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
ZIP is the most widely used file format used for lossless data compression and has been around longer than RAR, and it still accounts for a significant number of archive files on the internet. However, RAR has better compression speed, better encryption, and lower rate of data loss.
Reference:
https://tech-blogs.com/the-little-known-difference-between-rar-and-zip/

## Slide 114: Distinguish between backup and cloning
What is Backup?
Backup is the process of creating a copy of the data on your system that you use for recovery in case your original data is lost or corrupted.
You can also use backup to recover copies of older files if you have deleted them from your system.
Image Source:
https://us.norton.com/content/norton-msm/us/en-us/home/internetsecurity/how-to/the-importance-of-data-back-up.html/?lg=en&ct=US&cs=true
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 6
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Backup is the process of creating a copy of the data on your system that you use for recovery in case your original data is lost or corrupted.
Reference:
https://us.norton.com/content/norton-msm/us/en-us/home/internetsecurity/how-to/the-importance-of-data-back-up.html/?lg=en&ct=US&cs=true

## Slide 115: Distinguish between backup and cloning
Why should I back up my data?
Data loss prevention
Natural disaster
Hard drive Fails
Lost devices
Tax reporting and audits
Cyberthreats
Image Source:
https://www.g2.com/articles/what-is-backup
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
A computer could stop working at any time, and data on a hard drive could become corrupted or lost if the hard drive fails. When hardware or the computer stops working, data on the computer could be lost.
Reference:
https://www.g2.com/articles/what-is-backup

## Slide 116: Distinguish between backup and cloning
Types of Backups
Full backup
Differential backup
Incremental backup
Image Source:
https://spanning.com/blog/types-of-backup-understanding-full-differential-incremental-backup/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Types of Backups
Full Backup
A full backup is the most complete type of backup where you clone all the selected data. This includes files, folders, SaaS applications, hard drives and more. The highlight of a full backup is the minimal time it requires to restore data.
Differential Backup
A differential backup straddles the line between a full and an incremental backup. This type of backup involves backing up data that was created or changed since the last full backup.
Incremental Backup
An Incremental Backup is a backup of all changed files since the last Full or Incremental backup.
Reference:
https://spanning.com/blog/types-of-backup-understanding-full-differential-incremental-backup

## Slide 117: Distinguish between backup and cloning
Advantages and disadvantages of backup
Advantages
Quick Access to Files
Protection Against Power Failures
Added Anti-Virus Protection
Safeguard Against Failed Hard Drive
Recovery if Operating System Fails
Image Source:
https://www.techtarget.com/searchdatabackup/feature/Full-incremental-or-differential-How-to-choose-the-correct-backup-type
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Advantages of Backup:
Full Backup
This backup provides the best protection for your data. No matter what happens to your hardware, you know you’ll have a complete copy of all the company information you need.
Differential Backup
When compared to incremental backups, this form requires less time to restore and can offer you different versions of the same files.
Incremental Backup
These backups require far less time and storage to create more compact copies of data.
Reference:
https://www.techtarget.com/searchdatabackup/feature/Full-incremental-or-differential-How-to-choose-the-correct-backup-type

## Slide 118: Distinguish between backup and cloning
Advantages and disadvantages of backup
Disadvantages
Hardware failure
Hidden costs
Failed recoveries
Image Source:
https://www.webwerks.in/blogs/advantages-and-disadvantages-cloud-backup-services
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Disadvantages of Backup
Full Backup
Because these backups replicate so much information, they require a lot of storage space, time, and financial investment to complete.
Differential Backup
Because you’re backing up more data, these backups can consume far more storage space over time in comparison to incremental backups.
Incremental Backup
The time you save in making the backup is added to the time necessary to restore the data. If you want to review the files that were backed up incrementally on Monday, you’d first need to restore the full backup from Friday and move on from there.
Reference:
https://www.webwerks.in/blogs/advantages-and-disadvantages-cloud-backup-services

## Slide 119: Distinguish between backup and cloning
What is Cloning?
Cloning is also used to describe the act of making the exact copy of a directory file or disk inclusive of any subdirectories or files within the disk or directory.
Image Source:
https://www.ubackup.com/clone/clone-old-computer-to-a-new-one-4348.html
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Cloning is also used to describe the act of making the exact copy of a directory file or disk inclusive of any subdirectories or files within the disk or directory.
Reference:
https://www.ubackup.com/clone/clone-old-computer-to-a-new-one-4348.html

## Slide 120: Distinguish between backup and cloning
Simple steps with cloning software
Install all desired programs and files to a master computer
Use software create an image of the master computer's hard disk.
Clone the image to the other computers.
Image Source:
https://www.ubackup.com/windows-10/clone-hard-drive-windows-10-0528.html
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Simple steps with cloning software
Install all desired programs and files to a master computer
Use software create an image of the master computer's hard disk.
Clone the image to the other computers
Reference:
https://www.ubackup.com/windows-10/clone-hard-drive-windows-10-0528.html

## Slide 121: Distinguish between backup and cloning
Advantages and disadvantages of Cloning
Advantages
A faulty computer can be wiped clean of data and restored from the untouched master image
Don't have to waste the installing individual applications to new computers.
A comprehensive backup of operating systems and installed softwares
Image Source:
https://www.ubackup.com/features/disk-clone.html
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Advantages of Cloning:
A faulty computer can be wiped clean of data and restored from the untouched master image
Don't have to waste the installing individual applications to new computers.
A comprehensive backup of operating systems and installed softwares
Reference:
https://www.ubackup.com/features/disk-clone.html

## Slide 122: Distinguish between backup and cloning
Advantages and disadvantages of Cloning
Disadvantages
Need to have a high number of the same hardware for the same image
Must have dedicated IT staff when dealing with more than just a few computers
Image Source:
https://www.slideshare.net/jagjitsingh2010/cloning-4
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Disadvantages of Cloning:
Need to have a high number of the same hardware for the same image
Must have dedicated IT staff when dealing with more than just a few computers
Care must be given to ensure the master image reliable and uncorrupted
Isn’t appropriate for daily backups.
Reference:
https://www.slideshare.net/jagjitsingh2010/cloning-4

## Slide 123: Distinguish between backup and cloning
Backup Vs Clone
A backup disk creates an image file. You can use this to recover data if there’s an emergency.
Cloning copies data from one hard disk to another, if you want to change the drive.
Image Source:
https://recoverit.wondershare.com/harddrive-backup/backup-vs-clone.html
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
A backup disk creates an image file. You can use this to recover data if there's an emergency. Cloning copies data from one hard disk to another, if you want to change the drive.
Reference:
https://recoverit.wondershare.com/harddrive-backup/backup-vs-clone.html

## Slide 124: Able to work with Linux environment by using Linux commands.
(6 hours)
Notes: Title - The learning outcome
Subtitle - Duration

## Slide 125: In this section, we will discuss:
Introduction to Linux operating system
Familiarization with GUI environment
Syntax of shell commands
Shell Scripting
Notes: Mention the parent topics one by one. This particular learning outcome has 4 parent topics.

## Slide 126: Introduction to Linux operating system
What is an Operating System?
Operating System is defined as a collection of programs that coordinates the operations of computer hardware and software.
It acts as a bridge for the interface between man and machine.
Image Source:
https://www.guru99.com/introduction-linux.html
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
An operating system is system software that manages computer hardware, software resources, and provides common services for computer programs
Reference:
https://www.guru99.com/introduction-linux.html

## Slide 127: Introduction to Linux operating system
Types of Operating System (OS)
Batch Operating System
Multitasking/Time Sharing OS
Multiprocessing OS
Real Time OS
Distributed OS
Network OS
Image Source:
https://www.tutorialandexample.com/types-of-operating-system/
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Types of Operating System
Batch Operating System
Some computer processes are very lengthy and time-consuming. To speed the same process, a job with a similar type of needs are batched together and run as a group.
The user of a batch operating system never directly interacts with the computer. In this type of OS, every user prepares his or her job on an offline device like a punch card and submit it to the computer operator.
Multi-Tasking/Time-sharing Operating systems
Time-sharing operating system enables people located at a different terminal(shell) to use a single computer system at the same time. The processor time (CPU) which is shared among multiple users is termed as time sharing
.
Real time OS
A real time operating system time interval to process and respond to inputs is very small. Examples: Military Software Systems, Space Software Systems are the Real time OS example.
Distributed Operating System
Distributed systems use many processors located in different machines to provide very fast computation to its users.
Network Operating System
Network Operating System runs on a server. It provides the capability to serve to manage data, user, groups, security, application, and other networking functions.
Mobile OS
Mobile operating systems are those OS which is especially that are designed to power smartphones, tablets, and wearables devices.
Some most famous mobile operating systems are Android and iOS, but others include BlackBerry, Web, and watchOS.
Reference:
https://www.tutorialandexample.com/types-of-operating-system/

## Slide 128: Introduction to Linux operating system
Functions of Operating System
Process management
Memory management
File management
Device Management
I/O System Management
Secondary-Storage Management
Image Source:
https://www.tutorialandexample.com/functions-of-the-operating-system/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Functions of Operating System
Process management:
Process management helps OS to create and delete processes. It also provides mechanisms for synchronization and communication among processes.
Memory management:
Memory management module performs the task of allocation and de-allocation of memory space to programs in need of this resources.
File management:
It manages all the file-related activities such as organization storage, retrieval, naming, sharing, and protection of files.
Device Management:
Device management keeps tracks of all devices. This module also responsible for this task is known as the I/O controller. It also performs the task of allocation and de-allocation of the devices.
I/O System Management:
One of the main objects of any OS is to hide the peculiarities of that hardware devices from the user.
Secondary-Storage Management:
Systems have several levels of storage which includes primary storage, secondary storage, and cache storage. Instructions and data must be stored in primary storage or cache so that a running program can reference it.
Reference:
https://www.tutorialandexample.com/functions-of-the-operating-system/

## Slide 129: Introduction to Linux operating system
Functions of Operating System
Security
Command interpretation
Networking
Job accounting
Communication management
Image Source:
https://kullabs.com/class-miscellaneous/teacher-training/digital-literacy/introduction-and-function-of-operating-system
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Security:
Security module protects the data and information of a computer system against malware threat and authorized access.
Command interpretation:
This module is interpreting commands given by the and acting system resources to process those commands.
Networking:
A distributed system is a group of processors which do not share memory, hardware devices, or a clock. The processors communicate with one another through the network.
Job accounting:
Keeping track of time & resource used by various job and users.
Communication management:
Coordination and assignment of compilers, interpreters, and another software resource of the various users of the computer system
Reference:
https://kullabs.com/class-miscellaneous/teacher-training/digital-literacy/introduction-and-function-of-operating-system

## Slide 130: Introduction to Linux operating system
Advantages of Operating System
Advantages
User Friendly
Security
Sharing Resources
Hardware Accessibility
Multitasking
Image Source:
https://www.hitechwhizz.com/2021/02/5-advantages-and-disadvantages-limitations-benefits-of-operating-system.html
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Advantage of Operating System
Allows you to hide details of hardware by creating an abstraction
Easy to use with a GUI
Offers an environment in which a user may execute programs/applications
The operating system must make sure that the computer system convenient to use
Operating System acts as an intermediary among applications and the hardware components
It provides the computer system resources with easy-to-use format
Acts as an intermediator between all hardware’s and software’s of the system
Reference:
https://www.hitechwhizz.com/2021/02/5-advantages-and-disadvantages-limitations-benefits-of-operating-system.html

## Slide 131: Introduction to Linux operating system
Disadvantages of Operating System
Disadvantages
Cost
Reliability
Complexity
Fragmentation
Virus Attacks
Image Source:
https://www.hitechwhizz.com/2021/02/5-advantages-and-disadvantages-limitations-benefits-of-operating-system.html
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Disadvantages of Operating System
If any issue occurs in OS, you may lose all the contents which have been stored in your system
Operating system’s software is quite expensive for small size organization which adds burden on them. Example Windows
It is never entirely secure as a threat can occur at any time
Reference:
https://www.hitechwhizz.com/2021/02/5-advantages-and-disadvantages-limitations-benefits-of-operating-system.html

## Slide 132: Introduction to Linux operating system
What is Linux Operating System?
Linux is a community of open-source Unix like operating systems that are based on the Linux Kernel.
Linux is a Unix-like, open source and community-developed operating system (OS) for computers, servers, mainframes, mobile devices and embedded devices.
Image Source:
https://www.guru99.com/introduction-linux.html
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Linux is a Unix-like, open source and community-developed operating system (OS) for computers, servers, mainframes, mobile devices and embedded devices.
Reference:
https://www.guru99.com/introduction-linux.html

## Slide 133: Introduction to Linux operating system
Who created Linux?
Linux, computer operating system created in the early 1990s by Finnish software engineer Linus Torvalds and the Free Software Foundation.
Image Source:
https://souclou.com/linus-torvalds-creator-of-linux-kernel-explained-why-linux-desktop-was-not-a-thing/
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Linux is an open source operating system (OS). It was originally conceived of and created as a hobby by Linus Torvalds in 1991
Reference:
https://souclou.com/linus-torvalds-creator-of-linux-kernel-explained-why-linux-desktop-was-not-a-thing/

## Slide 134: Introduction to Linux operating system
History of Linux
In 1991, the Linux history started with the starting of a particular project by the Finland student Linus Torvalds for creating a new free OS kernel.
Image Source:
https://www.elprocus.com/linux-operating-system/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
History of Linux
Linux was proposed by the Finland student Linus Torvalds in 1991.
HP-UX (Hewlett Packard) 8.0 version was published.
Hewlett Packard 9.0 version was published in 1992.
FreeBSD 1.0 version and NetBSD8 version was released in 1993.
Red Hat Linux was proposed in 1994. Caldera was detected by Ransom love and Bryan Sparks and NetBSD 1.0 version published.
HP-UX 10.0 version and FreeBSD 2.0 version was released in 1995.
K Desktop Environment was established by Matthias Ettrich in 1996.
HP-UX 11.0 version was released in 1997.
The IRIX 6.5 version, i.e., the fifth SGI UNIX generation, Free BSD 3.0 version, and Sun Solaris 7 OS was released in 1998.
The Caldera System agreement with professional services division and SCO server software division was released in 2000.
Linus Torvalds published the Linux version 2.4 source code in 2001.
Microsoft filed the Trademark collection against Lindows.com in 2001.
Lindows name was modified to Linspire in 2004.
The first publication of Ubuntu was published in 2004.
The openSUSE project started a free distribution from the community of Novell In 2005.
Oracle published its Red Hat distribution in 2006.
Dell begun laptop distribution with Ubuntu which was pre-installed on it in 2007.
Linux kernel version 3.0 was released in 2011.
Linux-based android of Google insisted 75% of the market share of the Smartphone, based on the number of phones exported in 2013.
Ubuntu insisted on 20000000+ users in 2014.
Reference:
https://www.elprocus.com/linux-operating-system/

## Slide 135: Introduction to Linux operating system
Components of Linux System
Kernel
System Library
System Utility
Image Source:
https://www.tutorialspoint.com/operating_system/os_linux.htm
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Components opf Linux:
Kernel:
Kernel is the core part of Linux. It is responsible for all major activities of this operating system. It is consisting of various modules and it interacts directly with the underlying hardware. Kernel provides the required abstraction to hide low level hardware details to system or application programs.
System Library:
System libraries are special functions or programs using which application programs or system utilities accesses Kernel's features. These libraries implement most of the functionalities of the operating system and do not require kernel module's code access rights.
System Utility:
System Utility programs are responsible for doing specialized, individual level tasks.
Reference:
https://www.tutorialspoint.com/operating_system/os_linux.htm

## Slide 136: Introduction to Linux operating system
Basic features of Linux
Portable
Open Source
Multi-user
Multiprogramming
Hierarchical File System
Shell
Security
Image Source:
https://steemit.com/features/@arshi731/features-of-linux
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Features of Linux
Portable:
Portability means software can works on different types of hardware in same way. Linux kernel and application programs supports their installation on any kind of hardware platform.
Open Source :
Linux source code is freely available and it is community-based development project. Multiple teams work in collaboration to enhance the capability of Linux operating system and it is continuously evolving.
Multi-User:
Linux is a multiuser system means multiple users can access system resources like memory/ ram/ application programs at same time.
Multiprogramming:
Linux is a multiprogramming system means multiple applications can run at same time.
Hierarchical File System:
Linux provides a standard file structure in which system files/ user files are arranged.
Shell:
Linux provides a special interpreter program which can be used to execute commands of the operating system. It can be used to do various types of operations, call application programs. etc.
Security:
Linux provides user security using authentication features like password protection/ controlled access to specific files/ encryption of data.
Reference:
https://steemit.com/features/@arshi731/features-of-linux

## Slide 137: Introduction to Linux operating system
Architectures of Linux Operating System
The Kernel
System Library
Hardware layer
System
Shell utility.
Image Source:
https://www.javatpoint.com/architecture-of-linux
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Architecture of Linux
Hardware layer:
Hardware consists of all peripheral devices (RAM/ HDD/ CPU etc).
Kernel :
It is the core component of Operating System, interacts directly with hardware, provides low level services to upper layer components.
Shell :
An interface to kernel, hiding complexity of kernel's functions from users. The shell takes commands from the user and executes kernel's functions.
Utilities:
Utility programs that provide the user most of the functionalities of an operating systems
Reference:
https://www.javatpoint.com/architecture-of-linux

## Slide 138: Introduction to Linux operating system
The Linux Kernel
Linux kernel is a free, open-source, monolithic, modular, Unix-like operating system kernel.
It is the main component of the Linux operating system (OS) and is the core interface between the computer’s hardware and its processes.
Image Source:
https://www.javatpoint.com/architecture-of-linux
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Linux Kernel
The Process Scheduler:
This kernel subsystem is responsible for fairly distributing the CPU time among all the processes running on the system simultaneously.
The Memory Management Unit:
This kernel sub-unit is responsible for proper distribution of the memory resources among the various processes running on the system. The MMU does more than just simply provide separate virtual address spaces for each of the processes.
The Virtual File System:
This subsystem is responsible for providing a unified interface to access stored data across different filesystems and physical storage media.
Reference:
https://www.javatpoint.com/architecture-of-linux

## Slide 139: Introduction to Linux operating system
User-interface of Linux
A user interface (UI) refers to the part of an operating system, program, or device that allows a user to enter and receive information.
Image Source:
https://ubuntu.com/blog/whats-new-in-ubuntu-desktop-20-04-lts
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
A user interface (UI) refers to the part of an operating system, program, or device that allows a user to enter and receive information. A text-based user interface (see the image to the left) displays text, and its commands are usually typed on a command line using a keyboard.
Reference:
https://ubuntu.com/blog/whats-new-in-ubuntu-desktop-20-04-lts

## Slide 140: Introduction to Linux operating system
Distribution of Linux
Ubuntu
Linux Mint
Debian
Red Hat
Fedora
Image Source:
https://oracle-patches.com/en/os/choosing-the-right-linux-distribution-step-by-step-instruction
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Linux Distributions List
Ubuntu
It came into existence in 2004 by Canonical and quickly became popular. Canonical wants Ubuntu to be used as easy graphical Linux desktop without the use of command line. It is the most well-known Linux distribution. Ubuntu is a next version of Debian and easy to use for newbies. It comes with a lot of pre-installed apps and easy to use repositories libraries.
Linux Mint
Mint is based on Ubuntu and uses its repository software so some packages are common in both.
Earlier it was an alternative of Ubuntu because media codecs and proprietary software are included in mint but was absent in Ubuntu. But now it has its own popularity and it uses cinnamon and mate desktop instead of Ubuntu's unity desktop environment.
Debian
Debian has its existence since 1993 and releases its versions much slowly then Ubuntu and mint.
This makes it one of the most stable Linux distributors.
Ubuntu is based on Debian and was founded to improve the core bits of Debian more quickly and make it more user friendly. Every release name of Debian is based on the name of the movie Toy Story.
Red Hat Enterprise / CentOS
Red hat is a commercial Linux distributor. There products are red hat enterprise Linux (RHEL) and Fedora which are freely available. RHEL is well tested before release and supported till seven years after the release, whereas, fedora provides faster update and without any support.
Red hat uses trademark law to prevent their software from being redistributed. CentOS is a community project that uses red hat enterprise Linux code but removes all its trademark and make it freely available. In other words, it is a free version of RHEL and provide a stable platform for a long time.
Fedora
It is a project that mainly focuses on free software and provides latest version of software. It doesn't make its own desktop environment but used 'upstream' software. By default, it has GNOME3 desktop environment. It is less stable but provides the latest stuff.
Reference:
https://oracle-patches.com/en/os/choosing-the-right-linux-distribution-step-by-step-instruction

## Slide 141: Introduction to Linux operating system
Best Command-Line Editors in Linux
Vim
Emacs
Nano
Micro
Image Source:
https://www.javatpoint.com/linux-nano-editor
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Command Line Editors
Vim
Vim is the most common and famous text editor of the Linux world and comes installed by default (either vim or the more basic version vi) in most distributions.
Emacs
Just like vim, emacs is a classic Unix/Linux text editor that has been around since the 1970s. The rivalry between vim and emacs users actually triggered one of the first flame wars between computer users, achieving cult status in the sysadmin and hacker culture.
Nano
Nano is a development of the pico editor and was developed from the start to be user-friendly and intuitive for command-line beginners
Micro
Micro is another user-friendly editor and actually aims to emulate the simplicity of nano, while adding more powerful features on top.
Reference:
https://www.javatpoint.com/linux-nano-editor

## Slide 142: Introduction to Linux operating system
Types of Users in Linux
Root user
Regular user
Service Account
Image Source:
https://linoxide.com/list-users-linux-command-line/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Type of Users in Linux
The root user account
This is the main user account in Linux system. It is automatically created during the installation. It has the highest privilege in system. It can do any administrative work and can access any service. This account is intended for system administration and should be used only for this purpose. It should not be used for routine activities. It can’t be deleted. But if require, it can be disabled.
The regular user account
This is the normal user account. During the installation, one regular user account is created automatically. After the installation, we can create as many regular user accounts as we need. This account has moderate privilege. This account is intended for routine works. It can perform only the tasks for which it is allowed and can access only those files and services for which it is authorized. As per requirement, it can be disabled or deleted.
The service account
Service accounts are created by installation packages when they are installed. These accounts are used by services to run processes and execute functions. These accounts are neither intended nor should be used for routine work.
Reference:
https://linoxide.com/list-users-linux-command-line/

## Slide 143: Introduction to Linux operating system
Comparison of Linux with another Operating System
Linux is Open Source and is free to use. Windows is not open source and is not free to use.
Linux file system is case sensitive. Windows file system is case insensitive
Image Source:
https://pediaa.com/difference-between-linux-and-ubuntu/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Linux is an open source operating system so user can change source code as per requirement whereas Windows OS is a commercial operating system so user doesn’t have access to source code.
Linux is very well secure as it is easy to detect bugs and fix whereas Windows has a huge user base, so it becomes a target of hackers to attack windows system.
Comparing Windows file system vs Linux file system, Linux runs faster even with older hardware whereas Windows are slower compared to Linux.
Linux peripherals like hard drives, CD-ROMs, printers are considered files whereas Windows, hard drives, CD-ROMs, printers are considered as devices
Linux files are ordered in a tree structure starting with the root directory whereas in Windows, files are stored in folders on different data drives like C: D: E:
In Linux you can have 2 files with the same name in the same directory while in Windows, you cannot have 2 files with the same name in the same folder.
In Linux you would find the system and program files in different directories whereas in Windows, system and program files are usually saved in C: drive
Reference:
https://pediaa.com/difference-between-linux-and-ubuntu/

## Slide 144: Introduction to Linux operating system
Advantages and disadvantages of Linux operating system
Advantages
Open source
No anti-virus software needed
Text editors
Powerful command prompt
No reboot needed
Image Source:
https://www.guru99.com/introduction-linux.html
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Advantages of Linux operating system
Open source
Linux is an open-source OS that means anyone can see the source code and change it according to his needs. You can freely install Linux on many computers without getting paid license. If we compare this with windows or mac then they are paid operating systems. You have to get license of windows and mac to use on your machine.
No anti-virus software needed
In Linux, you do not need anti-virus software to be installed on your PC. Linux has fewer chances to be affected with virus. The reason for strong virus protection is that Linux has large number of open-source developers which keeps an eye on virus-related stuff. If any source code needs to be updated then it is done in no time.
Text editors
Linux has a vast range of text editors available. If you are a programmer then you can pick any of free software packages like visual studio code, Vim, Atom etc. Most of text editors are freely available and you can use it without any issue.
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 145: Introduction to Linux operating system
Advantages and disadvantages of Linux operating system
Low system specifications
Good at multitasking
Less disk space needed
File formats
Image Source:
https://www.techradar.com/how-to/how-to-speed-up-ubuntu-2004
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Powerful command prompt
Command prompt in Linux is very advanced and if you are developer then you can perform most of your work using the command-line interface. You can install different repositories and packages through the command-line interface.
No reboot needed
If you are windows user then you have seen system reboot while you install/uninstall any software or rebooting when the system becomes slow. But in case of Linux, you do not need to reboot your system in such cases.
Low system specifications
If you have an old computer that has low specification then you can still run Linux. Linux has different distributions that are available for all types of computers e.g. large scale computers, servers, Pc etc.
Good at multitasking
If you want to do some batch works like printing a large file or downloading large file then you can concurrently perform other tasks like typing or coding any program. Linux is good in doing such multitasking and your system will not slow down.
Less disk space needed
If you have limited disk space then you can still run Linux. You do not need extra disk space for running Linux for a longer time.
File formats
Linux supports a large number of file formats. So you have to not worry if any file format does not run on Linux. You can install different software packages for specific file format and it will work fine.
Reference:
https://www.techradar.com/how-to/how-to-speed-up-ubuntu-2004

## Slide 146: Introduction to Linux operating system
Advantages and disadvantages of Linux operating system
Disadvantages
Hardware drivers
Learning curve
Software alternative
No Games
Image Source:
https://www.techrepublic.com/article/evaluating-linux-reality-vs-hype/
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Disadvantages of Linux operating system
Hardware drivers:
One of the issues that most Linux users face is that some hardware drivers are not available for Linux. Hardware companies prefer to make drivers for windows or mac because they have more users as compared to Linux.
Learning curve:
Getting started with windows is easy for beginners but learning Linux is difficult. You have to learn about the command-line interface and searching for new software is also little bit difficult. If you face any problem in the operating system then finding solution is problematic. There are fewer experts for Linux as compared to windows and mac.
Software alternative:
Take an example of Photoshop which is a popular graphic editing tool. Photoshop is available for windows but is not present in Linux. There are other photo editing tools but Photoshop is a more powerful tool than others. MS office is another example which is not available for Linux users.
Games:
Most of the games are made for windows but not Linux. As windows platform is widely used so game developers have more interest in windows.
Reference:
https://www.techrepublic.com/article/evaluating-linux-reality-vs-hype/

## Slide 147: Familiarization with GUI environment
What is Graphical User Interface (GUI)?
A graphical user interface (GUI) is an interface through which a user interacts with electronic devices such as computers and smartphones through the use of icons, menus and other visual indicators or representations (graphics).
Image Source:
https://etipsguruji.com/gui/
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 2
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
GUI is an interface that allows users to interact with different electronic devices using icons and other visual indicators. The graphical user interfaces were created because command line interfaces were quite complicated and it was difficult to learn all the commands in it.
Reference:
https://etipsguruji.com/gui/

## Slide 148: Familiarization with GUI environment
Top 10 Linux Desktop Environments
GNOME
KDE Plasma
Unity
MATE
Cinnamon
Image Source:
https://technastic.com/5-best-linux-desktop-environments/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Linux Desktop Enviroments
GNOME
GNOME is probably the most popular desktop environment among Linux users, it is free and open source, simple, yet powerful and easy to use. It is designed from ground up to offer Linux desktop users a wonderful and exciting computing experience.
KDE Plasma
KDE is a well-known, powerful and highly customizable desktop environment, designed to offer Linux desktop users absolute control over their desktop.
Unity
Unity is a graphical desktop shell for GNOME desktop environment. The Unity project was started by Mark Shuttleworth and Canonical, the makers of the well-known Ubuntu Linux distribution.
MATE
MATE is an intuitive and appealing desktop environment, that is an extension of GNOME 2. It works on Linux and many other Unix-like systems. It comes with a handful of default applications such as Caja file manager, Pluma text editor, MATE terminal and more.
Cinnamon
Cinnamon is in fact a collection of several minor projects such as Cinnamon, a fork of the GNOME shell, Cinnamon screensaver, Cinnamon desktop, Cinnamon Menus, Cinnamon Settings Daemon coupled with many more.
Reference:
https://technastic.com/5-best-linux-desktop-environments/

## Slide 149: Familiarization with GUI environment
Top 10 Linux Desktop Environments
Budgie
LXQT
XFCE
Deepin
LXDE
Image Source:
https://commons.wikimedia.org/wiki/File:Desktop_Ubuntu_20.04.png
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Budgie
Budgie is a desktop environment that currently uses GNOME technologies such as GTK (> 3. x) and is developed by the Solus project as well as by contributors from numerous communities such as Arch Linux, Manjaro, openSUSE Tumbleweed and Ubuntu Budgie. Budgie's design emphasizes simplicity, minimalism, and elegance
LXQT
LXQt is also free, open source, lightweight, simple and fast desktop environment for Linux and BSD distributions. It is the latest version of LXDE, specifically designed, and a recommended desktop environment for cloud servers and old machines due to its remarkably low system resources usage such as low CPU and RAM consumption.
XFCE
It is modern, open source, lightweight and easy-to-use, desktop environment for Linux and several other Unix-like systems such as such as Mac OS X, *BSD, Solaris and many others, then you should consider checking out Xfce. It is fast, and importantly user friendly as well, with low system resources utilization.
Deepin
Deepin Desktop Environment(DDE) is also a simple, elegant and productive desktop environment for Linux, developed by the makers of Deepin OS.
LXDE
LXDE is a lightweight desktop environment for Unix and Unix-like operating system, such as BSD and Linux. It is designed to consume fewer system resources than other desktop environments such as GNOME.
Pantheon
Pantheon is a simple and well-designed desktop environment for Elementary OS, a Windows and MacOS X like Linux distribution. It offers users a clean and organized desktop experience. Due to its simplicity, Pantheon comes with not many visually observable features as compared to other popular desktop environments.
Reference:
https://commons.wikimedia.org/wiki/File:Desktop_Ubuntu_20.04.png

## Slide 150: Familiarization with GUI environment
CLI vs GUI
CLI, or Command Line Interface, is a text-based interface used to interact with software and operating system by typing commands into the interface and receive a response in the same way
GUI, or Graphical User Interface, is a visual-based interface which features the use of graphic images, including windows, icons, and menus.
Image Source:
https://pediaa.com/difference-between-gui-and-cli/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
What is CLI?
CLI, or Command Line Interface, is a text-based interface used to interact with software and operating system by typing commands into the interface and receive a response in the same way.
CLIs are provided by most operating systems by default and the two most popular ones are DOS (for Windows) and the bash shell (for Linux and OS X).
What is GUI?
GUI, or Graphical User Interface, is a visual-based interface which features the use of graphic images, including windows, icons, and menus. A mouse is the most common way to navigate through a GUI, although the keyboard is used sometimes.
A CLI is an interface that allows the user to perform tasks by issuing commands in successive lines of text or command lines. A graphical user interface enables users to interact with the operating system or application. It needs less memory than the GUI.
Reference:
https://pediaa.com/difference-between-gui-and-cli

## Slide 151: Syntax of shell commands
Linux directory structure
/ - Root
/bin - Binaries and other executable programs.
/etc - System configuration files.
/home - Home directories.
/opt - Optional or third party software.
Image Source:
https://www.geeksforgeeks.org/linux-directory-structure/
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 3
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Linux Directories
The /bin directory stores many utilities of Linux
The /dev directory stores all the device-related files for the system
The /etc directory stores the os related data which users and the os need to refer to, such as the passwd file
The /lib directory contains libraries of data for the compilers installed in the Linux operating system, for examples, the C language routines
The /home directory generally contains all the HOME directories of users
Reference:
https://www.geeksforgeeks.org/linux-directory-structure/

## Slide 152: Syntax of shell commands
Linux directory structure
/tmp - Temporary space, typically cleared on reboot.
/usr - User related programs.
/var - Variable data, most notably log files.
Image Source:
https://www.geeksforgeeks.org/linux-directory-structure/
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 3
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
The /usr directory stores the os files that are not involved in the boot process,
The /var directory has information specific to different utilities of Linux.
Reference:
https://www.geeksforgeeks.org/linux-directory-structure/

## Slide 153: Syntax of shell commands
Types of Files in Linux
Regular files (-)
Directory files (d)
Special files
Image Source:
https://www.2daygeek.com/find-identify-file-types-in-linux/
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Types of Files in Linux
Regular files (-): It contain programs, executable files and text files.
Directory files (d): It is shown in blue color. It contains list of files.
Special files
  Block file (b)
  Character device file (c)
  Named pipe file (p)
  Symbolic link file (l)
  Socket file (s)
Reference:
https://www.2daygeek.com/find-identify-file-types-in-linux

## Slide 154: Syntax of shell commands
What are Shell Commands?
In Linux, commands are ways or instructions through which you can instruct your system to do some action.
Commands are executed in the command line.
Image Source:
https://www.geeksforgeeks.org/basic-linux-commands-day-day-life/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
The shell is the Linux command line interpreter. It provides an interface between the user and the kernel and executes programs called commands. For example, if a user enters ls then the shell executes the ls command. The shell can also execute other programs such as applications, scripts, and user programs (e.g., written in c or the shell programming language).
Reference:
https://www.geeksforgeeks.org/basic-linux-commands-day-day-life/

## Slide 155: Syntax of shell commands
What is Shell?
The shell is the command interpreter on the Linux systems.
It the program that interacts with the users in the terminal emulation window.
Image Source:
https://www.educba.com/bash-shell-in-linux/
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
A shell is special user program which provide an interface to user to use operating system services. Shell accepts human readable commands from user and convert them into something which kernel can understand. It is a command language interpreter that execute commands read from input devices such as keyboards or from files
Reference:
https://www.educba.com/bash-shell-in-linux/

## Slide 156: Syntax of shell commands
What are the types of shell commands?
The C Shell
The Bourne Shell
The Korn Shell
GNU Bourne-Again Shell .
Image Source:
https://www.tutorialandexample.com/linux-bash/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Types of Shell Commands
Bourne shell:
If you are using a Bourne-type shell, the $ character is the default prompt.
C shell:
If you are using a C-type shell, the % character is the default prompt.
Reference:
https://www.tutorialandexample.com/linux-bash/

## Slide 157: Syntax of shell commands
What is Command Line Interface (CLI)?
The Command Line Interface (CLI), is a non-graphical, text-based interface to the computer system, where the user types in a command and the computer then successfully executes it.
The Terminal is the platform or the IDE that provides the command line interface (CLI) environment to the user.
Image Source:
https://docs.gigaspaces.com/latest/admin/tools-cli.html
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
The Command Line Interface (CLI), is a non-graphical, text-based interface to the computer system, where the user types in a command and the computer then successfully executes it. The Terminal is the platform or the IDE that provides the command line interface (CLI) environment to the user.
CLI is still used by software developers and system administrators to configure computers, install software, and access features that are not available in the graphical interface.
Reference:
https://docs.gigaspaces.com/latest/admin/tools-cli.html

## Slide 158: Syntax of shell commands
Basic Shell Commands in Linux
It is a command language interpreter that executes commands read from input devices such as keyboards or from files.
The shell gets started when the user logs in or starts the terminal.
Image Source:
https://www.journaldev.com/34067/linux-commands
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Basic Shell commands
ls – List directory contents.
cd /var/log – Change the current directory.
grep – Find text in a file.
su / sudo command – There are some commands that need elevated rights to run on a Linux system.
pwd – Print Working Directory.
mv – Move a file.
cp – Copy a file
Reference:
https://www.journaldev.com/34067/linux-commands

## Slide 159: Syntax of shell commands
Displaying the file contents on the terminal
cat
more
less
head
Tail
Image Source:
https://study.com/academy/lesson/linux-commands-for-managing-files-directories.html
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Displaying the file contents on the terminal
cat: It is generally used to concatenate the files. It gives the output on the standard output.
more: It is a filter for paging through text one screenful at a time.
less: It is used to viewing the files instead of opening the file. Similar to more command but it allows backward as well as forward movement.
head : Used to print the first N lines of a file. It accepts N as input and the default value of N is 10.
tail : Used to print the last N-1 lines of a file. It accepts N as input and the default value of N is 10.
Reference:
https://study.com/academy/lesson/linux-commands-for-managing-files-directories.html

## Slide 160: Syntax of shell commands
File and Directory Manipulation Commands
mkdir
cp
mv
rm
touch
Image Source:
https://study.com/academy/lesson/linux-commands-for-managing-files-directories.html
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
File and Directory Manipulation Commands
mkdir : Used to create a directory if not already exist. It accepts the directory name as an input parameter.
cp : This command will copy the files and directories from the source path to the destination path. It can copy a file/directory with the new name to the destination path. It accepts the source file/directory and destination file/directory.
mv : Used to move the files or directories. This command’s working is almost similar to cp command but it deletes a copy of the file or directory from the source path.
rm : Used to remove files or directories.
touch : Used to create or update a file.
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 161: Syntax of shell commands
Extract, sort, and filter data Commands
grep
grep with Regular Expressions
sort
wc
cut
Image Source:
https://www.computernetworkingnotes.com/linux-tutorials/how-to-use-the-sort-command-in-linux.html
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Extract, sort, and filter data Commands
grep : This command is used to search for the specified text in a file.
rep with Regular Expressions: Used to search for text using specific regular expressions in file.
sort : This command is used to sort the contents of files.
wc : Used to count the number of characters, words in a file.
cut : Used to cut a specified part of a file.
Reference:
https://www.computernetworkingnotes.com/linux-tutorials/how-to-use-the-sort-command-in-linux.html

## Slide 162: Syntax of shell commands
Basic Terminal Navigation Commands
pwd
ls -l
clear
cd path/name
cp -r source destination
up/down arrows
Image Source:
https://study.com/academy/lesson/linux-commands-for-managing-files-directories.html
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Basic Terminal Navigation Commands
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
ls : To get the list of all the files or folders.
ls -l: Optional flags are added to ls to modify default behavior, listing contents in extended form -l is used for “long” output
ls -a: Lists of all files including the hidden files, add -a flag
cd: Used to change the directory.
du: Show disk usage.
pwd: Show the present working directory.
man: Used to show the manual of any command present in Linux.
rmdir: It is used to delete a directory if it is empty.
ln file1 file2: Creates a physical link.
ln -s file1 file2: Creates a symbolic link.
locate: It is used to locate a file in Linux System
echo: This command helps us move some data, usually text into a file.
df: It is used to see the available disk space in each of the partitions in your system.
tar: Used to work with tarballs (or files compressed in a tarball archive)
Reference:
https://study.com/academy/lesson/linux-commands-for-managing-files-directories.html

## Slide 163: Syntax of shell commands
File Permissions Commands
chown
chgrp
chmod
Image Source:
https://study.com/academy/lesson/modifying-file-permissions-access-control-in-linux.html
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
.
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
File Permissions Commands
chown : Used to change the owner of the file.
chgrp : Used to change the group owner of the file.
chmod : Used to modify the access/permission of a user
Reference:
https://study.com/academy/lesson/modifying-file-permissions-access-control-in-linux.html

## Slide 164: Syntax of shell commands
What is the use of shell command?
It is a command language interpreter that executes commands read from input devices such as keyboards or from files.
The shell gets started when the user logs in or starts the terminal.
Image Source:
https://www.poweradmin.com/blog/essential-shell-commands-for-linux/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
It is a command language interpreter that executes commands read from input devices such as keyboards or from files
Reference:
https://www.poweradmin.com/blog/essential-shell-commands-for-linux

## Slide 165: Shell Scripting
Shell scripting
Shell Scripting is an open-source computer program designed to be run by the Unix/Linux shell.
Shell Scripting is a program to write a series of commands for the shell to execute.
Image Source:
https://mindmajix.com/shell-scripting-tutorial
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 4
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
A shell script is a text file that contains a sequence of commands for a UNIX-based operating system. It is called a shell script because it combines a sequence of commands, that would otherwise have to be typed into the keyboard one at a time, into a single script.
Reference:
Image Source:
https://mindmajix.com/shell-scripting-tutorial

## Slide 166: Shell Scripting
Types of Shell
The Bourne Shell
The C shell
Image Source:
https://www.slideshare.net/sschaturvedi2015/shell-and-its-types-in-linux-248788008
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
There are two main shells in Linux:
The Bourne Shell:
The prompt for this shell is $ and its derivatives are listed below:
  POSIX shell also is known as sh
  Korn Shell also knew as sh
  Bourne Again SHell also knew as bash (most popular)
The C shell:
The prompt for this shell is %, and its subcategories are:
  C shell also is known as csh
  Tops C shell also is known as tcsh
Reference:
https://www.slideshare.net/sschaturvedi2015/shell-and-its-types-in-linux-248788008

## Slide 167: Shell Scripting
Editors
VI Editor
Nano Editor
Image Source:
https://www.maketecheasier.com/linux-nano-text-editor-beginner-guide/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Linux text editors can be used for editing text files, writing codes, updating user instruction files, and more. ... There are two types of text editors in Linux, which are given below: Command-line text editors such as Vi, nano, pico, and more. GUI text editors such as gedit (for Gnome), Kwrite, and more
Reference:
https://www.maketecheasier.com/linux-nano-text-editor-beginner-guide/

## Slide 168: Shell Scripting
VI Editor
It is the default text editor that comes with most Linux systems.
It is a Terminal-based text editor that users need to learn, essentially when more user-friendly text editors are not available on the system.
sudo apt install vim
Image Source:
https://www.smashingmagazine.com/2010/05/vi-editor-linux-terminal-cheat-sheet-pdf/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
The VI editor is the most popular and classic text editor in the Linux family. Below, are some reasons which make it a widely used editor –
  It is available in almost all Linux Distributions
  It works the same across different platforms and Distributions
  It is user-friendly. Hence, millions of Linux users love it and use it for their editing needs
Reference:
https://www.smashingmagazine.com/2010/05/vi-editor-linux-terminal-cheat-sheet-pdf/

## Slide 169: Shell Scripting
Nano Editor
GNU nano is a simple terminal-based text editor
Nano can be used in a terminal window or at the system console..
sudo apt install nano
Image Source:
https://www.maketecheasier.com/linux-nano-text-editor-beginner-guide/
Notes: Continuing from the last slide:
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Nano is the most fundamental, command-line-based text editor for Linux. It has all common text editor features, including highlighting syntaxes, multiple buffers, scanning and replacement with regular expression support, type corrections, and UTF-8 encoding.
Reference:
https://www.maketecheasier.com/linux-nano-text-editor-beginner-guide/

## Slide 170: Shell Scripting
Why do we need shell scripts?
Using a shell script is most useful for repetitive tasks that may be time consuming to execute by typing one line at a time.
Image Source:
https://www.educba.com/uses-of-shell-scripting/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
There are many reasons to write shell scripts
  To avoid repetitive work and automation
  System admins use shell scripting for routine backups
  System monitoring
  Adding new functionality to the shell etc.
Reference:
https://www.educba.com/uses-of-shell-scripting/

## Slide 171: Shell Scripting
What is Bash?
BASH is an acronym for Bourne Again Shell
Bash or Shell is a command line tool that is used in open science to efficiently manipulate files and directories.
Image Source:
https://devopslearning.medium.com/100-days-of-devops-day-51-introduction-to-bash-scripting-9501ce7a32a4
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Bash or Shell is a command line tool that is used in open science to efficiently manipulate files and directories.
BASH is an acronym for Bourne Again Shell, a punning name, which is a tribute to Bourne Shell (i.e., invented by Steven Bourne).
Reference:
https://devopslearning.medium.com/100-days-of-devops-day-51-introduction-to-bash-scripting-9501ce7a32a4

## Slide 172: Shell Scripting
Features of Bash
Shell commands
I/O Redirection
Interactive
Manuals/help
Scripting
Functions
Extras
Image Source:
https://linuxaria.com/howto/7-hidden-features-of-bash
Notes: This slide talks about the case if we have to divide a subtopic further.
Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Features of Bash
Shell commands:
Shell has the power to command the OS with higher priority. Bash shell provides almost all kinds of commands to do several tasks from the terminal. We have commands for creating files “touch,” for text editor “vi,” for creating folder “mkdir,” for removing file and folder “rm,” etc.
I/O Redirection:
Input/Output redirection has a special place in the commands. With the help of these symbols, you can redirect the input and output of any command to another command or a file. Angular brackets are used for redirections.
Interactive:
The bash shell is interactive in behavior. You could give input and get output on the same screen.
Manuals/help:
bash shell has excellent documentation and manuals available for each command. These manuals provide each detail about using the command and give examples of using them with various options.
Scripting:
On the shell, only one line of commands can be run at a time. But shell also provides the functionality of running multiple commands at a time. This functionality is achieved by shell scripting.
Functions:
These functions provide the ability to run multiple commands for the later execution of them by using the single name of the group. After creating them can be used the same as a command.
Extras:
bash shell has some extra features like basic debugging, command-line completion, brace expansion, signal handling, and many more.
Reference:
https://linuxaria.com/howto/7-hidden-features-of-bash

## Slide 173: Shell Scripting
Bash Scripting
A Bash Shell Script is a plain text file containing a set of various commands that we usually type in the command line.
It is used to automate repetitive tasks on Linux filesystem.
Image Source:
https://dzone.com/articles/functions-in-shell-script/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
A Bash Shell Script is a plain text file containing a set of various commands that we usually type in the command line.
It is used to automate repetitive tasks on Linux filesystem.
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://dzone.com/articles/functions-in-shell-script/

## Slide 174: Shell Scripting
Shell Variables
A variable is a temporary storage area in memory that is either set by the user, shell, system, or any program that loads another program.
There are two categories of variables:
environment variables
shell variables
Image Source:
https://www.javatpoint.com/bash-variables
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Shell Variables
What are Variables?
A variable is a temporary storage area in memory that is either set by the user, shell, system, or any program that loads another program. There are two categories of variables:
There are two categories of variables:
  environment variables
  shell variables
The environment variables are valid for the duration of the session.
The shell variables apply only to the current instance of the shell and are used to set short-term working conditions.
Reference:
https://www.javatpoint.com/bash-variables

## Slide 175: Shell Scripting
Bash Operators
Integer Comparisons
String Comparisons
Logical Operators
File Test Operators
Image Source:
https://www.geeksforgeeks.org/linux-directory-structure/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Bash Operators:
Arithmetic Operators(+,-,*,/,%,=,==,!=)
Relational Operators(-eq,-ne,-gt,-lt,-ge,-le)
Boolean Operators(!,-o,-a)
String Operators(=,!=,-z,-n,str)
File Test Operators
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 176: Shell Scripting
Read User Input
‘read’ command is used to take input from user in bash
It takes input from the user and assigns it to the variable
read <variable_name>
Image Source:
https://www.javatpoint.com/bash-read-user-input
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Read User Input
To read the Bash user input, we use the built-in Bash command called read. It takes input from the user and assigns it to the variable. It reads only a single line from the Bash shell.
Reference:
https://www.javatpoint.com/bash-read-user-input

## Slide 177: Shell Scripting
Bash Conditional statements
if statement
if-else statement
Else If ladder
Nested if
switch statement
Image Source:
https://www.javatpoint.com/if-then-else-shell-scripting
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Conditional Statements: There are total 5 conditional statements which can be used in bash programming
if statement
if-else statement
if..elif..else..fi statement (Else If ladder)
if..then..else..if..then..fi..fi..(Nested if)
switch statement
if statement
This block will process if specified condition is true.
if-else statement
If specified condition is not true in if part then else part will be execute.
if..elif..else..fi statement (Else If ladder)
To use multiple conditions in one if-else block, then elif keyword is used in shell. If expression1 is true then it executes statement 1 and 2, and this process continues. If none of the condition is true then it processes else part.
if..then..else..if..then..fi..fi..(Nested if)
Nested if-else block can be used when, one condition is satisfies then it again checks another condition. In the syntax, if expression1 is false then it processes else part, and again expression2 will be check.
switch statement
case statement works as a switch statement if specified value match with the pattern then it will execute a block of that particular pattern
When a match is found all of the associated statements until the double semicolon (;;) is executed.
A case will be terminated when the last command is executed.
If there is no match, the exit status of the case is zero.
Reference:
https://www.javatpoint.com/if-then-else-shell-scripting

## Slide 178: Shell Scripting
Bash Looping
while statement
for statement
until statement
Image Source:
https://linuxhint.com/nested-loop-bash-script-examples/
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Looping Statements in Shell Scripting: There are total 3 looping statements which can be used in bash programming
  while statement
  for statement
  until statement
To alter the flow of loop statements, two commands are used they are,
  break
  continue
while statement
Here command is evaluated and based on the result loop will executed, if command raise to false then loop will be terminated
for statement
The for loop operate on lists of items. It repeats a set of commands for every item in a list.
Here var is the name of a variable and word1 to wordN are sequences of characters separated by spaces (words). Each time the for loop executes, the value of the variable var is set to the next word in the list of words, word1 to wordN.
until statement
The until loop is executed as many as times the condition/command evaluates to false. The loop terminates when the condition/command becomes true.
Reference:
https://linuxhint.com/nested-loop-bash-script-examples/

## Slide 179: Shell Scripting
Bash Functions
Functions in bash scripting are a great option to reuse code.
A Bash function can be defined as a set of commands which can be called several times within bash script
Image Source:
https://ro.linuxteaching.com/article/bash_call_function
Notes: Left (White Color space):
Title - Parent Topic
Body Text - Subtopic divisions (Subtopics of subtopics)
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Bash Functions:
A Bash function is essentially a set of commands that can be called numerous times. The purpose of a function is to help you make your bash scripts more readable and to avoid writing the same code repeatedly. Compared to most programming languages, Bash functions are somewhat limited
Reference:
https://ro.linuxteaching.com/article/bash_call_function

## Slide 180: Familiarization of open office tools
(5 hours)
Notes: Title - The learning outcome
Subtitle - Duration

## Slide 181: In this section, we will discuss:
OpenOffice tools for creating documents
OpenOffice tools for creating spreadsheet
OpenOffice tools for creating presentation
Notes: Mention the parent topics one by one. This particular learning outcome has 4 parent topics.

## Slide 182: OpenOffice tools for creating documents
What is open office
OpenOffice is the leading open-source office software suite for word processing, spreadsheets, presentations, graphics, databases and more.
Developed by Sun Microsystems Ltd.
Image Source: https://media.smallbiztrends.com/2016/12/open-office.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 183: OpenOffice tools for creating documents
Advantages of open office
No licensing fees
Cross-platform
Extensive language support
Consistent user interface
Integration
Granularity
File compatibility
Image: https://www.howtogeek.com/wp-content/uploads/2014/04/apache-openoffice.png?trim=1,1&bg-color=000&pad=1,1
Notes: This slide talks about the case if we have to divide a subtopic further.
Title Box - Parent Topic
Subtitle box - Sub Topic
Body Text - Subtopic divisions (Subtopics of subtopics)

## Slide 184: OpenOffice tools for creating documents
Features
Styles and formatting
Interoperability
Programmability
Image: https://www.howtogeek.com/wp-content/uploads/2014/04/apache-openoffice.png?trim=1,1&bg-color=000&pad=1,1
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 185: OpenOffice tools for creating documents
What are the minimum requirements
Microsoft Windows 98, ME, 2000 (Service Pack 2 or higher), XP or 2003
GNU/Linux Kernel version 2.2.13 and glibc 2.2.0 or newer
Mac OS X 10.3.x (10.3.5 recommended), Mac OS X 10.4.x, plus X11
Solaris version 8 or higher
Image Source: https://media.smallbiztrends.com/2016/12/open-office.png

## Slide 186: OpenOffice tools for creating documents
Parts of the main window
Title Bar
Control Buttons
Menu Bar
Tool Bar
Status Bar
Image: https://img.brainkart.com/imagebk34/RuTbyaO.jpg

## Slide 187: OpenOffice tools for creating documents
Working with documents
Starting a new document
Entering the Text
Saving the Document
Saving with password
Closing a Document
Image: https://wiki.openoffice.org/w/images/thumb/9/9d/Saveas.png/500px-Saveas.png

## Slide 188: OpenOffice tools for creating documents
Working with documents
Closing Unsaved Document
Opening an existing document
Editing a document
Deleting and renaming files
Deleting a file
Moving within a document
Image: https://wiki.openoffice.org/w/images/thumb/9/9d/Saveas.png/500px-Saveas.png

## Slide 189: Working with documents
Starting a new document
You can also start a new document in one of the following ways:
Use File > New and choose the type of document
Press Control+N on the keyboard.
Use File > Wizards for some types of documents.
Image: https://www.wikihow.com/images/thumb/3/3f/Use-OpenOffice.org-Writer-Step-2Bullet2.jpg/aid571139-v4-728px-Use-OpenOffice.org-Writer-Step-2Bullet2.jpg.webp

## Slide 190: Working with documents
Entering the Text
Once a new document is open, the text can be typed in blank area of the screen.
As the text is typed they appear on the screen and the flashing vertical bar.
Image: https://www.inkubit.com/wp-content/uploads/2020/08/word-und-openoffice-im-vergleich-bild-2-1024x639.png

## Slide 191: Working with documents
Saving the Document
Click File -> Save ‚ (or) File -> Save As (or) Ctrl + S
Select location to store your document
Type your document name in the File Name box
click “Save” button
Image: https://img.brainkart.com/imagebk34/ecA1qn9.jpg

## Slide 192: Working with documents
Saving with password
click on “Save with Password” check box and then click “Save” button
Enter a password and retype the same password
Click “Confirm Password”
click “OK” button
Image: https://img.brainkart.com/imagebk34/Ra2dcPS.jpg

## Slide 193: Working with documents
Closing a Document
After your document is saved
File -> Close command (or) Press Ctrl + W.
https://img.brainkart.com/imagebk34/CjylYx2.jpg

## Slide 194: Working with documents
Closing Unsaved Document
When you close an unsaved file using the close control button, Writer shows a warning message
https://img.brainkart.com/imagebk34/CjylYx2.jpg

## Slide 195: Working with documents
Opening an existing document
To open an existing document, Click on the File -> Open or Ctrl + O, the Open dialog box appears, enter the name of the file in the File Name text box and click on OPEN button
https://wiki.openoffice.org/w/images/thumb/e/ed/WindowsOpen.png/500px-WindowsOpen.png

## Slide 196: Working with documents
Deleting and renaming and moving files
You can rename or delete files within the OpenOffice.org dialogs. It is not possible to copy and paste files within the dialogs.
https://opentextbc.ca/computerstudies/wp-content/uploads/sites/322/2020/11/Move-to-Screeshot.png

## Slide 197: Page Preview, Setting the printer and Printing a document
Preview the document to be printed
Click File -> Page Preview
To close the preview click the Close Preview button
https://img.brainkart.com/imagebk34/4MkXDN8.jpg

## Slide 198: Page Preview, Setting the printer and Printing a document
Setting the Printer and Printing
Click File -> Print or Ctrl + P
Click General Tab
Select the required printer
Specify Number of Copies using spin arrows.
Click Print button.
https://img.brainkart.com/imagebk34/4MkXDN8.jpg

## Slide 199: Open Office tools for creating spreadsheet
Introduction to spreadsheet
Spreadsheet is use for calculate, graph, and analyze the information.
https://img.brainkart.com/imagebk34/gqWsgKo.jpg

## Slide 200: Open Office tools for creating spreadsheet
Features of OpenOffice Calc
Connecting with Excel
AutoSum
List AutoFill
AutoFill
Charts
Databases
Functions
https://www.openoffice.org/es/producto/pix/calc-big.png

## Slide 201: Structure of a Spreadsheet
Creating a new worksheet
Start -> All Programs ->OpenOffice -> OpenOffice Calc (or)
Double-click on “OpenOffice” icon the desktop
File -> New -> Spreadsheet
https://www.wikihow.com/images/thumb/7/7d/Learn-Spreadsheet-Basics-with-OpenOffice.org-Calc-Step-1.jpg/v4-460px-Learn-Spreadsheet-Basics-with-OpenOffice.org-Calc-Step-1.jpg.webp

## Slide 202: Structure of a Spreadsheet
Parts of the OpenOffice Calc Window
Title Bar
Control Buttons
Menu Bar
Tools Bar
Scroll bar
Status bar
https://img.brainkart.com/imagebk34/RuTbyaO.jpg

## Slide 203: Parts of the OpenOffice Calc Window
Title Bar
The title bar is displayed at the top most part of the window, which displays the name of the document and the name of the application.
https://wiki.openoffice.org/w/images/5/51/Calc3-mainwindow.png

## Slide 204: Parts of the OpenOffice Calc Window
Control Buttons
In the right corner of title bar: minimize, maximize/restore and (3) close control buttons are available.
https://img.brainkart.com/imagebk34/PPypAbe.jpg

## Slide 205: Parts of the OpenOffice Calc Window
Menu Bar
The menu bar is just below the title bar which comprises of various menus consisting of various options.
https://img.brainkart.com/imagebk34/O5uOC27.jpg

## Slide 206: Parts of the OpenOffice Calc Window
Tool Bar
Under the menu bar, there are two toolbars available by default. They are:
Standard Toolbar
Formatting Toolbar
https://img.brainkart.com/imagebk34/z1DLVq1.jpg

## Slide 207: Parts of the OpenOffice Calc Window
Tool Bar
Under the menu bar, there are two toolbars available by default. They are:
Standard Toolbar
Formatting Toolbar
https://img.brainkart.com/imagebk34/RR6C4Ld.jpg

## Slide 208: Parts of the OpenOffice Calc Window
Status Bar
The status bar is at the bottom of the window which shows the current status of the document such as number of pages, current page number, default language etc.
https://img.brainkart.com/imagebk37/8hBvqK7.jpg

## Slide 209: Structure of a Spreadsheet
Row, Column, Cell and Cell Pointer
The worksheet has number of rows and columns.
each column is labelled as A, B, C, D and rows are numbered from 1, 2, 3
OpenOffice Calc version 4.1.5 contains 1024 columns and 10,48,576 rows.
Intersection of each row and column makes a box which is called as “Cell”
https://img.brainkart.com/imagebk34/qbZdacA.jpg

## Slide 210: Structure of a Spreadsheet
Worksheet tabs
At the bottom of the grid of cells are the sheet tabs.
When you open a new worksheet, sheet1 is the default active sheet.
If you click on another sheet, it will become active and its color will turn white.
To select multiple sheet select sheet and press Ctrl+Click.
https://img.brainkart.com/imagebk34/raYfVHv.jpg

## Slide 211: Structure of a Spreadsheet
Worksheet tabs
On the left of the sheet tab, four navigation buttons are used to move between worksheets.
Move to the First sheet
Move to the previous sheet
Move to Next sheet
Move to the Last sheet
https://img.brainkart.com/imagebk34/IPuulWG.jpg

## Slide 212: Working with Spreadsheet
Working with Data
“Tab key” is used to move the cell pointer towards the right side .
“Shift+Tab” is used to move backward.
“Enter” key is also used to move the cell pointer.
Four “direction keys” are used to move the cell pointer anywhere in the worksheet.
https://upload.wikimedia.org/wikipedia/commons/9/93/OpenOffice_Calc_4.0.png

## Slide 213: Working with Data
Entering Data
Entering Number
Entering Text
Entering Date and Time
https://www.lifewire.com/thmb/rqQ0zO6Ii7DJKNdyWSJkxfFuv3k=/1600x870/filters:no_upscale():max_bytes(150000):strip_icc()/36-openoffice-calc-basic-spreadsheet-tutorial-599f0be867e9479f8773977cfbcc979e.jpg

## Slide 214: Working with Spreadsheet
Copy, Cut and Paste – Spreadsheet
Copy and paste Data
Select the cell or cells you want to copy
Select Edit -> Copy or Click “Copy” icon from the standard toolbar or Press Ctrl +C
Move the cell pointer to the cell in which you want to paste.
Select Edit -> Paste or Click “Paste” icon or Press Ctrl + V
https://www.shorttutorials.com/openoffice-spreadsheet/images/paste.jpg

## Slide 215: Working with Spreadsheet
Copy, Cut and Paste – Spreadsheet
Cut and Paste Data
Select the cell or cells you want to cut
Select Edit -> Cut or Click “Cut” icon from the standard toolbar or Press Ctrl + X
Move the cell pointer to the cell in which you want to paste.
Select Edit -> Paste or Click “Paste” icon or Press Ctrl + V
https://www.shorttutorials.com/openoffice-spreadsheet/images/paste.jpg

## Slide 216: Working with Spreadsheet
Copy, Cut and Paste – Spreadsheet
Copy a formula from one cell and paste it in multiple cells
Copy the formula from H2 using Ctrl + C
Select all cells (i.e., H3 to H11) in which you want to paste this addition formula.
Paste the copied formula using Ctrl + V or Edit -> Paste (or) Click “Paste” icon.
https://img.brainkart.com/imagebk34/ceZsIOh.jpg

## Slide 217: Inserting Columns, Rows and Cells – Spreadsheet
Inserting Columns
Select the column where a new column should be inserted
Right-click on the selected column name that you selected. A pop-up menu appears.
click the “Insert Columns” option from the menu.
https://img.brainkart.com/imagebk34/NDHDYwR.jpg

## Slide 218: Inserting Columns, Rows and Cells – Spreadsheet
Inserting Columns
A new column can also be inserted using Insert -> Column’s command.
https://img.brainkart.com/imagebk34/NDHDYwR.jpg

## Slide 219: Inserting Columns, Rows and Cells – Spreadsheet
Inserting Rows
Select the row where a new row to be inserted.
Right-click on the row number, a pop-up menu appears
click “Insert Rows” option from the menu.
https://img.brainkart.com/imagebk34/26kerh2.jpg

## Slide 220: Inserting Columns, Rows and Cells – Spreadsheet
Inserting Rows
A new row can also be inserted using Insert -> Rows
https://img.brainkart.com/imagebk34/g0pJCCq.jpg

## Slide 221: Inserting Columns, Rows and Cells – Spreadsheet
Inserting Cells
To insert a new cell between two existing cells, just right-click on any existing cell
From the pop-up menu, select “Insert” option
The “Insert Cells” dialog box appear with four options
Shift cells down
Shift cells right
Entire row
Entire Column
https://img.brainkart.com/imagebk34/d0pFgWE.jpg

## Slide 222: Inserting Columns, Rows and Cells – Spreadsheet
Inserting Cells
To insert a new cell between two existing cells, just right-click on any existing cell
From the pop-up menu, select “Insert” option
The “Insert Cells” dialog box appear with four options
Shift cells down
Shift cells right
Entire row
Entire Column
https://img.brainkart.com/imagebk34/d0pFgWE.jpg

## Slide 223: Inserting Columns, Rows and Cells – Spreadsheet
Inserting multiple columns or rows
Multiple columns or rows can be inserted at once rather than inserting one at a time.
Select multiple rows or columns for insertion.
https://img.brainkart.com/imagebk34/NDHDYwR.jpg

## Slide 224: Inserting Columns, Rows and Cells – Spreadsheet
Inserting Columns, Rows and Cells using “Insert Cells” Toolbar
Click View -> Toolbars -> Insert Cell
https://img.brainkart.com/imagebk34/kLsTJ3z.jpg

## Slide 225: Working with Spreadsheet
Deleting columns and rows - Spreadsheet
Delete single column or row.
Delete multiple columns or rows.
https://img.brainkart.com/imagebk34/Hab10Nr.jpg

## Slide 226: Save, Close and Open the Worksheet
Saving Worksheet
File -> Save (or) Ctrl + S (or) Click “Save”
If the file has not been saved previously, the Save As dialog box will appear.
Give “File Name”.
Click “Save” button.
https://img.brainkart.com/imagebk34/kJIIW7N.jpg

## Slide 227: Save, Close and Open the Worksheet
Closing a Worksheet
File -> Close command (or) Press Ctrl + W.
https://img.brainkart.com/imagebk34/kJIIW7N.jpg

## Slide 228: Save, Close and Open the Worksheet
Opening an existing worksheet
File → Open command (or) “Open” icon (or) Ctrl + O
https://img.brainkart.com/imagebk34/weTQMdS.jpg

## Slide 229: Creating Formulae – Spreadsheet
Creating Formulae
Operators
Construction of formula
https://wiki.openoffice.org/w/images/1/1a/CG3Ch3F14d.png

## Slide 230: Creating Formulae
Operators
Arithmetic Operators
Relational Operators
Reference Operators
Text Operator
https://img.brainkart.com/imagebk34/9csFCzE.jpg

## Slide 231: Creating Formulae
Operators
Arithmetic Operators
Relational Operators
Reference Operators
Text Operator
https://img.brainkart.com/imagebk34/e7frlNi.jpg

## Slide 232: Creating Formulae
Operators
Arithmetic Operators
Relational Operators
Reference Operators
Text Operator
https://img.brainkart.com/imagebk34/ZrOVphS.jpg

## Slide 233: Creating Formulae
Operators
Arithmetic Operators
Relational Operators
Reference Operators
Text Operator
https://img.brainkart.com/imagebk34/4z7Lh1I.jpg

## Slide 234: Creating Formulae
Construction of formula
Formula should begin with an = sign.
= cell reference1 <operator> cell reference2 <operator> ……………….
https://img.brainkart.com/imagebk34/dlB1grO.jpg

## Slide 235: Functions - Spreadsheet
Inserting Functions into Worksheet
Direct Insert method
SUM (range 1; range 2; range 3…… range n)
https://img.brainkart.com/imagebk34/ramRQqZ.jpg

## Slide 236: Functions - Spreadsheet
Inserting Functions into Worksheet
Using Function Wizard method
Insert -> Function (or) Ctrl + F2
https://img.brainkart.com/imagebk34/ajcHnGW.jpg

## Slide 237: Formatting Worksheet – Spreadsheet
Text Formatting
Making the cell contents as bold, italics, underlined, changing font style, size, colour etc
https://img.brainkart.com/imagebk34/hDWGpop.jpg

## Slide 238: Formatting Worksheet – Spreadsheet
Text Formatting
Number formatting options are used to visually change the format of a numeric content
https://img.brainkart.com/imagebk34/rNkLlHz.jpg

## Slide 239: Formatting Worksheet – Spreadsheet
Text Formatting
Number formatting options are used to visually change the format of a numeric content
https://img.brainkart.com/imagebk34/rNkLlHz.jpg

## Slide 240: Working with Chart – Spreadsheet
Chart Wizard
Steps
Chart type
Data Range
Data Series
Chart Elements.
https://img.brainkart.com/imagebk34/9RUqLW8.jpg

## Slide 241: Chart Wizard
Chart type
This step use to select Chart type under the “Choose a chart type” list box
Select Chart type
Select chart style.
Click, “Next” button.
https://img.brainkart.com/imagebk34/pjrCQ35.jpg

## Slide 242: Chart Wizard
Data Range
This step Specify the range of data for which the chart should be created
Click “Select data range”.
There are two checkboxes used to set the first row or first column or both, as X and Y axis labels to the chart.
Click "Next" button to move to the third step.
https://img.brainkart.com/imagebk34/j21BZTL.jpg

## Slide 243: Chart Wizard
Data Series
In this step, the user can fine tune the data to be included in the chart.
To add some more columns click “Add” button.
To remove columns click “Remove” button.
Click “Next” button to move the last step.
https://img.brainkart.com/imagebk34/DMIDX2P.jpg

## Slide 244: Chart Wizard
Chart Element
This step is used to insert or change titles and legend.
In “Title” box, type the title for the chart.
To add a subtitle type it in the “Subtitle” box.
User can add or modify the labels of X and Y axis.
To create a chart, click “Finish” button.
https://img.brainkart.com/imagebk34/DMIDX2P.jpg

## Slide 245: Working with Chart – Spreadsheet
Editing Chart elements
After inserting a chart any element of the chart can be modified. To modify the element
Double click on the element
Right click on the selected element
Select Format from the popup menu.
https://img.brainkart.com/imagebk34/O3mltu2.jpg

## Slide 246: Structure of Presentation
Opening a new presentation
To open impress click Start button and select All Programs -> Open Office -> OpenOffice Impress.
https://img.brainkart.com/imagebk34/hmXOjMx.jpg

## Slide 247: Structure of Presentation
Creating a new presentation
You can create a presentation by any one of the following methods.
By selecting an Empty presentation
By selecting from template
By selecting from Open existing presentation
https://img.brainkart.com/imagebk34/RCxsLNt.jpg

## Slide 248: Creating a new presentation
Using Empty presentation
Select Empty presentation under Type.
Click Next, Choose a design under Select a slide design
Click Next, click an item to see a preview of the transition.
Select how the presentation will be Speed drop-down menu.
Click Create, A new presentation is created
https://img.brainkart.com/imagebk34/7U1S8sf.jpg

## Slide 249: Creating a new presentation
Using Template
If you choose the option from template, it uses a template design already created as the basis for a new presentation. The wizard changes to show a list of available templates. Choose the template that you want.
https://img.brainkart.com/imagebk34/ynIHqs9.jpg

## Slide 250: Creating a new presentation
Using Open existing presentation
If you choose the option Open existing presentation, it helps in continuing the work on a previously created presentation.
You have to open a presentation already prepared by clicking Open button. The wizard changes to show a list of existing presentations, from which you can choose the one that you want.
https://img.brainkart.com/imagebk34/Uu8FTVW.jpg

## Slide 251: Structure of presentation
Parts of the main Impress window
The main Impress window has three parts:
Slides pane
Workspace
Task pane.
Additionally, several toolbars can be displayed or hidden during the creation of a presentation.
https://wiki.openoffice.org/w/images/thumb/d/dd/IG1-1.png/500px-IG1-1.png

## Slide 252: Parts of the main Impress window
Slides pane
The Slides pane contains thumbnail pictures of the slides in your presentation, in the order of our insertion of slides.
https://img.brainkart.com/imagebk34/OsL0cuW.jpg

## Slide 253: Parts of the main Impress window
Tasks pane
The Tasks pane has five sections:
Master Pages
Layout
Table Design
Custom Animation
Slide Transition
https://wiki.openoffice.org/w/images/thumb/d/dd/IG1-1.png/500px-IG1-1.png

## Slide 254: Structure of presentation
Window elements of Impress
The window elements of Impress includes: Title Bar, Menu Bar, Tool Bar, Ruler Bar which are similar to the elements in Open Office writer.
View Buttons
Status Bar
Navigator
https://img.brainkart.com/imagebk34/Nw6cNac.jpg

## Slide 255: Working with Presentation
Workspace
The Workspace has five tabs:
Normal
Outline
Notes
Handout
Slide Sorter
These five tabs are called View Buttons
The actual Workspace section is below the View Buttons
https://img.brainkart.com/imagebk34/Nw6cNac.jpg

## Slide 256: Working with Presentation
Formatting a presentation
Creating the first slide
Inserting additional slides
Deleting a Slide
Rearranging slides
https://wiki.openoffice.org/w/images/thumb/8/85/ImpressMainWindow.png/500px-ImpressMainWindow.png

## Slide 257: Formatting a presentation
Creating the first slide
The first slide is normally a title slide Decide the layout as per its purpose of presentation.
You can select a layout in the Layout section of the Tasks pane by clicking on it.
https://img.brainkart.com/imagebk34/n7wbHaV.jpg

## Slide 258: Formatting a presentation
Inserting additional slides
Insert a new slide. This can be done in a variety of ways.
Insert -> Slide.
Right-click on the present slide, and select Slide -> New Slide
Click the Slide icon in the Presentation toolbar
Select the layout slide that best fits your needs.
Modify the elements of the slide.
https://img.brainkart.com/imagebk34/pkBR8GI.jpg

## Slide 259: Formatting a presentation
Deleting a Slide
You can delete a slide at any time using the following procedure.
Select the slide you want to delete
Click Edit
Delete slide
Or else, right click the slide and choose Delete slide
https://img.brainkart.com/imagebk34/SEhh9AL.jpg

## Slide 260: Formatting a presentation
Rearranging slides
Select the slide that you want to rearrange.
Drag that slide to the desired position by holding the mouse using left click.
Release the mouse once you drag the slide to the desired place.
https://img.brainkart.com/imagebk34/sq6L4Tj.jpg

## Slide 261: Working with presentation
Running the slide show
To run the slide show, do one of the following:
Click Slide Show -> Slide Show on the main menu bar
Click the Slide Show button
Press F5 or F9
To exit the slide show, press the Esc key
https://img.brainkart.com/imagebk34/LLqz6RR.jpg

## Slide 262: Working with presentation
Saving a Presentation
To save the presentation, do one of the following:
Click File -> Save
Give file name
Click Save
https://img.brainkart.com/imagebk34/WCWQSaR.jpg

## Slide 263: Creating Graphic Objects – Presentation
Inserting images - presentation
To insert Image place the cursor in the place where you want the image to be inserted. Then, Click Insert -> select Picture From file.
https://img.brainkart.com/imagebk34/5C5ra5E.jpg

## Slide 264: Creating Graphic Objects – Presentation
Inserting audio and video
The audio and movie files can be inserted by clicking Insert Movie and Sounds Option from the Insert menu.
Select the audio or movie file form the specified location and open.
https://img.brainkart.com/imagebk34/5C5ra5E.jpg

## Slide 265: Familiarization with PC Management
(3 hours)
Notes: Title - The learning outcome
Subtitle - Duration

## Slide 266: In this section, we will discuss:
Disk management
Task scheduler
Even viewer
Device manager
Shared folders
Services and applications
Virus and Antivirus
Using different types of firewalls -pocket firewalls, State-full firewalls, Application layer firewalls and Proxy firewalls
Notes: Mention the parent topics one by one. This particular learning outcome has 4 parent topics.

## Slide 267: Familiarization with Disk management
Introduction
Disk Management is a Microsoft Windows utility first introduced in Windows XP as a replacement for the fdisk command. It enables users to view and manage the disk drives installed in their computer and the partitions associated with those drives.
Image Source:https://www.computerhope.com/issues/pictures/win10-disk-management.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 268: Familiarization with Disk management
How to Open Disk Management
Way1: The easiest way to open Disk Management in Windows 10 is from computer Desktop.
Right click on Start Menu (or press Windows+X hotkey) and then select "Disk Management".
Image Source: https://www.diskpart.com/windows-10/images/windows-10-disk-management/open-disk-management-windows-10.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 269: Familiarization with Disk management
How to Open Disk Management
Way2: Use Windows+R hotkey to open Run window. Then type "Diskmgmt.msc" and click "OK" or hit "Enter" key.
https://www.diskpart.com/windows-10/images/windows-10-disk-management/open-disk-management-from-run.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 270: Familiarization with Disk management
How to Open Disk Management
Way 3: Directly type "disk management" in the Search box and choose "Create and format hard disk partitions" from the results.
https://www.diskpart.com/windows-10/images/windows-10-disk-management/search-disk-management.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 271: Familiarization with Disk management
How to Use Disk Management
Disk Management has two main sections—a top and a bottom:
The top section contains a list of all the partitions, formatted or not, that Windows recognizes.
The bottom section contains a graphical representation of the physical drives installed in the computer.
https://www.isunshare.com/images/article/windows-8/access-disk-management-in-windows-8/find-disk-management.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 272: Familiarization with Disk management
How to Partition a Hard Drive
Open Disk Management the tool included in all versions of Windows that lets you partition drives, among a number of other things.
https://www.lifewire.com/thmb/0UXXUZDix55KTmmwa4fGJYgxmtE=/1227x884/filters:no_upscale():max_bytes(150000):strip_icc()/009_how-to-partition-a-hard-drive-2626081-5c82c5dc46e0fb0001cbf4cc.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 273: Familiarization with Disk management
How to Partition a Hard Drive
When Disk Management opens, you should see an Initialize Disk window with the message "You must initialize a disk before Logical Disk Manager can access it.
Choose a partition style for the new hard drive
Locate the hard drive where you want to partition.
https://www.lifewire.com/thmb/CDl9e9ow0Ra_ULfQ83rnJpWb9sQ=/1007x672/filters:no_upscale():max_bytes(150000):strip_icc()/001_how-to-partition-a-hard-drive-2626081-5c82ad7c4cedfd000190b160.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 274: Familiarization with Disk management
How to Partition a Hard Drive
Once you've found the space tap-and-hold or right-click anywhere on it, and choose New Simple Volume.
https://www.lifewire.com/thmb/ATQst9QBPgZEWXtUMWrYBmTB2gI=/1126x697/filters:no_upscale():max_bytes(150000):strip_icc()/002_how-to-partition-a-hard-drive-2626081-5c82c62d46e0fb00010f10b6.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 275: Familiarization with Disk management
How to Partition a Hard Drive
Choose Next > on the New Simple Volume Wizard window
https://www.lifewire.com/thmb/9zHKG3FGCmO-8EWWoPh1VUagwdg=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/003_how-to-partition-a-hard-drive-2626081-5c82adb846e0fb0001a0be31.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 276: Familiarization with Disk management
How to Partition a Hard Drive
Choose Next > on the Specify Volume Size step to confirm the size of the drive you're creating.
https://www.lifewire.com/thmb/4xtocdwN00p2tsp4W0rKb7JyyQs=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/004_how-to-partition-a-hard-drive-2626081-5c82add546e0fb0001a0be33.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 277: Familiarization with Disk management
How to Partition a Hard Drive
Select Next > on the Assign Drive Letter or Path step.
https://www.lifewire.com/thmb/m5ghUv2ipi2RYEJ4mSQoAifE2Us=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/005_how-to-partition-a-hard-drive-2626081-5c82adf64cedfd000190b164.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 278: Familiarization with Disk management
How to Partition a Hard Drive
Choose Do not format this volume on the Format Partition step, and then select Next >.
https://www.lifewire.com/thmb/2C8NQOgm8E61SFgnXYQ0kYFadlU=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/006_how-to-partition-a-hard-drive-2626081-5c82ae1c46e0fb000113662e.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 279: Familiarization with Disk management
How to Partition a Hard Drive
Verify your choices on the Completing the New Simple Volume Wizard screen
Choose Finish and Windows will partition the drive.
https://www.lifewire.com/thmb/E7Jh6NzEHjBl23UqxyZjhe0UHJQ=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/007_how-to-partition-a-hard-drive-2626081-5c82ae48c9e77c0001a3e4f4.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 280: Familiarization with Disk management
How to Partition a Hard Drive
Next, Windows will try to open the new drive automatically.
you'll see this message instead: "You need to format the disk in drive F: before you can use it. Do you want to format it?“
Select Cancel
https://www.lifewire.com/thmb/kyLqh1cebh2m014peEIavGBvS40=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/008_how-to-partition-a-hard-drive-2626081-5c82ae75c9e77c0001a6761a.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 281: Familiarization with Disk management
How to Format A Hard Drive in Windows
Open Disk Management, the hard drive manager included with all versions of Windows.
https://www.lifewire.com/thmb/BAfcDsXhVa_FevvK8x6qelrTVFU=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/001_how-to-format-a-hard-drive-2626077-5c3e8296c9e77c0001323453.jpg

## Slide 282: Familiarization with Disk management
How to Format A Hard Drive in Windows
After Disk Management opens, which might take several seconds, look for the drive you want to format from the list at the top. There's a lot of information in Disk Management, so if you can't see everything, maximize the window.
https://www.lifewire.com/thmb/ZbPAraYUOebfV10OtPmq_TdKvno=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/002_how-to-format-a-hard-drive-2626077-5c3e82adc9e77c00012a04ab.jpg

## Slide 283: Familiarization with Disk management
How to Format A Hard Drive in Windows
If you don't see the drive listed on the top or an Initialize Disk window appears, it probably means that the hard drive is new and has not yet been partitioned. Partitioning is something that must be done before a hard drive is formatted.
https://www.lifewire.com/thmb/CnaftQSECOW9KiWCp7RXrnc16Ew=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/003_how-to-format-a-hard-drive-2626077-5c3e82c6c9e77c00019f8939.jpg

## Slide 284: Familiarization with Disk management
How to Format A Hard Drive in Windows
The first of several formatting details which we'll cover over the next several steps is the volume label, which is essentially a name given to the hard drive.
In the Volume label textbox, enter whatever name you'd like to give to the drive.
https://www.lifewire.com/thmb/ULWAd0M1yuZoE5D760-eSQNA5ls=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/004_how-to-format-a-hard-drive-2626077-5c3e82e2c9e77c00016ee2c0.jpg

## Slide 285: Familiarization with Disk management
How to Format A Hard Drive in Windows
Next up is the file system choice. In the File system textbox, choose NTFS.
https://www.lifewire.com/thmb/FXk--js9sw3JIIMXp-3BwFAdor4=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/005_how-to-format-a-hard-drive-2626077-5c3e8301c9e77c00012a16e7.jpg

## Slide 286: Familiarization with Disk management
How to Format A Hard Drive in Windows
In the Allocation unit size textbox, choose Default. The best allocation size based on the size of the hard drive will be chosen.
https://www.lifewire.com/thmb/LLEq6hLThS5AjOLYd_bZW7qNtKY=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/006_how-to-format-a-hard-drive-2626077-5c3e831cc9e77c0001a9258c.jpg

## Slide 287: Familiarization with Disk management
How to Format A Hard Drive in Windows
Next Click on “Perform a quick format checkbox”.
https://www.lifewire.com/thmb/Y_A6WN76uQO48YbmuinItp5fOFc=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/007_how-to-format-a-hard-drive-2626077-5c3e833a46e0fb0001aa2acc.jpg

## Slide 288: Familiarization with Disk management
How to Format A Hard Drive in Windows
The final format option is the Enable file and folder compression setting that is unchecked by default, which we recommend sticking with.
https://www.lifewire.com/thmb/9jJpxH6DWXVuIkfUpJ92Or9hyhk=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/008_how-to-format-a-hard-drive-2626077-5c3e835dc9e77c0001325f39.jpg

## Slide 289: Familiarization with Disk management
How to Format A Hard Drive in Windows
Review the settings you've made in the last several steps and then click OK.

## Slide 290: Familiarization with Disk management
How to Format A Hard Drive in Windows
Windows is usually pretty good about warning you before you might do something damaging, and a hard drive format is no exception.
https://www.lifewire.com/thmb/JVNJP4Vd-JCpYjgdOHCkCIfHtSs=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/010_how-to-format-a-hard-drive-2626077-5c3e846dc9e77c0001329a59.jpg

## Slide 291: Familiarization with Disk management
How to Format A Hard Drive in Windows
The hard drive format has begun! You can check the progress by watching the Formatting
https://www.lifewire.com/thmb/BptGPHyWzUy_bgo4qjV0kEnN84Y=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/011_how-to-format-a-hard-drive-2626077-5c3e848b46e0fb0001526cb5.jpg

## Slide 292: Familiarization with Disk management
How to Format A Hard Drive in Windows
That's it! Your hard drive has been formatted and it's ready for use in Windows.
https://www.lifewire.com/thmb/hQxcswELoqi-45n_usnJnbjniv4=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/013_how-to-format-a-hard-drive-2626077-5c3e84c4c9e77c00019ff4b4.jpg

## Slide 293: Task scheduler
How to create an automated task using Task Scheduler on Windows
Windows Scheduler helps you automate your work.
Task Scheduler works by keeping tabs of the time and events on your computer and executes the task as soon as the condition is met.
https://www.windowscentral.com/sites/wpcentral.com/files/styles/xlarge/public/field/image/2019/01/create-task-automation-task-scheduler-windows-10.jpg

## Slide 294: Task scheduler
How to create a basic task using Task Scheduler
Select the Task Scheduler app from start window.
Right click on Task Scheduler Library in the left navigation tree, and select New Folder.
https://www.lifewire.com/thmb/RNr_fUghjXvgPXXBHN09JdEOcCA=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/A1-CreateanAutomatedTaskwithWindows10TaskScheduler-annotated-78bd399f1e1143e6a7ed82e03e00b340.jpg

## Slide 295: Task scheduler
How to create a basic task using Task Scheduler
Give the folder a name like "My Tasks" and select OK.
https://www.lifewire.com/thmb/kNhis6PP_2niv800XyA9en31jTQ=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/A3-CreateanAutomatedTaskwithWindows10TaskScheduler-annotated-e35ab416d0c64fdda282e0692d84b1a2.jpg

## Slide 296: Task scheduler
How to create a basic task using Task Scheduler
Select the new folder you've created. In the Actions navigation bar on the right, select Create Basic Task. This will open the Create Basic Task Wizard. Type a name for the task in the Name field. Select Next to continue.
https://www.lifewire.com/thmb/HBVzZxV5INUP4WZNTtvLjEX0-iY=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/A4-CreateanAutomatedTaskwithWindows10TaskScheduler-annotated-b678b1b51be44a77afdcfb4d0f445c8d.jpg

## Slide 297: Task scheduler
How to create a basic task using Task Scheduler
The next step of the wizard is to choose a trigger for your task. You can choose one of the time intervals, or one of the system events. In this example, we'll select Daily. Select Next to continue.
https://www.lifewire.com/thmb/n1qc96cze8AqNsZTWqx6NEBeAls=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/A5-CreateanAutomatedTaskwithWindows10TaskScheduler-annotated-d9bde967c811431196dc03dd9b9119cc.jpg

## Slide 298: Task scheduler
How to create a basic task using Task Scheduler
The next step is to fine tune the interval trigger. In this case we'll set the trigger to happen at 8 AM every day, starting today. Set the recurrence to every 1 day. Select Next to continue
https://www.lifewire.com/thmb/l3vbtXCxQnvw7CF_fo2iSKmKsMY=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/A6-CreateanAutomatedTaskwithWindows10TaskScheduler-annotated-57456959f53c4477a0bdeb1e3392d041.jpg

## Slide 299: Task scheduler
How to create a basic task using Task Scheduler
The next step is to set up the Action for the task. In this case, select Start a Program and then select Next.
https://www.lifewire.com/thmb/l3vbtXCxQnvw7CF_fo2iSKmKsMY=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/A6-CreateanAutomatedTaskwithWindows10TaskScheduler-annotated-57456959f53c4477a0bdeb1e3392d041.jpg

## Slide 300: Task scheduler
How to create a basic task using Task Scheduler
Select the Browse button and browse to Chrome which should be located at "C:\Program Files (x86) \Google\Chrome\Application\". The file name is chrome.exe. Once you browse to the file, select it and select Open. Select Next to continue
https://www.lifewire.com/thmb/FYhWIuRaosRiGaad8ra-IBVw7CI=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/A8-CreateanAutomatedTaskwithWindows10TaskScheduler-annotated-315d4492766344d78d151a7c16628b6d.jpg

## Slide 301: Task scheduler
How to create an advanced task using Task Scheduler
On the Finish tab of the Wizard, you'll see the Trigger status and Action you've created. Select Finish to close the Basic Task wizard.
You'll see your new task in the main pane in the Task Scheduler window. You can right click the task and select Run
https://www.lifewire.com/thmb/PSVOXzQ1-CLIpEFu3T9s09jGxBg=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/A9-CreateanAutomatedTaskwithWindows10TaskScheduler-annotated-af9aa5e1784c4c2aa018ea76bbaf4193.jpg

## Slide 302: Task scheduler
How to create a basic task using Task Scheduler
Go to Task Scheduler window, select Create Task in the right navigation pane.
On the General tab, type a name for your task in the Name field.
On the Triggers tab, select New, select Monthly, select all months in the Months dropdown and set the Days dropdown to 30 for the end of the month. Make sure Enabled is selected. Select OK.
https://www.lifewire.com/thmb/FnMJ5Ebj5rcHcw-_dTgR_ylfOWg=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/A3-CreateanAutomatedTaskwithWindows10TaskScheduler-annotated-7b1371ad86014c54bb89c4e41ae7adba.jpg

## Slide 303: Task scheduler
How to create a basic task using Task Scheduler
On the Actions tab, select New. Select Start a program in the Action dropdown. Select the Browse button and browse to the Word executable at "C:\Program Files\Microsoft Office\root\Office16\". The file name is winword.exe. Once you browse to the file, select it and select Open. Select OK.
https://www.lifewire.com/thmb/pBtrLJyv4M17FdT3or9hYBYcHHI=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/B4-CreateanAutomatedTaskwithWindows10TaskScheduler-annotated-ac753d42c0104558b56221eb19fa503f.jpg

## Slide 304: Task scheduler
How to create a basic task using Task Scheduler
On the Conditions tab, configure your task to run.
On the Settings tab, configure your task.
Once you're done setting up all of the task tabs, select OK to finish. You'll see the task appear in the main Task Scheduler window.
https://www.lifewire.com/thmb/1Hd1QceJxjuMNA_BqO8SdbspUQE=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/B6-CreateanAutomatedTaskwithWindows10TaskScheduler-annotated-4dcf01a5683043a4a801234548c83806.jpg

## Slide 305: Task scheduler
How to run, edit, and delete a task using Task Scheduler
Open Start, Search Task Scheduler, click to open the experience.
Expand the Task Scheduler Library.
Select the folder with your tasks.
To run a task right-click it and select the Run option.
To edit a task, right-click it and select the Properties options.
To delete a task, right-click it and select the Delete option.
https://i0.wp.com/techdirectarchive.com/wp-content/uploads/2020/04/screenshot-2020-04-02-at-16.30.42.png?resize=478%2C316&ssl=1

## Slide 306: Even viewer
Definition
The Windows Event Viewer is an administrative tool found in all versions of Windows. It allows you to view events, errors, and additional important information about what's happening under the hood in your operating system.
https://www.computerhope.com/jargon/e/eventviewer-win10.jpg

## Slide 307: Opening the Event Viewer
Open it by search
Type event in the search box on taskbar and choose View event logs in the result.
https://www.isunshare.com/images/article/windows-10/6-ways-to-open-event-viewer-in-windows-10/type-event-and-tap-view-event-logs.png

## Slide 308: Opening the Event Viewer
Turn on Event Viewer via Run
Press Windows+R to open the Run dialog, enter eventvwr (or eventvwr.msc) and hit OK
https://www.isunshare.com/images/article/windows-10/6-ways-to-open-event-viewer-in-windows-10/enter-eventvwr-and-hit-ok.png

## Slide 309: Opening the Event Viewer
Turn on Event Viewer via Run
Open Command Prompt, type eventvwr and press Enter
https://www.isunshare.com/images/article/windows-10/6-ways-to-open-event-viewer-in-windows-10/type-eventvwr-and-press-enter.png

## Slide 310: Opening the Event Viewer
Open Event Viewer in Control Panel
Access Control Panel, enter event in the top-right search box and click View event logs in the result.
https://www.isunshare.com/images/article/windows-10/6-ways-to-open-event-viewer-in-windows-10/open-event-viewer-in-control-panel.png

## Slide 311: Opening the Event Viewer
Open it in This PC
Open This PC, type event viewer in the search box on the top-right corner, and then double-click Event Viewer in the list.
https://www.isunshare.com/images/article/windows-10/6-ways-to-open-event-viewer-in-windows-10/open-event-viewer-in-this-pc.png

## Slide 312: Device manager
What Is Device Manager
Device Manager is used to manage the hardware devices installed in a computer like hard disk drives, keyboards, sound cards, USB devices, and more.
https://www.lifewire.com/thmb/_uKM1QCadzk06CvvYR2AK03d7FY=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/device-manager-101f5f25854b46b9811278cc4608632f.png

## Slide 313: Device manager
How to Access Device Manager
Device Manager can be accessed in several different ways in all versions of Windows, most commonly from the Control Panel, the Command Prompt, or Computer Management.
Device Manager can also be opened through the command-line or Run dialog box with a special command.
https://www.lifewire.com/thmb/c4VGe_uuVYKcTF-nRFXX1x_MMm8=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/device-manager-windows-10-start-menu-d6c9d5b991144df488027d2e439f3858.png

## Slide 314: Device manager
How to Use Device Manager
Device Manager lists devices in separate categories so that it's easier to find what you're looking for. You can expand each section to see which devices are listed inside. Once you find the right hardware device, double-click it to see more information like its current status, driver details, or in some cases its power management options.
https://www.lifewire.com/thmb/GXa_TZB89Phc5hH7OafO2Uhoo28=/650x0/filters:no_upscale():max_bytes(150000):strip_icc():format(webp)/device-manager-code-22-7a1e74f0662240f18ee19c5efa22b01a.png

## Slide 315: Shared folders
Share files or folders over a network
Right-click or press a file, select Give access to > Specific people.
Select a file, select the Share tab at the top of File Explorer, then in the Share with section select Specific people.
https://support.content.office.net/en-us/media/4436f313-6596-0ace-52dc-d04d96fa0257.png

## Slide 316: Shared folders
Stop sharing files or folders
Right-click or press a file or folder, then select Give access to > Remove access.
Select a file or folder, select the Share tab at the top of File Explorer, and then in the Share with section select Remove access.
https://support.content.office.net/en-us/media/75a38268-1dcd-7258-5dbf-45c0776a7a08.png

## Slide 317: Services and applications
Definition of services
A Windows service is an application that usually serves a core operating system function running in the background and has no user interface.
https://2.bp.blogspot.com/-BLD7zBOXjas/VNHsTZHZSOI/AAAAAAAAGjk/dAI8wBhiZ5U/s1600/openoffice-service2.PNG

## Slide 318: Services and applications
Definition of application
A program that is written to run under the Microsoft Windows operating system, also called a "Windows app." All 32-bit Windows applications run in the 32-bit and 64-bit versions of Windows. All 64-bit applications require 64-bit Windows, which is the standard on new Windows computers and tablets.
https://2.bp.blogspot.com/-BLD7zBOXjas/VNHsTZHZSOI/AAAAAAAAGjk/dAI8wBhiZ5U/s1600/openoffice-service2.PNG

## Slide 319: Virus and its type and Antivirus
Definition of VIRUS
A computer virus is a program which can harm our device and files and infect them for no further use. When a virus program is executed, it replicates itself by modifying other computer programs and instead enters its own coding.
https://miro.medium.com/max/624/1*0fBUSoM_Oigllf786MPoGA.png

## Slide 320: Virus and its type and Antivirus
Types of Computer Virus
Boot Sector Virus.
Direct Action Virus.
Resident Virus.
Multipartite Virus.
Overwrite Virus
Polymorphic Virus
https://cdn.ttgtmedia.com/rms/onlineimages/security-computer_virus-f_mobile.png

## Slide 321: Virus and its type and Antivirus
Types of Computer Virus
File Infector Virus
Space filler Virus
Macro Virus
https://cdn.ttgtmedia.com/rms/onlineimages/security-computer_virus-f_mobile.png

## Slide 322: Virus and its type and Antivirus
What Causes Computer Viruses
The delivery of a computer virus can happen in several ways.
One common method is via a phishing email.
Another technique is hosting malware on a server that promises to provide a legitimate program.
It can be delivered using macros or by injecting malicious code into legitimate software files.
https://intersys.co.uk//wp-content/uploads/2018/11/Computer_Malware.jpg

## Slide 323: Virus and its type and Antivirus
What Is a Computer Worm
A computer worm is malware, just like a virus, but a worm takes a copy of itself and propagates it to other users. Worms can also deliver a payload and exhaust resources.
https://blog.emsisoft.com/wp-content/uploads/2017/07/malware-worms-blog-banner.png

## Slide 324: Virus and its type and Antivirus
What Does a Computer Virus Do
The way a computer virus acts depends on how it’s coded. It could be something as simple as a prank that doesn’t cause any damage, or it could be sophisticated, leading to criminal activity and fraud.
Many viruses only affect a local device, but others spread across a network environment to find other vulnerable hosts.
https://enterprise.comodo.com/images/what-does-a-malware-virus-do.png

## Slide 325: Virus and its type and Antivirus
Symptoms of Computer Virus
Malware authors write code that is undetectable until the payload is delivered. However, like any software program, bugs could present issues while the virus runs.
https://image.slidesharecdn.com/computerviruses-140131070746-phpapp02/95/computer-viruses-7-638.jpg?cb=1391152119

## Slide 326: Virus and its type and Antivirus
Examples of Computer Virus
The web contains millions of computer viruses, but only a few have gained popularity and infect record numbers of machines. Some examples of widespread computer viruses include:
Morris Worm
Nimda
ILOVEYOU
https://hightouchtechnologies.com/wp-content/uploads/images/services/security-solutions/computer-viruses.png

## Slide 327: Virus and its type and Antivirus
Examples of Computer Virus
SQL Slammer
Stuxnet
CryptoLocker
Conficker
Tinba
Welchia
Shlayer
https://hightouchtechnologies.com/wp-content/uploads/images/services/security-solutions/computer-viruses.png

## Slide 328: Virus and its type and Antivirus
How to Prevent Computer Viruses
Install antivirus software
Don’t open executable email attachments.
Keep your operating system updated
Avoid questionable websites
Don’t use pirated software
https://cdn.redshift.autodesk.com/2014/04/How_To_Prevent_Malware_Secure_Network_2021.jpg

## Slide 329: Virus and its type and Antivirus
What is an Anti-Virus
Antivirus is a program that helps to secure various systems by scanning, detecting and removing viruses, malware, computer worms, and so on.
https://observer.com/wp-content/uploads/sites/2/2021/02/best-antivirus.jpg?quality=80

## Slide 330: Virus and its type and Antivirus
Different types of software
Cloud-Based Software
Standalone Software
Security Software Suites
https://images.slideplayer.com/19/5901606/slides/slide_6.jpg

## Slide 331: Virus and its type and Antivirus
What Does AntiVirus Software Do
Scan specific files or directories for any malware or known malicious patterns
Allow you to schedule scans to automatically run for you
Allow you to initiate a scan of a particular file or your entire computer, or of a CD or flash drive at any time.
http://www.hackingtutorials.org/wp-content/uploads/2016/04/how-does-antivirus-software-work-artwork.jpg

## Slide 332: Virus and its type and Antivirus
What Does AntiVirus Software Do
Remove any malicious code detected –sometimes you will be notified of an infection and asked if you want to clean the file, other programs will automatically do this behind the scenes.
Show you the ‘health’ of your computer.
http://www.hackingtutorials.org/wp-content/uploads/2016/04/how-does-antivirus-software-work-artwork.jpg

## Slide 333: Virus and its type and Antivirus
What are the Benefits of Antivirus Software
Antivirus solutions protect more than just laptops, office computers, smartphones and tablets.
They protect precious memories, music and photo libraries, and important documents from destruction by malware.
https://i1.wp.com/www.rrstech.in/wp-content/uploads/2020/02/Quick-heal-total-security-provider-nangloi-delhi.jpg

## Slide 334: Virus and its type and Antivirus
How Does Antivirus Software Work
Many antivirus software programs still download malware definitions straight to your device and scan your files in search of matches.
But since, as we mentioned, most malware regularly morphs in appearance to avoid detection, Webroot works differently.
https://i.ytimg.com/vi/1_rXO2Es5B8/maxresdefault.jpg

## Slide 335: Using different types of firewalls
What Is Firewall
A firewall is a network security device that monitors incoming and outgoing network traffic and decides whether to allow or block specific traffic based on a defined set of security rules.
https://static.javatpoint.com/tutorial/firewall/images/what-is-firewall-1.png

## Slide 336: Using different types of firewalls
Types of Firewalls
There are multiple types of firewalls based on their traffic filtering methods, structure, and functionality.
https://static.javatpoint.com/tutorial/firewall/images/types-of-firewall.png

## Slide 337: Using different types of firewalls
How Does a Firewall Work
There are multiple types of firewalls based on their traffic filtering methods, structure, and functionality.
https://drsoft.com/static/30c698446206093634f26a342b29ee72/a8378/how-a-firewall-works.png

## Slide 338: Using different types of firewalls
Advantages of Using Firewalls
Firewalls play an important role in the companies for security management.
It provides enhanced security and privacy from vulnerable services.
It prevents unauthorized users from accessing a private network that is connected to the internet.
https://www.referenceforbusiness.com/photos/firewalls-578.jpg

## Slide 339: Using different types of firewalls
Advantages of Using Firewalls
Firewalls provide faster response time and can handle more traffic loads.
A firewall allows you to easily handle and update the security protocols from a single authorized device.
It safeguards your network from phishing attacks.
https://www.referenceforbusiness.com/photos/firewalls-578.jpg

## Slide 340: Using different types of firewalls
How to Use Firewall Protection
Here are some tips to help you improve your firewall security:
Constantly update your firewalls as soon as possible
Use antivirus protection
Limit accessible ports and host
Have active network
https://securitytoday.com/-/media/SEC/Security-Products/Images/2015/02/Firewall_Protection.jpg

## Slide 341
Hardware Maintenance

## Slide 342: In this section, we will discuss:
Explain and apply common prevention methods
Explain Service Flow Sequence (SFS) and Trouble Shooting Chart (TSC) of PC
Safetyprecautions in handling PC
Sub assemblies and components
Important points to be considered while purchasingand replacing components
Concept of Preventive and corrective maintenance.
Tools required
Active & Passive Maintenance
Maintenance scheduling
Need of diagnostics program. Features, limitations. Examples of commonly used diagnostic programs.
Monitor, Monochrome and color, Types of Monitor
Components of Graphics Card
LCD and CRT Monitors
Flat screens vs CRT display systems
Displays memory quality and performance

## Slide 343: Explain and apply common prevention methods
Monitors
Keep it clean-use periodic cleaning, dusting.
Use simple cleaning solutions, not
aerosol sprays, solvents, or commercial cleansers. DON'T use windows sprays on a monitor screen.
Do not leave monitors on unattended for extended periods of time.

## Slide 344: Explain and apply common prevention methods
Monitors Continue...
Don't attempt to work inside the cabinet unless you are properly trained to do so.
Don't tamper with the monitor.
DON'T use windows sprays on a monitor screen.

## Slide 345: Explain and apply common prevention methods
Hard Disk Drives
Avoid rough handling.
Never move a hard disk when it is still spinning.
Never expose the internal housing to
open air.
Perform regular data backups.
Image Source: https://encrypted-tbn0.gstatic.com/images?q=tbn:ANd9GcQSR9tj7A-DQSYAk9jASl1zJ3NahmQItsoGyg&usqp=CAU

## Slide 346: Explain and apply common prevention methods
Image Source: https://en.wikipedia.org/wiki/Floppy_disk
.
Floppy Disk Drives
Do not expose the disks to magnets
Never touch the exposed surface of a floppy disk.
Do not allow smoking near a computer.

## Slide 347: Explain and apply common prevention methods
Image Source: https://www.medicalexpo.com/prod/pac-technology/product-106764-
© Edunet Foundation. All rights reserve7d9.3349.html
Keyboards and Pointing Devices
Use a hand-held vacuum cleaner to remove dust from the small crevasses.
Never use spray cleaners.
Clean a mouse or trackball by removing the ball and cleaning the x and y rollers.
When using a light pen, never touch the ends with your finger.

## Slide 348: Explain and apply common prevention methods
Image Source: https://www.forbes.com/sites/anthonykarcz/2019/08/01/the-best-printers-of-
© Edunet Foundation. All rights reserve2d0.19/#48bac15514a4
Printers
Printers are more mechanical than other peripherals and therefore require more attention.
Because they use paper, ink, or carbon, printers generate pollutants
that can build up and cause problems.
Here are a few steps for cleaning the most popular types of printers:

## Slide 349: Explain and apply common prevention methods
Image Source:https ://www.amazon.in/Epson-FX-2175II-Dot-Matrix-Printer/dp/B005VQWSEE
.
Printers
Dot-Matrix Printers
Adjust the print-head spacing.
Clean the printer's roller surfaces.
Clean the surface of the platen.
Clean the gear train of the paper- handling motor.
Apply a light coating of oil to the rails.

## Slide 350: Explain and apply common prevention methods
Printers
Ink-Jet Printers
Adjust the print-head spacing.
Check the tension on the print-head- positioning belt.
Clean the printer and its mechanism.
Clean the printer's roller surfaces.
Clean the gear train of the paper- handling motor.
Move the carriage assembly to distribute the oil.
Image Source: https://m.media-amazon.com/images/I/61-0Tco3ZgL._SL1432_.jpg
.

## Slide 351: Explain and apply common prevention methods
Printers Laser Printers
Vacuum to remove dust buildup and excess toner from the interior. Remove the toner cartridge before vacuuming.
Clean the laser printer's rollers using a damp cloth or denatured alcohol.
Clean the gear train of the paper- handling motor using a foam swab.
Apply light oil to the gears using a foam swab.
Image Source: https://m.media-amazon.com/images/I/71oZh2MUEBL._AC_SL1500_.jpg
.

## Slide 352: Explain and apply common prevention methods
Summary
The best preventive maintenance is to keep a computer clean.
Never use solvent-based cleaners on a computer
Never use liquids on the electrical
components inside a computer.
Create and implement a regular
maintenance program for each computer under your care.
Image Source: https://www.medicalexpo.com/prod/pac-technology/product-106764-

## Slide 353: Explain Service Flow Sequence (SFS) and Trouble Shooting Chart (TSC) of PC
SFS
Any problem that has anything to do with your HD can be diagnosed using
this Flowchart
Image Source: https://www.medicalexpo.com/prod/pac-technology/product-106764-

## Slide 354: Safetyprecautions in handling PC
Finding a Place to Work
The first thing you need to think about when planning your new homebuilt computer has nothing to do with parts, performance, or configuration.
You need to find a place to work.
Image Source: https://slideplayer.com/slide/3539407/

## Slide 355: Safetyprecautions in handling PC
Staking Out your Work Area
Professionals and die-hard home computer builders usually have work benches that are dedicated to nothing but computer work.
You need a sturdy table or workbench
The table should be clean and non- metallic.
Avoid places that are damp, subject to
temperature extremes, dirty, or dusty.
Image Source: https://slideplayer.com/slide/3539407/

## Slide 356: Safetyprecautions in handling PC
COMPUTER SAFETY TIPS
Backups
The most important precaution against any risk of data loss is a full, up-to-date backup.
Tape backup drives are the wisest form of insurance for your computer
Good tape drives are very inexpensive
full backups weekly and partial backups
daily is best
Image Source: https://slideplayer.com/slide/3539407/

## Slide 357: Safetyprecautions in handling PC
COMPUTER SAFETY TIPS
Telephone line danger
One potential threat to your computer which most often goes unnoticed is your modem connection.
Surges and power fluctuations can hit your
system through your phone line and cause serious damage.
Make sure your power strip or battery backup has telephone line protection.
Image Source: https://slideplayer.com/slide/3539407/

## Slide 358: Safetyprecautions in handling PC
COMPUTER SAFETY TIPS
Battery backups
A single power outage is not as damaging to your computer as the extreme surges and drops in power that occur during a blackout, brownout, or just your ordinary lightning storm.
Your computer is very sensitive to power
fluctuations - protect yourself against this.
Uninterrupted Power Supplies (UPS) are available at most any computer store or
Image Source: https://slideplayer.com/slide/3539407/
.
Office supply store.

## Slide 359: Safetyprecautions in handling PC
COMPUTER SAFETY TIPS
Turn off your computer
Monsoon season is the exception to the rule.
Whenever a storm or brownout is expected, your safest strategy is to turn off all computers and monitors.
These precautions can save you a great deal of frustration and loss.
Image Source: https://slideplayer.com/slide/3539407/

## Slide 360: sub assemblies and components
sub-assemblies and components
Subassemblies are electronic parts of the computer
that are a portion or part of a functional area.
A subassembly can contain pcbs or just electronic parts.
Two or more components combined into a
unit will form a subassembly.
Image Source: https://www.industrybuying.com/articles/5-essential-components-to-consider-. en-buying-a-pc/

## Slide 361: sub assemblies and components
sub-assemblies and components
Some of the items you will find in subassemblies of computers are as follows
Memory stacks of a memory unit.
Dc-to-dc converters in modules.
Dc switching regulators of a power supply.
Image Source: https://www.industrybuying.com/articles/5-essential-components-to-consider-. en-buying-a-pc/

## Slide 362: sub assemblies and components
sub-assemblies and components
Basic PC Components:
Motherboard
Processor
Memory (RAM)
Case/chassis
Power supply
Hard drive
Image Source:https ://www.computerhope.com/jargon/m/mothboar.htm

## Slide 363: sub assemblies and components
sub-assemblies and components
Basic PC Components:
ROM
Keyboard
Mouse
Video card
Monitor
Sound card
Image Source: https://www.amazon.in/ZAZZ-Basic-Wired-USB-Keyboard/dp/B07CNDCMPW

## Slide 364: Important points to be considered while purchasingand replacing components.
Three most important factors
The three most important factors to consider when purchasing computer hardware and software are:
Quality
Price
Service after the sale

## Slide 365: Important points to be considered while purchasingand replacing components.
Quality
You can determine quality by asking yourself the following questions:
How well does this product meet my specific needs?
Does it have the features and functions I
require?
How well is it made?
How long will it last?

## Slide 366: Important points to be considered while purchasing and replacing components.
Price
Everyone has a budget, but that doesn’t mean buying cheap is necessarily the way to go.
if you purchase a product that breaks easily or doesn’t fully meet your needs
you’ll end up needing to replace it, thereby busting your budget.

## Slide 367: Important points to be considered while purchasingand replacing components.
Service after the sale
Here are a few aspects you’d be wise to look into before purchasing:
Return policy
Warranty
Service agreement

## Slide 368: Concept of Preventive and corrective maintenance.
TYPES OF MAINTENANCE
Preventive Maintenance
Preventive Maintenance (PM)
Preventive maintenance can be defined as an equipment maintenance strategy based on replacing, or restoring, an asset at a fixed interval regardless of its condition.
Scheduled restoration tasks and replacement tasks are examples of preventive maintenance tasks.
Image Source: https://adibahnd2csa.wordpress.com/2013/05/30/154/

## Slide 369: Concept of Preventive and corrective maintenance.
TYPES OF MAINTENANCE
Preventive Maintenance
Time Based Maintenance(TBM)
Time-Based Maintenance refers to replacing or renewing an item to restore its reliability at a fixed time, interval or usage regardless of its condition.
Failure Finding Maintenance(FFM)
Failure Finding Maintenance tasks are aimed at detecting hidden failures typically associated with protective functions.
Image Source: https://www.slideshare.net/RheighHenleyCalderon/5 -pc-maintenance

## Slide 370: Concept of Preventive and corrective maintenance.
TYPES OF MAINTENANCE
Preventive Maintenance
Risk Based Maintenance(RBM)
Risk Based Maintenance (RBM) is when you use a risk assessment methodology to assign your scarce maintenance resources to those assets that carry the most risk in case of a failure (remembering that risk = likelihood x consequence).

## Slide 371: Concept of Preventive and corrective maintenance.
Image Source: https://1912milligrams.wordpress.com/2012/05/20/pc-preventive-maintenance/
.
TYPES OF MAINTENANCE
Preventive Maintenance
Condition Based Maintenance(CBM)
It may be possible to take action to prevent it from failing completely and/or to avoid the consequences of failure. Condition Based Maintenance as a strategy therefore looks for physical evidence that a failure is occurring or is about to occur.

## Slide 372: Concept of Preventive and corrective maintenance.
TYPES OF MAINTENANCE
Preventive Maintenance
Predictive Maintenance(PM)
Predictive Maintenance (PDM) this was essentially as a synonym for Condition Based Maintenance.

## Slide 373: Concept of Preventive and corrective maintenance.
TYPES OF MAINTENANCE
Corrective Maintenance
Corrective Maintenance (CM)
A Run to Failure or Corrective Maintenance strategy only restores the function of an item after it has been allowed to fail

## Slide 374: Concept of Preventive and corrective maintenance.
TYPES OF MAINTENANCE
Corrective Maintenance
Deferred Corrective Maintenance(DCM)
when a corrective maintenance work request is raised it is essential that you prioritize it properly to make sure that where possible you defer the work request and give your team the time to properly plan and schedule the work.
Emergency Maintenance(EM)

## Slide 375: Concept of Preventive and corrective maintenance.
TYPES OF MAINTENANCE
Corrective Maintenance
Emergency Maintenance(EM)
Emergency Maintenance is corrective maintenance that is so urgent that it breaks into your Frozen Weekly Schedule
Emergency Maintenance is the one and only
maintenance type that we really want to avoid as much as possible.
Image Source: https://www.synopc.com/our-services

## Slide 376: Tools required
7 Must-Have Hand Tools
Flat-Tip Screwdrivers
Philips-Head Screwdrivers
Torx Screwdrivers and Nut Drivers
Wire Cutters
Image Source: https://waneyhcsb.wordpress.com/2012/05/17/pc-tool-kits-and-their-functions/

## Slide 377: Tools required
7 Must-Have Hand Tools
Needle-Nose Pliers
Wire Strippers
Crimpers

## Slide 378: Active & Passive Maintenance
Active Maintenance
The following is a sample weekly disk-maintenance checklist:
Back up any data or important files.
Delete all temporary files.
Empty the Recycle Bin.
Check for and install antivirus software updates.
Finally, run a disk-defragmenting program.
Image Source: https://rheniumsolutions.co.ke/preventive-maintenance-2/

## Slide 379: Active & Passive Maintenance
Active Maintenance
The following are some monthly maintenance procedures you should perform:
Create an operating system startup disk.
Check for and install any BIOS updates.
Check for and install any updated drivers for the video, sound, modem, and other devices.
Check for and install any operating system
updates.
Clean the system
Check that the cooling fans are operating properly.
Image Source: https://rheniumsolutions.co.ke/preventive-maintenance-2/

## Slide 380: Active & Passive Maintenance
Passive Maintenance
Passive preventive maintenance involves taking care of the system by providing the best possible environment—both physical and electrical—for the system.
General System Care and Handling
The Operating Environment
Temperature, Humidity, and Altitude
Image Source:https ://slideplayer.com/slide/12793023/

## Slide 381: Maintenance scheduling
Maintenance scheduling
There are no universal maintenance schedules that work on every computer. Each schedule must be individualized to meet the needs of the work environment.
Do This Daily
Back up data.
Check computer ventilation to ensure that it is
clear.
Remove any paper, books, or boxes that might impede the flow of air into or out of the computer.
Image Source: https://www.slideshare.net/RheighHenleyCalderon/5-pc-maintenance

## Slide 382: Maintenance scheduling
Maintenance scheduling
Do This Weekly
Clean the outside of the case.
Clean the screen.
Run CHKDSK or ScanDisk on all hard disk
drives.
Run a current antivirus program and check all drives.
Inspect all peripheral devices.
Image Source: https://www.slideshare.net/RheighHenleyCalderon/5-pc-maintenance

## Slide 383: Maintenance scheduling
Maintenance scheduling
Do This Monthly
Clean the inside of the system.
Clean the inside of any printers.
Vacuum the keyboard.
Clean the mouse ball and x and y wheels.
Defragment all hard disk drives.
Delete any unnecessary temporary files.
Image Source: https://www.slideshare.net/RheighHenleyCalderon/5-pc-maintenance

## Slide 384: Maintenance scheduling
Maintenance scheduling
Do This Every Six Months
Perform an extensive preventive maintenance check
Apply an antistatic solution to the entire computer.
Check and reseat all cables.
Run the printer's self-test programs.
Image Source: https://www.slideshare.net/RheighHenleyCalderon/5-pc-maintenance
© Edunet Foundation. All rights reserved.

## Slide 385: Maintenance scheduling
Maintenance scheduling
Do This Annually
Reformat the hard disk drive and reinstall all software. Don't forget to back up data first
Check all floppy disk drives.
Consider an upgrade to your computer. Check to see that your components can handle your workload.
Image Source: https://www.slideshare.net/RheighHenleyCalderon/5-pc-maintenance
© Edunet Foundation. All rights reserved.

## Slide 386: Maintenance scheduling
Maintenance scheduling
Summary
The best maintenance practice is to keep a
computer clean.
Never use solvent-based cleaners on a computer.
Never use liquids on the electrical components
inside a computer.
Create and implement a regular maintenance program for each computer under your care.
Image Source: https://www.slideshare.net/RheighHenleyCalderon/5-pc-maintenance
© Edunet Foundation. All rights reserved.

## Slide 387: Need of diagnostics program Features, limitations. Examples of commonly used diagnostic programs.
Need of diagnostics program
Computer diagnostics tools are pieces of software that give you the knowledge you need to be able to potentially repair your own computer.
Some of these tools come built in to your operating system while others come from 3rd party software developers.
Image Source:https ://www.syvir.com/pc_diagnostic.aspx

## Slide 388: Need of diagnostics program Features, limitations. Examples of commonly used diagnostic programs.
Need of diagnostics program
The best diagnostic tools to detect the problem in your Windows PC and fix it right away.
Process Explorer
Image Source:https://thegeekpage.com/hardware-diagnostic-tools/
© Edunet Foundation. All rights reserved.

## Slide 389: Need of diagnostics program Features, limitations. Examples of commonly used diagnostic programs.
Need of diagnostics program
Windows Sysinternal Suite
Image Source:https://thegeekpage.com/hardware-diagnostic-tools/
© Edunet Foundation. All rights reserved.

## Slide 390: Need of diagnostics program Features, limitations. Examples of commonly used diagnostic programs.
Need of diagnostics program
Wifi Analyzer
Image Source:https://thegeekpage.com/hardware-diagnostic-tools/
© Edunet Foundation. All rights reserved.

## Slide 391: Need of diagnostics program Features, limitations. Examples of commonly used diagnostic programs.
Need of diagnostics program
Performance Monitor
Image Source:https://thegeekpage.com/hardware-diagnostic-tools/

## Slide 392: Need of diagnostics program Features, limitations. Examples of commonly used diagnostic programs.
Need of diagnostics program
Reliability Monitor
Image Source:https://thegeekpage.com/hardware-diagnostic-tools/
.

## Slide 393: Need of diagnostics program Features, limitations. Examples of commonly used diagnostic programs.
Need of diagnostics program
Resource Monitor
Image Source:https://thegeekpage.com/hardware-diagnostic-tools/
.

## Slide 394: Need of diagnostics program Features, limitations. Examples of commonly used diagnostic programs.
Need of diagnostics program
ESET SysInpector
Image Source:https://thegeekpage.com/hardware-diagnostic-tools/

## Slide 395: Need of diagnostics program Features, limitations. Examples of commonly used diagnostic programs.
Need of diagnostics program
CPU-Z
Image Source:https://thegeekpage.com/hardware-diagnostic-tools/
.

## Slide 396: Need of diagnostics program Features, limitations. Examples of commonly used diagnostic programs.
Need of diagnostics program
System Explorer
Image Source:https://thegeekpage.com/hardware-diagnostic-tools/
.

## Slide 397: Types of monitor, Monochrome and color
What is a Monitor ?
A monitor is an electronic output device that is also known as a video display terminal (VDT) or a video display unit (VDU).

## Slide 398: Types of monitor, Monochrome and color
Types of Monitor
Cathode Ray Tube (CRT) Monitors
Flat Panel Monitors
  Liquid Crystal Display: LCD
  Gas Plasma Display
  Touch Screen Monitors
  LED Monitors
  OLED Monitors
Image Source:https://static.javatpoint.com/computer/images/types-of-monitors1.png
.

## Slide 399: Types of monitor, Monochrome and color
Types of Monitor(Cond.)
Flat Panel Monitors
  DLP Monitors
  TFT Monitor
  Plasma Screen Monitor
Image Source: https://static.javatpoint.com/computer/images/types-of-monitors2.png
.

## Slide 400: Types of monitor, Monochrome and color
Monochrome Monitor
Also known as monochromatic monitors
Used extensively during the middle to latter part of the 20th century
Monochrome monitor is somewhat like
that of a black and white television set

## Slide 401: Types of monitor, Monochrome and color
CRT Monitor
CRT Monitor display by using a combination of phosphors
The phosphors are different colors
  Beam Penetration Method
  Shadow-Mask Method

## Slide 402: Types of monitor, Monochrome and color
Beam Penetration Method
It used with random-scan monitors
CRT screen is coated with two layers of phosphor
This method produces four colors only, red, green, orange and yellow

## Slide 403: Types of monitor, Monochrome and color
Shadow-Mask Method
It is commonly used in the Raster-Scan System
It is used in the majority of color TV sets and monitors
Shadow mask grid is pierced with small
round holes in a triangular pattern.

## Slide 404: CGA, EGA, VGA, SVGA, Digital Analogue
CGA (Color Graphics Adapter)
The CGA standard, introduced in 1981
CGA card came video memory different modes
  Text mode
  Color Mode
  Monochrome Graphics Mode

## Slide 405: CGA, EGA, VGA, SVGA, Digital Analogue
EGA(Enhanced Graphics Adapter)
Enhanced Graphics Adapter was
introduced by IBM in 1984
EGA increased resolution to 640×350 pixels in 16 colors
256KB of video memory to allow full
implementation of all EGA modes
  High-resolution mode
  CGA mode
  MDA mode

## Slide 406: CGA, EGA, VGA, SVGA, Digital Analogue
VGA(Video Graphics Array)
VGA graphics started to come on the motherboard as a single chip
VGA’s 640×480 remains a sort of
lowest common denominator for all graphics cards
The VGA specification dictated 256KB of video RAM, 16- and 256-color modes

## Slide 407: CGA, EGA, VGA, SVGA, Digital Analogue
SVGA(Super Video Graphics Array)
Super VGA was first defined in 1989
It was invented by the Video Electronics Standards Association (VESA)
SVGA evolved to 1024×768 with 256 colors and even higher resolutions and colors as time went on

## Slide 408: Main components & connectors on Display
Components of Graphics Card
GPU or Graphics Processing Unit is the main component and heart of the graphics card
It is also known as Graphics Processor and does all the processing in your graphics card

## Slide 409: Main components & connectors on Display
Components of Graphics Card
VRAM
VRM(Voltage Regulator Module)
Cooler
PCB
PCI Express x16 connector
  8 Pin
  6 Pin
SLI / Cross Fire Slot

## Slide 410: LCD and CRT Monitors
CRT Monitors
It is an evacuated glass
An electron gun at the rear of the tube produce a beam of electrons
Inner side screen is coated with phosphor substance which gives light when it is stroked
The control grid voltage determines how many electrons are actually in the electron beam.

## Slide 411: LCD and CRT Monitors
CRT Monitors
The voltage applied to vertical and horizontal deflection plates is control vertical and horizontal deflection, respectively.
There are two techniques used for producing images on the CRT screen:
Vector scan/Random scan
Raster scan display

## Slide 412: LCD and CRT Monitors
LCD Monitors
The American inventor J. Fergason created the first working liquid crystal display in 1970.
Even though liquid crystals were discovered a long time ago, at first, they were applied for different purposes. Molecules of liquid crystals under the influence of electricity

## Slide 413: LCD and CRT Monitors
LCD Monitors
LCD screens are an array of small segments called pixels, which can be manipulated for information displaying.
Such displays have several layers, where two panels, made of glass material free of sodium and called substrate.
The liquid crystal panel is illuminated by a light source

## Slide 414: LCD and CRT Monitors
LCD Monitors
When an electric field appears, the molecules are partially aligned along it
By producing screens using LCD monitor technology, the backlight of the monitor is used to output a color image so that light is generated at the back of the LCD monitors.
By combining the three primary colors for each pixel of the screen, you can reproduce any color

## Slide 415: CRT vs LCD display systems

## Slide 416: Displays memory quality and performance
VRAM
VRAM (video RAM) is a reference to any type of random access memory (RAM) used to store image data for a computer display.
All types of VRAM are special arrangements of dynamic RAM (DRAM)

## Slide 417: Displays memory quality and performance
Types of VRAM
Multibank Dynamic RAM (MDRAM)
Rambus Dynamic RAM (RDRAM)
Synchronous Graphics RAM (SGRAM)
Window RAM (WRAM)

## Slide 418
Disclaimer: The content is curated for educational purposes only.
© Edunet Foundation. All rights reserved.
Able to perform basic troubleshoot of PC
(3 hours)

## Slide 419
In this section, we will discuss:
© Edunet Foundation. All rights reserved.
Proper troubleshooting Techniques for motherboards, I/O Devices.

## Slide 420: Proper troubleshooting Techniques for motherboards, I/O Devices
Image Source: https://www.fieldengineer.com/skills/pc-support-technician-devices-db57ecc1262d
How to Diagnose Motherboard or Processor
Problems?
The motherboard and processor are two of the most important hardware components inside the computer.
The various pieces of hardware inside the PC
communicate with one another through the circuits on the motherboard, while the CPU stores and executes programming instructions.
The motherboard and CPU can both be expensive to replace, however, but diagnosing
hardware failure on your own can reduce the potential repair costs for your business.
© Edunet Foundation. All rights reserved.

## Slide 421: Proper troubleshooting Techniques for motherboards, I/O Devices
How to Diagnose Motherboard or Processor
Problems?
Turn Off the Computer
Touch a Bare Metal Surface
Turn on the Computer
Navigate to Motherboard Manufacturer's Website
Uninstall Hardware
Loosen the HeatSink and Processor Fan
Touch the Processor
Lift Out the CPU
Lock the CPU in Place
Image Source: https://www.pearsonitcertification.com/articles/article.aspx?p=2731934&seqNum=28
© Edunet Foundation. All rights reserved.

## Slide 422: Proper troubleshooting Techniques for motherboards, I/O Devices
How to Diagnose Motherboard or Processor
Problems?
Reconnect the Power
Check for Damage on Motherboard
Remove the CLRTC Jumper
Reconnect the Keyboard
Load Fail-Safe Defaults
Restart the Computer
Image Source: https://www.pearsonitcertification.com/articles/article.aspx?p=2731934&seqNum=28
© Edunet Foundation. All rights reserved.

## Slide 423: Proper troubleshooting Techniques for motherboards, I/O Devices
Motherboard Troubleshooting
Check the power supply to see if the fan is turning. If the CPU or motherboard has a fan, see if it is turning. Check voltages going from the power supply to the motherboard.
Check the BIOS/UEFI settings for accuracy
Check for overheating. Power down the computer and allow the computer to cool. Power on the computer with the cover off.
Check the motherboard for distended
capacitors. These are small components that
might appear to be bulging. If sighted, replace the motherboard as soon as possible.
Image Source: https://www.easypcmod.com/know-motherboard-bad-fix-troubleshooting-guide-282
© Edunet Foundation. All rights reserved.

## Slide 424: Proper troubleshooting Techniques for motherboards, I/O Devices
Motherboard Troubleshooting
Reseat the CPU, adapters, and memory chips.
Remove unnecessary adapters and devices and boot the computer.
Plug the computer into a different power outlet
and circuit, if possible.
Check to determine whether the motherboard is
shorting out on the frame.
Check the CMOS battery
With a motherboard that has diagnostic LEDs, check the output for any error code.
Image Source: https://www.easypcmod.com/know-motherboard-bad-fix-troubleshooting-guide-282
© Edunet Foundation. All rights reserved.

## Slide 425: Proper troubleshooting Techniques for motherboards, I/O Devices
Troubleshooting I/O Devices
Solution 1: Make certain that all cables are
connected correctly
Solution 2: Start the computer in a clean boot state
Solution 3: Change the transfer mode for the
drive in IDE Channel Properties
Solution 4: Check the status of the device in Device Manager
Solution 5: Contact the hardware manufacturer
Image Source: https://slideplayer.com/slide/253942/
© Edunet Foundation. All rights reserved.

## Slide 426: Understand basic computer network technology
Disclaimer: The content is curated for educational purposes only.
© Edunet Foundation. All rights reserved.

## Slide 427: In this section, we will discuss:
© Edunet Foundation. All rights reserved.
Introduction to networks
Type of area networks - LAN, VLAN, CAN, MAN, WAN
Internet and Intranet etc.
Uses and benefits of Network
Server-client based network,
peer to peer networks
Network Interface Card
Transmission Media and Topologies Media Type
Crimping tools and Color standards for Straight crimping and Crosscrimping

## Slide 428: Introduction to Networks
© Edunet Foundation. All rights reserved.
What is a Computer Network?
A computer network is a set of computers connected together for the purpose of sharing resources.
The term network originated during the mid of the 1960s in the Department of Defense in the United States.
A network is a collection of computers, servers, mainframes, network devices, peripherals, or other devices connected to one another to allow the sharing of
data.
ImageSource: https://www.tutorialspoint.com/computer_fundamentals/computer_networking.htm

## Slide 429: Introduction to Networks
Characteristics of a Computer Network
Share resources from one computer to another.
Create files and store them in one computer, access those files from the other computer(s) connected over the network.
ImageSource: https://www.tutorialspoint.com/computer_fundamentals/computer_networking.htm
© Edunet Foundation. All rights reserved.

## Slide 430: Introduction to Networks
Characteristics of a Computer Network(continued)
Connect a printer, scanner, or a fax machine to one computer within the network and let other computers of the network use the machines available over the network.
ImageSource: https://www.tutorialspoint.com/computer_fundamentals/computer_networking.htm
© Edunet Foundation. All rights reserved.

## Slide 431: Introduction to Networks
Characteristics of a Computer Network(continued)
Devices required for computer Networking:
Network Cables
Distributors
Routers
Internal Network Cards
External Network Cards
ImageSource: https://tyrocity.com/topic/computer-networks/
© Edunet Foundation. All rights reserved.

## Slide 432: Introduction to Networks
Basics Components Of Computer Network
Servers
Clients
Transmission Media
Network Interface card
Modem
Hub
Switch
Cables and connectors
Router
LAN cable
ImageSource: https://beginnersbook.com/2019/03/computer-network-components/
© Edunet Foundation. All rights reserved.

## Slide 433: Introduction to Networks
Features of a Computer Network
Performance
Data Sharing
Backup
Software and hardware compatibility
Reliability
Security
Scalability
ImageSource: https://beginnersbook.com/2019/03/computer-network-features/
© Edunet Foundation. All rights reserved.

## Slide 434: Introduction to Networks
Advantages of Computer Networks
Workgroups
Shared databases
Distributed Systems
Communications
Device Sharing
Software sharing
Security
© Edunet Foundation. All rights reserved.
Ref: https://d8it4huxumps7.cloudfront.net/bites/wp-content/banners/2021/9/6139a6825ca07_advantages_and_disadvantages_of_computer_network.png?d=700x400
.

## Slide 435: Introduction to Networks
Disadvantages of Computer Networks
Buying the computer cable and servers can be very expensive.
Viruses can spread to other computers throughout a computer network.
People can hack your computer.
It encourages people to become dependent on computers.
It comes with the risk of security issues.
ImageSource:https://www.pixuffle.net/disadvantages-of-computer-network/
© Edunet Foundation. All rights reserved.

## Slide 436: Area Networks
Type of Area Networks
LAN
MAN
WAN
VLAN
WLAN
VPN
CAN
SAN
SHAN
PAN
ImageSource:https://www.quora.com/What-are-the-different-types-of-networking
© Edunet Foundation. All rights reserved.

## Slide 437: Type of Area Networks
LAN(Local Area Network)
Group of interconnected computers within a small area. (room, building, campus)
Two or more pc's can from a LAN to share files, folders, printers, applications and other devices
Coaxial or CAT 5 cables are normally used for connections.
ImageSource:https://www.javatpoint.com/types-of-computer-network
© Edunet Foundation. All rights reserved.

## Slide 438: Type of Area Networks
LAN(Local Area Network)(continued)
Due to short distances, errors and noise are minimum.
Local Area Network provides higher security.
Data transfer rate is 10 to 100 mbps.
Example: A computer lab in a school
ImageSource:https://www.networkstraining.com/different-types-of-networks/
© Edunet Foundation. All rights reserved.

## Slide 439: Type of Area Networks
MAN(Metropolitan Area Network)
Design to extend over a large area.
Connecting number of LAN's to form larger network, so that resources can be shared.
Government agencies use MAN to connect to the citizens and private industries
ImageSource:https://www.networkstraining.com/different-types-of-networks/
© Edunet Foundation. All rights reserved.

## Slide 440: Type of Area Networks
MAN(Metropolitan Area Network)(continued)
In MAN, various LANs are connected to each other through a telephone exchange line.
Networks can be up to 5 to 50 km.
Data transfer rate is low compared to LAN.
Example: Organization with different branches located in the city.
ImageSource:https://www.javatpoint.com/types-of-computer-network
© Edunet Foundation. All rights reserved.

## Slide 441: Type of Area Networks
WAN(Wide Area Network)
A Wide Area Network is a network that extends over a large geographical area such as states or countries.
Contains multiple LAN's and MAN's.
A Wide Area Network is quite bigger network than the LAN.
ImageSource:https://www.javatpoint.com/types-of-computer-network
© Edunet Foundation. All rights reserved.

## Slide 442: Type of Area Networks
WAN(Wide Area Network)(continued)
Distinguished in terms of geographical range.
Data transfer rate depends upon the ISP provider and varies over the location.
Example:Internet
ImageSource:https://www.networkstraining.com/different-types-of-networks/
© Edunet Foundation. All rights reserved.

## Slide 443: Type of Area Networks
WLAN(Wireless Local Area Network)
A WLAN makes use of a Wireless Access Point (WAP) device, which serves as the point of connectivity for wireless clients on the network.
A LAN that uses high frequency radio waves for communication.
Provides short range connectivity with high speed data transmission
ImageSource:https://www.networkstraining.com/different-types-of-networks/
© Edunet Foundation. All rights reserved.

## Slide 444: Type of Area Networks
VLAN(Virtual Local Area Network)
Virtual Local Area Networks (VLANs) divide a single existing physical network into multiple logical networks.
Thereby, each VLAN forms its own broadcast domain.
ImageSource:https://www.geeksforgeeks.org/virtual-lan-vlan/
© Edunet Foundation. All rights reserved.

## Slide 445: Type of Area Networks
VLAN(Virtual Local Area Network)(continued)
Communication between two different VLANs is only possible through a router that has been connected to both VLANs.
VLANs behave as if they had been constructed using switches that are independent of each other.
ImageSource: http://www.codesandtutorials.com/networking/basics/computer_network-types.php
© Edunet Foundation. All rights reserved.

## Slide 446: Type of Area Networks
VPN(Virtual Private Network)
A Virtual Private Network is a type of network that makes use of existing private or public network infrastructure (e.g the Internet) to provide a secure network connection.
This is often achieved by creating an encrypted tunnel for secured end-to-end connectivity.
ImageSource:https://www.networkstraining.com/different-types-of-networks/
© Edunet Foundation. All rights reserved.

## Slide 447: Type of Area Networks
VPN(Virtual Private Network)(continued)
A Virtual Private Network uses data encryption techniques to provide security for files that are sent or received over the network.
This is often used by organizations that have highly sensitive data to transfer.
ImageSource: https://en.wikipedia.org/wiki/Virtual_private_network
© Edunet Foundation. All rights reserved.

## Slide 448: Type of Area Networks
CAN(Campus Area Network)
A campus area network (CAN) is a network of multiple interconnected local area networks (LAN) in a limited geographical area.
CAN is smaller than WAN (Wide Area Network)
CAN is also known as a controller area network.
Example:Network in university
ImageSource:https://www.networkstraining.com/different-types-of-networks/
© Edunet Foundation. All rights reserved.

## Slide 449: Type of Area Networks
SAN(Storage Area Network)
A Storage Area Network (SAN) is a specialized, high-speed network that provides block-level network access to storage.
Connects servers to data storage devices via fiber-optic cables.
ImageSource: http://www.codesandtutorials.com/networking/basics/computer_network-types.php
© Edunet Foundation. All rights reserved.

## Slide 450: Type of Area Networks
SAN(Storage Area Network)(continued)
SANs are typically composed of hosts, switches, storage elements, and storage devices that are interconnected using a variety of technologies, topologies, and protocols.
Example: Used for daily backup of organization or a mirror copy
ImageSource:https://www.networkstraining.com/different-types-of-networks/
© Edunet Foundation. All rights reserved.

## Slide 451: Type of Area Networks
© Edunet Foundation. All rights reserved.
SHAN(Smart Home Area Network)
A home area network (HAN) is a network contained within a user's home that connects a person's digital devices, from multiple computers and their peripheral devices to telephones, VCRs, televisions, video games, home security systems, smart appliances, fax machines and other digital devices that are wired into the network.
The SHAN network generally used in
homes and office space.
ImageSource: https://networkencyclopedia.com/home-area-network-han/

## Slide 452: Type of Area Networks
PAN(Personal Area Network)
Personal Area Network is a network arranged within an individual person, typically within a range of 10 meters.
Personal Area Network is used for connecting the computer devices of personal use is known as Personal Area Network.
ImageSource: https://www.networkstraining.com/different-types-of-networks/
© Edunet Foundation. All rights reserved.

## Slide 453: Type of Area Networks
PAN(Personal Area Network)(continued)
Personal computer devices that are used to develop the personal area network are the laptop, mobile phones, media player and play stations.
Personal Area Network covers an area of 30 feet.
ImageSource: https://www.javatpoint.com/types-of-computer-network
© Edunet Foundation. All rights reserved.

## Slide 454: Internet and Intranet etc
Internet
The Internet consists of a network of computers that anyone can access.
Many intranets together make up the internet.
It is a public network therefore anyone can access the internet.
There is no limit to the number of users who can use the internet at any given time
ImageSource:
© Edunet Foundation. Ahtltlprsi:g//hstpsecretrsumer.vieeede..org/tech-talk/aerospace/satellites/facebook-may-have-secret-plans-to-launch-a-intern

## Slide 455: Internet and Intranet etc
Internet(continued)
There is no limit to the number of users who can use the internet at any given time
ImageSource: https://alphatronicsinitsolutions.com/internet-solutions/
© Edunet Foundation. All rights reserved.

## Slide 456: Internet and Intranet etc
Intranet(continued)
An intranet is a smaller network of computers that allows access to a particular group of users.
One can access the intranet from the internet. However, there are restrictions on the number of users.
Only a specific few users can access the intranet.
ImageSource: https://www.javatpoint.com/intranet
© Edunet Foundation. All rights reserved.

## Slide 457: Internet and Intranet etc
Intranet(continued)
There are limitations on the volume of traffic at any given time.
It is a private network therefore anyone can’t access intranet.
Intranet contains a specific kind of information only.
ImageSource: https://www.shutterstock.com/search/intranet
© Edunet Foundation. All rights reserved.

## Slide 458: Internet and Intranet etc
Difference between Internet and Intranet
The Internet
is a wide
computers whereas
that is available to Intranet is a network
network of
all of
computers designed for a certain group of users.
Internet is a public network and Intranet is a private network.
Number of internet users are very high but the number of users of Intranet is limited.
ImageSource: https://techdifferences.com/difference-between-internet-and-intranet.html
© Edunet Foundation. All rights reserved.

## Slide 459: Internet and Intranet etc
Difference between Internet and Intranet(continued)
Internet contains various source of information while Intranet only contains group-specific information.
Anyone can access the internet while Intranet is accessible only by the organization employees or admin who have login details.
ImageSource: https://www.ictlounge.com/html/internet_intranet.htm
© Edunet Foundation. All rights reserved.

## Slide 460: Internet and Intranet etc
Extranet
An extranet is a communication network based on the internet protocol such as Transmission Control protocol and internet protocol.
It is used for information sharing.
The access to the extranet is restricted to only those users who have login credentials.
ImageSource: https://www.quora.com/What-is-the-difference-between-the-internet-intranet-and-extranet
© Edunet Foundation. All rights reserved.

## Slide 461: Internet and Intranet etc
Extranet(continued)
An extranet is the lowest level of internetworking.
An extranet cannot have a single LAN, atleast it must have one connection to the external network.
ImageSource: ttps://www.quora.com/What-is-the-difference-between-the-internet-intranet-and-extranet
© Edunet Foundation. All rights reserved.

## Slide 462: Uses and benefits of Network
Increased speed and reduced cost
File Sharing from one system to another.
Remote access
Hardware sharing like a printer, scanner, storage
ImageSource: https://ouritpro.net/2016/11/07/the-importance-of-computer-networks/
© Edunet Foundation. All rights reserved.

## Slide 463: Uses and benefits of Network
Communication i.e. instant messaging, video calls, mail communication etc.
Online business
Ease of administration
Information security
ImageSource: https://www.ccsipro.com/blog/uses-of-computer-network/
© Edunet Foundation. All rights reserved.

## Slide 464: Server-client based Network
A Computer networking model where one or more powerful computers (servers) provide the different computer network services and all other user of computer network (clients) access those services to perform user's tasks is known as client/server computer networking model.
ImageSource: https://www.educative.io/edpresso/what-are-p2p-and-clientserver-networks
© Edunet Foundation. All rights reserved.

## Slide 465: Server-client based Network
In such networks, there exists a central controller called server. A server is a specialized computer that controls the network resources and provides services to other computers in the network.
All other computers in the network are called clients.
A client computer receives the requested services from a server.
ImageSource:http://ecomputernotes.com/computernetworkingnotes/computer-network/explain-clientserver-
© Edunet Foundation. Anelltwriogrhktinsgr-emsoedrevled.

## Slide 466: Server-client based Network
A server performs all the major operations like security and network management.
All the clients communicate with each other via centralized server
If client 1 wants to send data to client 2, it first sends request to server to seek permission for it. The server then sends a signal to client 1 allowing it to initiate the communication.
ImageSource: https://www.educative.io/edpresso/what-are-p2p-and-clientserver-networks
© Edunet Foundation. All rights reserved.

## Slide 467: Server-client based Network
A server is also responsible for managing all the network resources such as files, directories, applications & shared devices like printer etc.
If any of the clients wants to access these services, it first seeks permission from the server by sending a request.
ImageSource: https://en.wikipedia.org/wiki/Client%E2%80%93server_model
© Edunet Foundation. All rights reserved.

## Slide 468: Server-client based Network
Advantages of Client Server Networks
Centralized backup is possible.
Use of dedicated server improves the performance of whole system.
Security is better in these networks as all the shared resources are centrally administered.
Use of dedicated servers also increases the speed of sharing resources.
ImageSource: https://sites.google.com/site/clientserverarchitecture/advantages-of-client-server-architecture
© Edunet Foundation. All rights reserved.

## Slide 469: Server-client based Network
Disadvantages of Client Server Networks
It requires specialized servers with large memory and secondary storage. This leads to increase in the cost.
The cost of network operating system that manages the various clients is also high.
It requires dedicated network administrator.
ImageSource: https://sites.google.com/site/clientserverarchitecture/advantages-of-client-server-architecture
© Edunet Foundation. All rights reserved.

## Slide 470: Peer to peer Networks
© Edunet Foundation. All rights reserved.
In the peer to peer computer network model we simply use the same
Workgroup for all the computers and a unique name for each computer in a computer network.
There is no master or controller or central server in this computer network and computers join hands to share files, printers and Internet access.
Peer to peer relationship is suitable for small networks having less than 10
computers on a single LAN.
ImageSource:https://www.educative.io/edpresso/what-are-p2p-and-clientserver-networks

## Slide 471: Peer to peer Networks
© Edunet Foundation. All rights reserved.
It is practical for workgroups of a dozen or less computers making it common environments, where each PC acts as an independent workstation and maintaining its own security that stores data on its own disk but which can share it with all other PCs on the network.
Software for peer-to-peer network is included with most modern desktop operating systems such as Windows
and Mac OS.
ImageSource: https://www.educative.io/edpresso/what-are-p2p-and-clientserver-networks

## Slide 472: Peer to peer Networks
Advantages of Peer to Peer Networks
Such networks are easy to set up and maintain as each computer manages itself.
It eliminates extra cost required in setting up the server.
Since each device is master of its own, they an: not dependent on other computers for their operations.
ImageSource: http://mdalikhoja.blogspot.com/2006/04/advantages-of-peer-to-peer-networks.html
© Edunet Foundation. All rights reserved.

## Slide 473: Peer to peer Networks
Disadvantages of Peer to Peer Networks
In peer-to-peer network, the absence of centralized server make it difficult to backup data as data is located on different workstations.
Security is weak as each system manages itself only.
There is no central point of data storage for file archiving.
ImageSource:
© Edunet Foundation. Ahtltlprsi:g//hettserrneaslseurnvsehdin.eoftheismind.wordpress.com/2013/02/18/advantages-and-disadvantages-of-p2p/

## Slide 474: Peer to peer Networks
Difference between Client-server and Peer to Peer Networks
Both peer-to-peer and client-server networks connect computers so that they can share resources from one computer to others such as files, videos, and pictures.
ImageSource: http://it-asean.blogspot.com/2014/10/understanding-differences-between.html
© Edunet Foundation. All rights reserved.

## Slide 475: Network Interface Card
What is a Network Interface Card?
A network interface card (NIC) is a hardware component without which a computer cannot be connected over a network.
It is also called Ethernet Card,interface controller,Lan Adapter or Network Adapter.
ImageSource:
© Edunet Foundation. Ahtltlprsi:g//hwtwswre.ttsteecrhv.ecdo.m/products/aerospace-space/development-test-vv/development-end-systems/tte-netw

## Slide 476: Network Interface Card
What is a Network Interface Card?(continued)
It is a
circuit board
installed in a
computer that provides a dedicated network connection to the computer.
Every NIC has a 48-bit unique serial number called a MAC address which is stored in ROM carried on the card.
NIC allows both wired and wireless communications
ImageSource:https://techterms.com/definition/nic
© Edunet Foundation. All rights reserved.

## Slide 477: Network Interface Card
Components of NIC
An external Memory is used to store the data temporarily and uses the stored data whenever required while processing the communication.
Connectors are used to make the physical link between cables and plugin with the board, this type of connection is especially seen in Ethernet type of NIC cables.
ImageSource:https://medium.com/computing-technology-with-it-fundamentals/expansion-cards-and-their-sl
© Edunet Foundation. Aotlsl-roign-hmtsotrheesrbeorvaerdd-9. afb07aaeae1

## Slide 478: Network Interface Card
Components of NIC(continued)
A Processor converts the data message into a signal format for communication to take place easily.
Different types of standard Buses are plugged into Buses Connector slots, based on the compatibility of the operation process buses are chosen.
ImageSource: https://sites.google.com/site/ktsnetworktechnology/home/basic-part-of-a-network
© Edunet Foundation. All rights reserved.

## Slide 479: Network Interface Card
Components of NIC(continued)
Jumpers or Dual in package switches are used to control the communication operation, which is either by turning on or turning off the switch.
A router is an NIC device that is used to connect wirelessly to the internet.
ImageSource: https://www.youtube.com/watch?v=SfEXvbQbi0E
© Edunet Foundation. All rights reserved.

## Slide 480: Network Interface Card
Components of NIC(continued)
MAC address which is a unique identity address is given to network interface card where ethernet packets are communicated with the computer.
MAC address is also known as a physical network address.
ImageSource:https://www.elprocus.com/network-interface-card-nic/
© Edunet Foundation. All rights reserved.

## Slide 481: Network Interface Card
Types of NIC Cards
Wired
Wireless
USB
ImageSource: https://www.javatpoint.com/computer-network-components
© Edunet Foundation. All rights reserved.

## Slide 482: Network Interface Card
Types of NIC Cards(continued)
Wired
These NIC have input jacks made of cables(Ethernet Cable).
The motherboard has a slot for the network cards where they are inserted.
The most widely used LAN technology is Ethernet.
ImageSource:https://www.tutorialspoint.com/what-is-network-interface-card-nic
© Edunet Foundation. All rights reserved.

## Slide 483: Network Interface Card
Types of NIC Cards(continued)
Wired
Ethernet-based NIC is available in hardware shops.
The speed of Ethernet-based NIC can be 10/100/1000 Mbps.
ImageSource:https://www.tutorialspoint.com/what-is-network-interface-card-nic
© Edunet Foundation. All rights reserved.

## Slide 484: Network Interface Card
Types of NIC Cards(continued)
Wireless
Wireless network cards are inserted into the motherboard but no network cables are required to connect the computer to
designed for Wi-Fi
the internet.
These NICs are connections.
ImageSource: https://afteracademy.com/blog/what-is-a-network-interface-card
© Edunet Foundation. All rights reserved.

## Slide 485: Network Interface Card
Types of NIC Cards(continued)
USB
These are NICs that provide network connection over the device plugged in the
USB port.
ImageSource: https://afteracademy.com/blog/what-is-a-network-interface-card
© Edunet Foundation. All rights reserved.

## Slide 486: Network Interface Card
Advantages of NIC
The communication speed using the Internet is high usually in Gigabytes
Highly reliable connection
Many peripheral devices can be connected using many ports of NIC cards.
Bulk data can be shared among many users.
ImageSource: https://study.com/academy/lesson/network-interface-card-nic-types-function-definition.html
© Edunet Foundation. All rights reserved.

## Slide 487: Network Interface Card
Disadvantages of NIC
Inconvenient in case of wired cable NIC, as it is not portable like a wireless router
The configuration should be proper for better communication.
Data is unsecured.
ImageSource:https://www.omnisecu.com/basic-networking/what-is-nic-card-network-interface-card.php
© Edunet Foundation. All rights reserved.

## Slide 488: Transmission Media and Topologies Media Type
What is Transmission Media?
A communication channel that is used to carry the data from the transmitter to the receiver through the electromagnetic signals.
The main function of this is to carry the data in the bits form through the Local Area Network (LAN). In data communication, it works like a physical path between the sender & the receiver.
ImageSource: http://alissazainal.blogspot.com/2018/01/table_11.html
© Edunet Foundation. All rights reserved.

## Slide 489: Transmission Media and Topologies Media Type
Types of Transmission Media
Physical transmission media/Guided media/Wired
Wireless transmission media/Unguided media/Wireless
.
ImageSource: https://mangoguys.wordpress.com/2013/12/03/wireless-transmission-media/
© Edunet Foundation. All rights reserved.

## Slide 490: Crimping tools and Color standards for Straight crimping and Crosscrimping
Crimping Tools
A crimping tool is a device used to conjoin two pieces of metal by deforming one or both of them in a way that causes them to hold each other. The result of the tool's work is called a crimp.
ImageSource:https://www.computerhope.com/jargon/c/crimp.htm
© Edunet Foundation. All rights reserved.
.

## Slide 491: Crimping tools and Color standards for Straight crimping and Crosscrimping
Crimping Tools(continued)
For instance, network cables and phone cables are created using a crimping tool (shown below) to join the RJ-45 and RJ-11 connectors to both ends of either phone or Cat 5 cable.
ImageSource: https://mangoguys.wordpress.com/2013/12/03/wireless-transmission-media/
© Edunet Foundation. All rights reserved.
.

## Slide 492: Crimping tools and Color standards for Straight crimping and Crosscrimping
Ethernet Cable Color
A straight-thru is used as a patch cord in Ethernet connections.
A crossover is used to connect two Ethernet devices without a hub or for connecting two hubs.
A crossover has one end with the Orange set of wires switched with the Green set.
ImageSource: https://incentre.net/ethernet-cable-color-coding-diagram/
© Edunet Foundation. All rights reserved.

## Slide 493: Crimping tools and Color standards for Straight crimping and Crosscrimping T-568A Straight-Through Ethernet Cable
The TIA/EIA 568-A standard which was ratified in 1995, was replaced by the TIA/EIA 568-B standard in 2002 and has been updated since.
Both standards define the T-568A and T-568B pin-outs for using Unshielded Twisted Pair cable and RJ-45 connectors for Ethernet connectivity.
ImageSource: https://incentre.net/ethernet-cable-color-coding-diagram/
© Edunet Foundation. All rights reserved.

## Slide 494: Crimping tools and Color standards for Straight crimping and Crosscrimping T-568A Straight-Through Ethernet Cable(continued)
The standards and pinout specification appear to be related and interchangeable, but are not the same and should not be used interchangeably.
ImageSource: https://www.networkkings.org/color-coding-of-straight-and-crossover-cable/
.
© Edunet Foundation. All rights reserved.

## Slide 495: Crimping tools and Color standards for Straight crimping and Crosscrimping T-568B Straight-Through Ethernet Cable
Both the T-568A and the T-568B standard Straight-Through cables are used most often as patch cords for your Ethernet connections.
ImageSource:https://incentre.net/ethernet-cable-color-coding-diagram/
.
© Edunet Foundation. All rights reserved.

## Slide 496: Crimping tools and Color standards for Straight crimping and Crosscrimping T-568B Straight-Through Ethernet Cable(continued)
If user require a cable to connect two Ethernet devices directly together without a hub or when you connect two hubs together, you will need to use a Crossover cable alternative.
ImageSource:https://www.make-it.ca/technical-notes/how-to-crimp-rj45-connector/
© Edunet Foundation. All rights reserved.
.

## Slide 497: Crimping tools and Color standards for Straight crimping and Crosscrimping
RJ-45 Crossover Ethernet Cable
A good way of remembering how to wire a Crossover Ethernet cable is to wire one end using the T-568A standard and the other end using the T-568B standard.
ImageSource: https://www.networkkings.org/color-coding-of-straight-and-crossover-cable/
© Edunet Foundation. All rights reserved.

## Slide 498: Crimping tools and Color standards for Straight crimping and Crosscrimping
RJ-45 Crossover Ethernet Cable
Another way of remembering the color coding is to simply switch the Green set of wires in place with the Orange set of wires.
Specifically, switch the solid Green (G) with the solid Orange, and switch the green/white with the orange/white.
ImageSource: https://incentre.net/ethernet-cable-color-coding-diagram/
© Edunet Foundation. All rights reserved.

## Slide 499: Crimping tools and Color standards for Straight crimping and Crosscrimping
Ethernet Cable Instructions
Pull the cable off the reel to the desired length and cut. If you are pulling cables through holes, its easier to attach the RJ-45 plugs after the cable is pulled.
ImageSource:https://cabling.4cornerit.com/
© Edunet Foundation. All rights reserved.

## Slide 500: Crimping tools and Color standards for Straight crimping and Crosscrimping Ethernet Cable Instructions(continued)
The total length of wire segments between a PC and a hub or between two PC's cannot exceed 100 Meters (328 feet) for 100BASE-TX and 300 Meters for 10BASE-T
ImageSource:https://cabling.4cornerit.com/
© Edunet Foundation. All rights reserved.

## Slide 501: Crimping tools and Color standards for Straight crimping and Crosscrimping Ethernet Cable Instructions(continued)
Start on one end and strip the cable jacket off (about 1″) using a stripper or a knife. Be extra careful not to nick the wires, otherwise you will need to start over.
ImageSource:https://www.dx.com/p/rj45-connector-cable-plier-network-crimper
© Edunet Foundation. All rights reserved.

## Slide 502: Crimping tools and Color standards for Straight crimping and Crosscrimping Ethernet Cable Instructions(continued)
Spread, untwist the pairs, and arrange the wires in the order of the desired cable end. Flatten the end between your thumb and forefinger. Trim the ends of the wires so they are even with one another, leaving only 1/2″ in wire length.
ImageSource:https://www.vcelink.com/blogs/focus/how-to-crimp-rj45-connectors
© Edunet Foundation. All rights reserved.

## Slide 503: Crimping tools and Color standards for Straight crimping and Crosscrimping Ethernet Cable Instructions(continued)
If it is longer than 1/2″ it will be out-of-spec and susceptible to crosstalk. Flatten and insure there are no spaces between wires.
Hold the RJ-45 plug with the clip facing down or away from you. Push the wires firmly into the plug.
ImageSource: https://cabling.4cornerit.com/
© Edunet Foundation. All rights reserved.

## Slide 504: Crimping tools and Color standards for Straight crimping and Crosscrimping Ethernet Cable Instructions(continued)
Inspect each wire is flat even at the front of the plug. Check the order of the wires. Double check again. Check that the jacket is fitted right against the stop of the plug.Carefully hold the wire and firmly crimp the RJ-45 with the crimper.
ImageSource: https://medium.com/@julydd/how-to-make-your-own-ethernet-cables-513d56470698
© Edunet Foundation. All rights reserved.

## Slide 505: Crimping tools and Color standards for Straight crimping and Crosscrimping
Ethernet Cable Instructions
Check the color orientation, check that the crimped connection is not about to come apart, and check to see if the wires are flat against the front of the plug. If even one of these are incorrect, you will have to start over. Test the Ethernet cable.
ImageSource:https://instrumentationtools.com/make-rj45-cable/
© Edunet Foundation. All rights reserved.

## Slide 506: Transmission Media and Topologies Media types
(15 hours)
Notes: Title - The learning outcome
Subtitle - Duration

## Slide 507: In this section, we will discuss:
Concept of Server, client
Node
Segment
Backbone
Host
Analog and Digital transmission
Base band and Broadband transmission
STP cable, UTP cable, Coaxial cable, Fiber cable and Connectors
Physical and logical topologies, Bus, Star, Ring and Mesh topologies
Concept of Asynchronous & Synchronous Transmission
Notes: Mention the parent topics one by one. This particular learning outcome has 4 parent topics.

## Slide 508: Concept of Server, client
Client-Server Model
It is a distributed application framework dividing tasks between servers and clients
Clients initiate requests for services and servers provide that function or service.
Image Source: https://www.omnisci.com/technical-glossary/client-server
Notes: The client-server model, or client-server architecture, is a distributed application framework dividing tasks between servers and clients, which either reside in the same system or communicate through a computer network or the Internet. The client relies on sending a request to another program in order to access a service made available by a server. The server runs one or more programs that share resources with and distribute work among clients.
The client server relationship communicates in a request–response messaging pattern and must adhere to a common communications protocol, which formally defines the rules, language, and dialog patterns to be used. Client-server communication typically adheres to the TCP/IP protocol suite.
Reference:
https://www.omnisci.com/technical-glossary/client-server

## Slide 509: Concept of Server, client
Categories of Client-Server Computing
There are four main categories of client-server computing:
One-Tier architecture
Two-Tier architecture
Three-Tier architecture
N-Tier architecture
Image Source: https://www.omnisci.com/technical-glossary/client-server
Notes: There are four main categories of client-server computing:
One-Tier architecture: consists of a simple program running on a single computer without requiring access to the network. User requests don’t manage any network protocols, therefore the code is simple and the network is relieved of the extra traffic.
Two-Tier architecture: consists of the client, the server, and the protocol that links the two tiers. The Graphical User Interface code resides on the client host and the domain logic resides on the server host. The client-server GUI is written in high-level languages such as C++ and Java.
Three-Tier architecture: consists of a presentation tier, which is the User Interface layer, the application tier, which is the service layer that performs detailed processing, and the data tier, which consists of a database server that stores information.
N-Tier architecture: divides an application into logical layers, which separate responsibilities and manage dependencies, and physical tiers, which run on separate machines, improve scalability, and add latency from the additional network communication. N-Tier architecture can be closed-layer, in which a layer can only communicate with the next layer down, or open-layer, in which a layer can communicate with any layers below it.
Reference:
https://www.omnisci.com/technical-glossary/client-server

## Slide 510: Concept of Server, client
Difference Between Client and Server
Client computing is classified as:
Thick client
Thin client
Hybrid client
Image Source: https://www.omnisci.com/technical-glossary/client-server
Notes: Clients, also known as service requesters, are pieces of computer hardware or server software that request resources and services made available by a server. Client computing is classified as Thick, Thin, or Hybrid.
Thick Client: a client that provides rich functionality, performs the majority of data processing itself, and relies very lightly upon the server.
Thin Client: a thin-client server is a lightweight computer that relies heavily on the resources of the host computer -- an application server performs the majority of any required data processing.
Hybrid Client: possessing a combination of thin client and thick client characteristics, a hybrid client relies on the server to store persistent data, but is capable of local processing.
Reference:
https://www.omnisci.com/technical-glossary/client-server

## Slide 511: Concept of Server, client
Difference Between Client and Server
A server is a device or computer program that provides functionality for other devices or programs.
Some common examples of servers include:
Application Server
Computing Server
Database Server
Web Server
Image Source: https://www.omnisci.com/technical-glossary/client-server
Notes: A server is a device or computer program that provides functionality for other devices or programs. Any computerized process that can be used or called upon by a client to share resources and distribute work is a server. Some common examples of servers include:
• Application Server: hosts web applications that users in the network can use without needing their own copy.
• Computing Server: shares an enormous amount of computer resources with networked computers that require more CPU power and RAM than is typically available for a personal computer.
• Database Server: maintains and shares databases for any computer program that ingests well-organized data, such as accounting software and spreadsheets.
• Web Server: hosts web pages and facilitates the existence of the World Wide Web.
Reference:
https://www.omnisci.com/technical-glossary/client-server

## Slide 512: Concept of Server, client
Difference Between Server-Side Programming and Client-Side Programming
Server-side programming refers to a program that runs on the server and focuses on the generation of dynamic content.
Client-side programming refers to a program that runs on the client machine and focuses on the user interface and other processes such as reading and/or writing cookies.
Image Source: https://www.omnisci.com/technical-glossary/client-server
Notes: Server-side programming refers to a program that runs on the server and focuses on the generation of dynamic content. Server-side programming is used for querying and interacting with the database, accessing files on a server, interacting with other servers, processing user input, and structuring web applications. Popular programming languages for server-side programming include C++, Java and JSP, PHP, Python, and Ruby on Rails.
Client-side programming refers to a program that runs on the client machine and focuses on the user interface and other processes such as reading and/or writing cookies. Client-side programming is used for sending requests to the server, interacting with local storage, interacting with temporary storage, creating interactive web pages, and functions as an interface between client and server. Popular programming languages for client-server programming include AJAX, CSS, HTML, Javascript, and VBScript.
Reference:
https://www.omnisci.com/technical-glossary/client-server

## Slide 513: Concept of Server, client
Client-Server vs Peer-to-Peer
Peer-to-peer (P2P) is a decentralized communications model
In client-server computing, a centralized communications model, the server is the central node that communicates with other client nodes.
Image Source: https://www.omnisci.com/technical-glossary/client-server
Notes: Peer-to-peer (P2P) is a decentralized communications model in which all nodes in the network have equivalent capability and can function as both a client and server. Nodes in peer-to-peer computing collectively use their resources and communicate with each other directly on-demand.
An algorithm in the peer-to-peer communications protocol balances load, making other peers available to compensate for any resource downtime, and rerouting requests as the load capacity and availability of peers changes. A major advantage of peer-to-peer networking is the ability to expand the network to manage a large number of clients.
In client-server computing, a centralized communications model, the server is the central node that communicates with other client nodes. A major advantage that the client-server relationship has over the peer-to-peer relationship is the ability to manage data and applications in one, centralized server.
Reference:
https://www.omnisci.com/technical-glossary/client-server

## Slide 514: Node
What is a computer network and where do network nodes fit in?
A computer network is a system of computers and computing devices that are connected via communication links.
A network node is a connection point in a communications network.
Image Source: https://www.elprocus.com/what-are-network-nodes-in-computer-network-and-their-types/
Notes: A computer network is a system of computers and computing devices that are connected via communication links. These links allow the computers and other devices to send information over the network.
A network node is a connection point in a communications network. Each node is an endpoint for data transmissions or redistribution. Nodes have either a programmed or engineered capability to recognize, process and forward transmissions to other network nodes.
The concept of network nodes came into being with the use of distributed networks and packet switching. Depending on the application, network nodes perform a variety of functions.
Reference:
https://www.techtarget.com/searchnetworking/definition/node#:~:text=A%20network%20node%20sits%20at,as%20modems%2C%20PCs%20and%20printers.

## Slide 515: Node
What does a network node do?
A network node sits at a point in the network where it sends, receives, stores or creates information.
It transmits data to communicate with other nodes in the network.
Image Source: https://www.elprocus.com/what-are-network-nodes-in-computer-network-and-their-types/
Notes: A network node sits at a point in the network where it sends, receives, stores or creates information. It transmits data to communicate with other nodes in the network.
In a computer network, nodes can be physical networked devices, such as modems, PCs and printers. These devices recognize transmissions from other nodes and forward them to other nodes. A node checks for identification, such as an IP address, to grant access to the node.
Nodes connect over a link or communication channel. In a computer network these may be cable, fiber optic or wireless connections.
Reference:
https://www.techtarget.com/searchnetworking/definition/node#:~:text=A%20network%20node%20sits%20at,as%20modems%2C%20PCs%20and%20printers.

## Slide 516: Node
Types of network nodes
By network Type
Data communications
Internet network
LANs and wide area networks
Telecommunications network
Cable system
Image Source: https://www.elprocus.com/what-are-network-nodes-in-computer-network-and-their-types/
Notes: There are several ways to categorize nodes. One way is by network type; another is by network topology.
Network type
Data communications. In data communications, physical network nodes include data communications equipment or devices that sit between data terminal equipment (DTE) and data transmission circuits. These include switches, bridges, modems or hubs that perform signal conversion, coding and line clocking. These nodes also include DTE, such as digital telephone handsets, printers, routers, servers and workstations.
Internet network. On the internet and with intranets, most physical network nodes are host computers identified by an IP address. However, some data link devices, such as wireless local area network (LAN) access points, do not have IP host addresses. They are considered physical network or LAN nodes rather than internet nodes or hosts.
LANs and wide area networks. These nodes are devices that perform a specific function. Each one must have a Media Access Control address for each network interface card. Examples include modems with Ethernet interfaces, wireless LAN access points and computers.
Telecommunications network. In fixed telephone networks, nodes may be public or private telephone exchanges or a computer providing an intelligent network service. In cellular communications, nodes include base station controllers that control one or more base stations. Cellular network base stations are not considered nodes.
Cable system. In cable systems, nodes use fiber optic cable to connect to businesses and homes served by a common fiber optic receiver within a geographic location. A fiber optic node describes the number of homes or businesses that a specific fiber node can serve.
Reference:
https://www.techtarget.com/searchnetworking/definition/node#:~:text=A%20network%20node%20sits%20at,as%20modems%2C%20PCs%20and%20printers.

## Slide 517: Node
Types of network nodes
By network topologies:
Bus topology
Ring topology
Star topology
Mesh topology
Image Source: https://www.techtarget.com/searchnetworking/definition/node#:~:text=A%20network%20node%20sits%20at,as%20modems%2C%20PCs%20and%20printers.
Notes: Another way to categorize nodes is by how they are arranged in a physical computer network. This is known as the network topology approach. Some common network topologies include these four:
Bus topology - connects individual nodes directly to a main cable.
Ring topology - has nodes connected in a loop or ring; each node has a neighbor on each side.
Star topology - connects all nodes to a central hub.
Mesh topology - has every node connected to every other node.
Reference:
https://www.techtarget.com/searchnetworking/definition/node#:~:text=A%20network%20node%20sits%20at,as%20modems%2C%20PCs%20and%20printers.

## Slide 518: Segment
What is network segment?
A network segment is a portion of a computer network.
Image Source: https://www.reddit.com/r/ccnp/comments/cu85ui/what_is_the_definition_of_a_network_segment/
Notes: A network segment is a portion of a computer network. The nature and extent of a segment depends on the nature of the network and the device or devices used to interconnect end stations.
Reference:
https://en.wikipedia.org/wiki/Network_segment#:~:text=A%20network%20segment%20is%20a,used%20to%20interconnect%20end%20stations.

## Slide 519: Backbone
What is a backbone network?
A Backbone Network is a Network containing a high capacity connectivity infrastructure that backbone to the different part of the network.
Image Source: https://www.geeksforgeeks.org/types-and-uses-of-backbone-networks/
Notes: A Backbone is most important part of a system which provides the central support to the rest system, for example backbone of a human body that balance and hold all the body parts. Similarly in Computer Networks a Backbone Network is as a Network containing a high capacity connectivity infrastructure that backbone to the different part of the network.
Actually a backbone network allows multiple LANs to get connected in a backbone network, not a single station is directly connected to the backbone but the stations are part of LAN, and backbone connect those LANs.
Reference:
https://www.geeksforgeeks.org/types-and-uses-of-backbone-networks/#:~:text=The%20backbone%20itself%20is%20a,%3A%20Bus%20backbone%2C%20Star%20backbone.

## Slide 520: Host
What is web hosting?
Web hosting is an online service that allows you to publish your website files onto the internet.
Image Source: https://www.educba.com/what-is-web-hosting/
Notes: Web hosting is an online service that allows you to publish your website files onto the internet. So, anyone who has access to the internet has access to your website. In practice, it usually refers to the service you get from a web hosting provider.
Reference:
https://https://www.one.com/en/hosting/what-is-web-hosting

## Slide 521: Host
How does web hosting work?
Your web host is responsible for making sure your server is up and running.
Prevents any security breaches and store all your files, assets and databases onto the server.
Image Source: https://www.educba.com/what-is-web-hosting/
Notes: Once you’ve chosen your domain name and signed up to a hosting plan, then your website is accessible on the internet.
When you use web hosting services, your web host is responsible for making sure your server is up and running. Not only that, but it is also a hosts job to prevent any security breaches and store all your files, assets and databases onto the server.
Reference:
https://https://www.one.com/en/hosting/what-is-web-hosting

## Slide 522: Host
Types of web hosting
Shared Hosting
WordPress Hosting
VPS Hosting
Dedicated Hosting
Cloud Hosting
Image Source: https://www.educba.com/what-is-web-hosting/
Notes: Shared Hosting
Shared hosting is when a web hosting provider hosts a number of different websites on the same server. It is the most affordable form of hosting because you share the same server, so you split costs. If you are looking to start a blog or have a business that's just starting up, then shared hosting is a good option.
WordPress Hosting
WordPress Hosting simply means hosting that has been optimised for WordPress on a server level to ensure smooth sailing.
VPS Hosting
VPS stands for Virtual Private Server. Like shared hosting, websites that run on VPS share a physical server with other websites. However, each VPS tenant has its own partition with guaranteed dedicated resources. There’s often more memory, storage and processing power available – with a price tag to match.
Dedicated Hosting
Dedicated hosting means you have the entire server to yourself. It gives you access like a VPS, but you don’t have to share the server with other sites or apps. Effectively, you are leasing a physical web server housed at your service provider’s facility.
Cloud Hosting
These days, cloud hosting has become a bit of a nebulous term. So, we would strongly recommend looking closely at what you are getting if you are signing up for “Cloud Hosting”.
Reference:
https://https://www.one.com/en/hosting/what-is-web-hosting

## Slide 523: Host
How much does website hosting cost?
Website hosting cost will vary by provider.
Free web hosting
Paid web hosting
Image Source: https://www.educba.com/what-is-web-hosting/
Notes: Your website hosting cost will vary by provider. Technically you can use a free web hosting service.
By opting for free hosting, you may encounter problems such as unwanted advertising on your page and their domain name in your URL. When you pay for web hosting, you are in full control of what content is on your website.
Reference:
https://https://www.one.com/en/hosting/what-is-web-hosting

## Slide 524: Host
Where do domains come into the picture with website hosting?
The domain is the means through which the browser locates the right server and downloads the website files.
Image Source: https://www.educba.com/what-is-web-hosting/
Notes: Let’s think of your website as a house built from individual files. The web hosting is the land the house (website) is on, and the domain is its address. When someone types in the domain name into their web browser or clicks a web link, the domain is the means through which the browser locates the right server and downloads the website files.
Reference:
https://https://www.one.com/en/hosting/what-is-web-hosting

## Slide 525: Analog Transmission
Concept
An analog wave form (or signal) is characterized by being continuously variable along amplitude and frequency.
Image Source: https://www.guru99.com/analog-vs-digital.html
Notes: An analog wave form (or signal) is characterized by being continuously variable along amplitude and frequency. In the case of telephony, for instance, when you speak into a handset, there are changes in the air pressure around your mouth. Those changes in air pressure fall onto the handset, where they are amplified and then converted into current, or voltage fluctuations. Those fluctuations in current are an analog of the actual voice pattern—hence the use of the term analog to describe these signals.
Reference:
https://www.informit.com/articles/article.aspx?p=24687&seqNum=5
https://www.guru99.com/analog-vs-digital.html
https://www.monolithicpower.com/en/analog-vs-digital-signal

## Slide 526: Analog Transmission
Advantages
Easier in processing
Best suited for audio and video transmission.
It has a low cost and is portable.
It has a much higher density so that it can present more refined information.
Not necessary to buy a new graphics board.
Uses less bandwidth than digital sounds
Provide more accurate representation of a sound
It is the natural form of a sound.
Image Source: https://www.guru99.com/analog-vs-digital.html
Notes: Here, are pros/benefits of Analog Signals
• Easier in processing
• Best suited for audio and video transmission.
• It has a low cost and is portable.
• It has a much higher density so that it can present more refined information.
• Not necessary to buy a new graphics board.
• Uses less bandwidth than digital sounds
• Provide more accurate representation of a sound
• It is the natural form of a sound.
Reference:
https://www.informit.com/articles/article.aspx?p=24687&seqNum=5
https://www.guru99.com/analog-vs-digital.html
https://www.monolithicpower.com/en/analog-vs-digital-signal

## Slide 527: Analog Transmission
Disadvantages
Analog tends to have a lower quality signal than digital.
The cables are sensitive to external influences.
The cost of the Analog wire is high and not easily portable.
Low availability of models with digital interfaces.
Recording analog sound on tape is quite expensive if the tape is damaged
It offers limitations in editing
Image Source: https://www.guru99.com/analog-vs-digital.html
Notes: Here are cons/drawback of Analog Signals:
• Analog tends to have a lower quality signal than digital.
• The cables are sensitive to external influences.
• The cost of the Analog wire is high and not easily portable.
• Low availability of models with digital interfaces.
• Recording analog sound on tape is quite expensive if the tape is damaged
• It offers limitations in editing
• Tape is becoming hard to find
• It is quite difficult to synchronize analog sound
• Quality is easily lost
• Data can become corrupted
• Plenty of recording devices and formats which can become confusing to store a digital signal
• Digital sounds can cut an analog sound wave which means that you can’t get a perfect reproduction of a sound
• Offers poor multi-user interfaces
Reference:
https://www.informit.com/articles/article.aspx?p=24687&seqNum=5
https://www.guru99.com/analog-vs-digital.html
https://www.monolithicpower.com/en/analog-vs-digital-signal

## Slide 528: Analog Transmission
Disadvantages
Tape is becoming hard to find
It is quite difficult to synchronize analog sound
Quality is easily lost
Data can become corrupted
Plenty of recording devices and formats which can become confusing to store a digital signal
Digital sounds can cut an analog sound wave which means that you can’t get a perfect reproduction of a sound
Offers poor multi-user interfaces
Image Source: https://www.guru99.com/analog-vs-digital.html
Notes: • Tape is becoming hard to find
• It is quite difficult to synchronize analog sound
• Quality is easily lost
• Data can become corrupted
• Plenty of recording devices and formats which can become confusing to store a digital signal
• Digital sounds can cut an analog sound wave which means that you can’t get a perfect reproduction of a sound
• Offers poor multi-user interfaces
Reference:
https://www.informit.com/articles/article.aspx?p=24687&seqNum=5
https://www.guru99.com/analog-vs-digital.html
https://www.monolithicpower.com/en/analog-vs-digital-signal

## Slide 529: Digital Transmission
Concept
It is a series of discrete pulses, representing one bits and zero bits.
Image Source: https://www.guru99.com/analog-vs-digital.html
Notes: Digital transmission is quite different from analog transmission. For one thing, the signal is much simpler. Rather than being a continuously variable wave form, it is a series of discrete pulses, representing one bits and zero bits.
Reference:
https://www.informit.com/articles/article.aspx?p=24687&seqNum=5
https://www.guru99.com/analog-vs-digital.html
https://www.monolithicpower.com/en/analog-vs-digital-signal

## Slide 530: Digital Transmission
Advantages
Digital data can be easily compressed.
Any information in the digital form can be encrypted.
Equipment that uses digital signals is more common and less expensive.
Digital signal makes running instruments free from observation errors like parallax and approximation errors.
A lot of editing tools are available
You can edit the sound without altering the original copy
Easy to transmit the data over networks
Image Source: https://www.guru99.com/analog-vs-digital.html
Notes: Here, are pros/advantages of Digital Signals:
Digital data can be easily compressed.
Any information in the digital form can be encrypted.
Equipment that uses digital signals is more common and less expensive.
Digital signal makes running instruments free from observation errors like parallax and approximation errors.
A lot of editing tools are available
You can edit the sound without altering the original copy
Easy to transmit the data over networks
Reference:
https://www.informit.com/articles/article.aspx?p=24687&seqNum=5
https://www.guru99.com/analog-vs-digital.html
https://www.monolithicpower.com/en/analog-vs-digital-signal

## Slide 531: Digital Transmission
Disadvantages
Sampling may cause loss of information.
A/D and D/A demands mixed-signal hardware
Processor speed is limited
Develop quantization and round-off errors
It requires greater bandwidth
Systems and processing is more complex.
Image Source: https://www.guru99.com/analog-vs-digital.html
Notes: Here, are disadvantages of Digital Signals:
Sampling may cause loss of information.
A/D and D/A demands mixed-signal hardware
Processor speed is limited
Develop quantization and round-off errors
It requires greater bandwidth
Systems and processing is more complex.
Reference:
https://www.informit.com/articles/article.aspx?p=24687&seqNum=5
https://www.guru99.com/analog-vs-digital.html
https://www.monolithicpower.com/en/analog-vs-digital-signal

## Slide 532: Analog and Digital Signals
Systems and Applications
Audio recording and reproduction
Temperature sensors
Image sensors
Radio signals
Telephones
Control systems
Communication systems (broadband, cellular)
Networking and data communications
Digital interfaces for programmability
Image Source: https://www.guru99.com/analog-vs-digital.html
Notes: Traditional audio and communication systems used analog signals. However, with advances in silicon process technologies, digital signal processing capabilities, encoding algorithms, and encryption requirements — in addition to increases in bandwidth efficiencies — many of these systems have become digital. They are still some applications where analog signals have legacy use or benefits. Most systems that interface to real-world signals (such as sound, light, temperature, and pressure) use an analog interface to capture or transmit the information. A few analog signal applications are listed below:
• Audio recording and reproduction
• Temperature sensors
• Image sensors
• Radio signals
• Telephones
• Control systems
Although many original communication systems used analog signaling (telephones), recent technologies use digital signals because of their advantages with noise immunity, encryption, bandwidth efficiency, and the ability to use repeaters for long-distance transmission. A few digital signal applications are listed below:
• Communication systems (broadband, cellular)
• Networking and data communications
• Digital interfaces for programmability
Reference:
https://www.informit.com/articles/article.aspx?p=24687&seqNum=5
https://www.guru99.com/analog-vs-digital.html
https://www.monolithicpower.com/en/analog-vs-digital-signal

## Slide 533: Base band and Broadband transmission
Broadband system and Baseband transmission
Broadband system use modulation techniques to reduce the effect of noise in the environment.
Baseband is a digital signal. It is transmitted on the medium using one of the signal codes like NRZ, RZ Manchester biphase-M code etc. is called baseband transmission.
Image Source: https://www.computernetworkingnotes.com/networking-tutorials/differences-between-baseband-and-broadband-explained.html
Notes: Broadband system use modulation techniques to reduce the effect of noise in the environment. Broadband transmission employs multiple channel unidirectional transmission using combination of phase and amplitude modulation.
Baseband is a digital signal is transmitted on the medium using one of the signal codes like NRZ, RZ Manchester biphase-M code etc. is called baseband transmission.
Reference:
https://www.geeksforgeeks.org/difference-between-broadband-and-baseband-transmission/

## Slide 534: Network cables and connectors
Coaxial Cables
A solid-core copper wire conductor runs down the middle of the cable.
Around that solid-core copper wire is a layer of insulation, and
Covering that insulation is braided wire and metal foil shield, which shields against electromagnetic interference.
A final layer of plastic insulation jacket covers the braided wire.
Image Source: https://techdifferences.com/difference-between-optical-fibre-and-coaxial-cable.html
Notes: Cables are commonly used to carry communication signals within Local Area Networks (LAN). There are three common types of cable media that can be used to connect devices to a network and they are coaxial cable, twisted-pair cable, and fiber-optic cable.
Coaxial cable looks similar to the cable used to carry TV signal. A solid-core copper wire conductor runs down the middle of the cable. Around that solid-core copper wire is a layer of insulation, and covering that insulation is braided wire and metal foil shield, which shields against electromagnetic interference. A final layer of plastic insulation jacket covers the braided wire.
Reference:
https://www.omnisecu.com/basic-networking/common-network-cable-types.php
https://www.homedepot.com/c/ab/types-of-cables-and-connectors-in-networking/9ba683603be9fa5395fab90e9250f90

## Slide 535: Network cables and connectors
Coaxial Cables Types
There are two types of coaxial cabling:
ThinNet and
ThickNet.
Image Source: https://slideplayer.com/slide/14121004/
Notes: There are two types of coaxial cabling: ThinNet and ThickNet. ThinNet is a flexible coaxial cable about ¼ inch thick. ThinNet is used for short-distance. ThinNet connects directly to a workstation’s network adapter card using a British Naval Connector (BNC). The maximum length of thinnet is 185 to 200 meters. ThickNet coaxial cable is thicker cable than ThinNet. ThickNet cable is about ½ inch thick and can support data transfer over longer distances than ThinNet. ThickNet has a maximum supported cable length of 500 meters and usually is used as a backbone to connect several smaller ThinNet-based networks.
Reference:
https://www.omnisecu.com/basic-networking/common-network-cable-types.php
https://www.homedepot.com/c/ab/types-of-cables-and-connectors-in-networking/9ba683603be9fa5395fab90e9250f90

## Slide 536: Network cables and connectors
Twisted Pair Cables
A pair of wires forms a circuit that can transmit data.
The pairs are twisted to provide protection against crosstalk.
Image Source: https://slideplayer.com/slide/14121004/
Notes: Twisted-pair cable is the most common type of cabling you can see in today's Local Area Networks (LAN) networks. A pair of wires forms a circuit that can transmit data. The pairs are twisted to provide protection against crosstalk. Crosstalk is the undesired signal noise generated by the electromagnetic fields of the adjacent wires.
When a wire is carrying a current, the current creates a magnetic field around the wire. This field can interfere with signals on nearby wires. To eliminate this, pairs of wires carry signals in opposite directions, so that the two magnetic fields also occur in opposite directions and cancel each other out. This process is known as cancellation.
Color codes used for Twisted Pair wire’s plastic insulation are Orange, Orange-White, Blue, Blue-White, Green, Green-White, Brown and Brown-White.
Two types of twisted pair cables are Unshielded Twisted Pair (UTP) and Shielded Twisted Pair (STP).
Reference:
https://www.omnisecu.com/basic-networking/common-network-cable-types.php
https://www.homedepot.com/c/ab/types-of-cables-and-connectors-in-networking/9ba683603be9fa5395fab90e9250f90

## Slide 537: Network cables and connectors
Unshielded Twisted Pair (UTP)
Unshielded Twisted Pair (UTP) cable is the most common networking media.
Unshielded Twisted Pair (UTP) consists of four pairs of thin, copper wires covered in color-coded plastic insulation that are twisted together.
Image Source: https://www.fiberoptics4sale.com/blogs/archive-posts/95046918-what-is-unshielded-twisted-pair-utp-cable
Notes: Two types of twisted pair cables are Unshielded Twisted Pair (UTP) and Shielded Twisted Pair (STP).
Unshielded Twisted Pair (UTP) cable is the most common networking media. Unshielded Twisted Pair (UTP) consists of four pairs of thin, copper wires covered in color-coded plastic insulation that are twisted together. The wire pairs are then covered with a plastic outer jacket. UTP cables are of small diameter and it doesn’t need grounding. Since there is no shielding for UTP cabling, it relies only on "cancellation" to avoid noise.
Reference:
https://www.omnisecu.com/basic-networking/common-network-cable-types.php
https://www.homedepot.com/c/ab/types-of-cables-and-connectors-in-networking/9ba683603be9fa5395fab90e9250f90

## Slide 538: Network cables and connectors
Shielded Twisted Pair (STP) cables
Shielded Twisted Pair (STP) cables additionally have an overall conducting metallic shields covering four twisted pair wires.
There may be another conducting metallic shields covering individual twisted pairs also.
These metallic shields blocks out electromagnetic interference to prevent unwanted noise from the communication circuit.
Image Source: https://www.electronicsmedia.info/2018/01/02/unshielded-twisted-pair-and-shielded-twisted-pair-cable/
Notes: Shielded Twisted Pair (STP) cables additionally have an overall conducting metallic shields covering four twisted pair wires. There may be another conducting metallic shields covering individual twisted pairs also. These metallic shields blocks out electromagnetic interference to prevent unwanted noise from the communication circuit.
Drain wires are also used in Shielded Twisted Pair (STP) cables together with metallic shields for grounding purpose. The drain wire provides a low-resistance connection to shield for better grounding. The main purpose of drain wire is to carry away unwanted interference noise to ground.
Reference:
https://www.omnisecu.com/basic-networking/common-network-cable-types.php
https://www.homedepot.com/c/ab/types-of-cables-and-connectors-in-networking/9ba683603be9fa5395fab90e9250f90

## Slide 539: Network cables and connectors
Types of Connectors
Ethernet Cable Connectors
RJ45 connectors are used for CAT6 cables and CAT5e cables.
These connectors for twisted-pair Ethernet cables are similar in appearance to a standard telephone cord connector.
Image Source: https://www.homedepot.com/c/ab/types-of-cables-and-connectors-in-networking/9ba683603be9fa5395fab90e9250f90
Notes: RJ45 connectors are used for CAT6 cables and CAT5e cables. These connectors for twisted-pair Ethernet cables are similar in appearance to a standard telephone cord connector. They are wider, however, because they have eight conductors compared to only four conductors on a telephone jack.
Reference:
https://www.omnisecu.com/basic-networking/common-network-cable-types.php
https://www.homedepot.com/c/ab/types-of-cables-and-connectors-in-networking/9ba683603be9fa5395fab90e9250f90

## Slide 540: Network cables and connectors
Types of Connectors
Coaxial Cable Connectors
BNC connectors are a type of F-series connectors commonly found in households.
This type of connector for RG59 or RG6 coaxial cable is used for cable television equipment, broadcast TV antenna applications and CCTV security camera installations.
Image Source: https://www.homedepot.com/c/ab/types-of-cables-and-connectors-in-networking/9ba683603be9fa5395fab90e9250f90
Notes: BNC connectors are a type of F-series connectors commonly found in households. This type of connector for RG59 or RG6 coaxial cable is used for cable television equipment, broadcast TV antenna applications and CCTV security camera installations. They are easy to connect and disconnect from equipment and provide inexpensive, stable connections to these communications devices and other cables.
Reference:
https://www.omnisecu.com/basic-networking/common-network-cable-types.php
https://www.homedepot.com/c/ab/types-of-cables-and-connectors-in-networking/9ba683603be9fa5395fab90e9250f90

## Slide 541: Network cables and connectors
Types of Connectors
USB Connectors
USB (Universal Serial Bus) connectors typically join external devices to a personal computer or are used for mobile phone charging.
Image Source: https://www.homedepot.com/c/ab/types-of-cables-and-connectors-in-networking/9ba683603be9fa5395fab90e9250f90
Notes: USB connectors are perhaps most familiar to the majority of people. USB (Universal Serial Bus) connectors typically join external devices to a personal computer or are used for mobile phone charging. There are adapters that will allow an Ethernet cable to connect directly to a USB port, though this type of setup would be a temporary solution for networking.
Reference:
https://www.omnisecu.com/basic-networking/common-network-cable-types.php
https://www.homedepot.com/c/ab/types-of-cables-and-connectors-in-networking/9ba683603be9fa5395fab90e9250f90

## Slide 542: Network cables and connectors
Types of Connectors
Fiber Optic Cable Connectors
These types of connectors in networking must align glass fibers with precision to allow for communication.
Image Source: https://www.homedepot.com/c/ab/types-of-cables-and-connectors-in-networking/9ba683603be9fa5395fab90e9250f90
Notes: Fiber optic connectors require different types of connectors from those used with coax or twisted-pair cables, such as CAT5e. These types of connectors in networking must align glass fibers with precision to allow for communication. If you choose to use optical cable over twisted pair Ethernet, you may need to install a special adapter in your computer to utilize various fiber optic cable connector types.
Reference:
https://www.omnisecu.com/basic-networking/common-network-cable-types.php
https://www.homedepot.com/c/ab/types-of-cables-and-connectors-in-networking/9ba683603be9fa5395fab90e9250f90

## Slide 543: Physical and logical topologies
Physical Topology
Physical topology indicates arrangement of different elements of a network.
It reflects physical layout of devices and cables to a form a connected network.
Image Source: https://www.javatpoint.com/computer-network-topologies
Notes: Physical topology indicates arrangement of different elements of a network. It reflects physical layout of devices and cables to a form a connected network. It is concerned with essentials of network ignoring minute details like transfer of data and device type. The pattern of arrangement of nodes (computers) and network cables depends on ease of installation and setup of the network. It affects cost and bandwidth capacity based on solution of devices. It takes into account placement of nodes and distance between them. Devices can be arranged to form a ring (Ring Topology) or linearly connected in a line called Bus Topology.
Reference:
https://www.geeksforgeeks.org/difference-between-physical-and-logical-topology/
https://www.javatpoint.com/computer-network-topologies

## Slide 544: Physical and logical topologies
Logical Topology
Logical Topology reflects arrangement of devices and their communication.
It is the transmission of data over physical topology.
Image Source: https://www.javatpoint.com/computer-network-topologies
Notes: Logical Topology reflects arrangement of devices and their communication. It is the transmission of data over physical topology. It is independent of physical topology, irrespective of arrangements of nodes. It is concerned with intricate details of network like type of devices (switches, routers) chosen and their quality, which affect rate and speed of data packets delivery. The logical topology ensures optimal flow control that can be regulated within network.
Reference:
https://www.geeksforgeeks.org/difference-between-physical-and-logical-topology/
https://www.javatpoint.com/computer-network-topologies

## Slide 545: Types of Network Topology
Bus Topology
The bus topology is designed in such a way that all the stations are connected through a single cable known as a backbone cable.
Each node is either connected to the backbone cable by drop cable or directly connected to the backbone cable.
Image Source: https://www.javatpoint.com/computer-network-topologies
Notes: The bus topology is designed in such a way that all the stations are connected through a single cable known as a backbone cable.
Each node is either connected to the backbone cable by drop cable or directly connected to the backbone cable.
When a node wants to send a message over the network, it puts a message over the network. All the stations available in the network will receive the message whether it has been addressed or not.
The bus topology is mainly used in 802.3 (ethernet) and 802.4 standard networks.
The configuration of a bus topology is quite simpler as compared to other topologies.
The backbone cable is considered as a "single lane" through which the message is broadcast to all the stations.
The most common access method of the bus topologies is CSMA (Carrier Sense Multiple Access).
Reference:
https://www.geeksforgeeks.org/difference-between-physical-and-logical-topology/
https://www.javatpoint.com/computer-network-topologies

## Slide 546: Types of Network Topology
Ring Topology
Ring topology is like a bus topology, but with connected ends.
The node that receives the message from the previous computer will retransmit to the next node.
Image Source: https://www.javatpoint.com/computer-network-topologies
Notes: Ring topology is like a bus topology, but with connected ends.
The node that receives the message from the previous computer will retransmit to the next node.
The data flows in one direction, i.e., it is unidirectional.
The data flows in a single loop continuously known as an endless loop.
It has no terminated ends, i.e., each node is connected to other node and having no termination point.
The data in a ring topology flow in a clockwise direction.
The most common access method of the ring topology is token passing.
Token passing: It is a network access method in which token is passed from one node to another node.
Token: It is a frame that circulates around the network.
Reference:
https://www.geeksforgeeks.org/difference-between-physical-and-logical-topology/
https://www.javatpoint.com/computer-network-topologies

## Slide 547: Types of Network Topology
Star Topology
Star topology is an arrangement of the network in which every node is connected to the central hub, switch or a central computer.
The central computer is known as a server, and the peripheral devices attached to the server are known as clients.
Image Source: https://www.javatpoint.com/computer-network-topologies
Notes: Star topology is an arrangement of the network in which every node is connected to the central hub, switch or a central computer.
The central computer is known as a server, and the peripheral devices attached to the server are known as clients.
Coaxial cable or RJ-45 cables are used to connect the computers.
Hubs or Switches are mainly used as connection devices in a physical star topology.
Star topology is the most popular topology in network implementation.
Reference:
https://www.geeksforgeeks.org/difference-between-physical-and-logical-topology/
https://www.javatpoint.com/computer-network-topologies

## Slide 548: Types of Network Topology
Tree topology
Tree topology combines the characteristics of bus topology and star topology.
A tree topology is a type of structure in which all the computers are connected with each other in hierarchical fashion.
Image Source: https://www.javatpoint.com/computer-network-topologies
Notes: Tree topology combines the characteristics of bus topology and star topology.
A tree topology is a type of structure in which all the computers are connected with each other in hierarchical fashion.
The top-most node in tree topology is known as a root node, and all other nodes are the descendants of the root node.
There is only one path exists between two nodes for the data transmission. Thus, it forms a parent-child hierarchy.
Reference:
https://www.geeksforgeeks.org/difference-between-physical-and-logical-topology/
https://www.javatpoint.com/computer-network-topologies

## Slide 549: Types of Network Topology
Mesh topology
Mesh technology is an arrangement of the network in which computers are interconnected with each other through various redundant connections.
There are multiple paths from one computer to another computer.
Image Source: https://www.javatpoint.com/computer-network-topologies
Notes: Mesh technology is an arrangement of the network in which computers are interconnected with each other through various redundant connections.
There are multiple paths from one computer to another computer.
It does not contain the switch, hub or any central computer which acts as a central point of communication.
The Internet is an example of the mesh topology.
Mesh topology is mainly used for WAN implementations where communication failures are a critical concern.
Mesh topology is mainly used for wireless networks.
Mesh topology can be formed by using the formula:
Number of cables = (n*(n-1))/2;
Where n is the number of nodes that represents the network.
Reference:
https://www.geeksforgeeks.org/difference-between-physical-and-logical-topology/
https://www.javatpoint.com/computer-network-topologies

## Slide 550: Types of Network Topology
Hybrid Topology
The combination of various different topologies is known as Hybrid topology.
A Hybrid topology is a connection between different links and nodes to transfer the data.
Image Source: https://www.javatpoint.com/computer-network-topologies
Notes: The combination of various different topologies is known as Hybrid topology.
A Hybrid topology is a connection between different links and nodes to transfer the data.
When two or more different topologies are combined together is termed as Hybrid topology and if similar topologies are connected with each other will not result in Hybrid topology. For example, if there exist a ring topology in one branch of ICICI bank and bus topology in another branch of ICICI bank, connecting these two topologies will result in Hybrid topology.
Reference:
https://www.geeksforgeeks.org/difference-between-physical-and-logical-topology/
https://www.javatpoint.com/computer-network-topologies

## Slide 551: Asynchronous & Synchronous Transmission
Synchronous Transmission
In Synchronous Transmission, data is sent in form of blocks or frames.
This transmission is the full duplex type.
Image Source: https://www.guru99.com/difference-between-synchronous-and-asynchronous-transmission.html
Notes: In Synchronous Transmission, data is sent in form of blocks or frames. This transmission is the full duplex type. Between sender and receiver the synchronization is compulsory. In Synchronous transmission, There is no gap present between data. It is more efficient and more reliable than asynchronous transmission to transfer the large amount of data.
Reference:
https://www.geeksforgeeks.org/difference-between-synchronous-and-asynchronous-transmission/
https://www.guru99.com/difference-between-synchronous-and-asynchronous-transmission.html

## Slide 552: Asynchronous & Synchronous Transmission
Asynchronous Transmission
In Asynchronous Transmission, data is sent in form of byte or character.
This transmission is the half duplex type transmission.
Image Source: https://www.guru99.com/difference-between-synchronous-and-asynchronous-transmission.html
Notes: In Asynchronous Transmission, data is sent in form of byte or character. This transmission is the half duplex type transmission. In this transmission start bits and stop bits are added with data. It does not require synchronization.
Reference:
https://www.geeksforgeeks.org/difference-between-synchronous-and-asynchronous-transmission/
https://www.guru99.com/difference-between-synchronous-and-asynchronous-transmission.html

## Slide 553
Different types of
Protocols
Notes: Title - The learning outcome
Subtitle - Duration

## Slide 554
Definitions
Definition 1: A protocol is a standard set of rules that allow electronic devices to communicate with each other.
Definition 2: A protocol is a set of guidelines to govern the data transfer between the devices.
Image Source: https://upload.wikimedia.org/wikipedia/commons/thumb/0/0d/Protocol_architecture.svg/220px-Protocol_arc
Different types of protocols
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 555
Introduction
It provides a full transport layer services to applications.
TCP is a connection oriented protocol and offers end-to-end packet delivery. It acts as back bone for connection
TCP is a reliable protocol as it detects the error and retransmits the damaged frames.
Image Source: https://lh3.googleusercontent.com/proxy/MmQAe8LlPH97fO51WtYBRv6hMEL4GNj-QprSgwN8WXL_zGga4j
Transmission Control Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 556
Transmission Control Protocol Offers
Stream Data Transfer.
Reliability.
Efficient Flow Control
Full-duplex operation.
Multiplexing.
TCP offers connection oriented
Image Source: https://lh3.googleusercontent.com/proxy/MmQAe8LlPH97fO51WtYBRv6hMEL4GNj-QprSgwN8WXL_zGga4j
Transmission Control Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 557
Image Source: https://lh3.googleusercontent.com/proxy/MmQAe8LlPH97fO51WtYBRv6hMEL4GNj-QprSgwN8WXL_zGga4j
Transmission Control Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 558
Benefits
It is an Open standard and is independent of hardware and software manufacturer.
It can send data between different computer systems running completely through Operating system.
It is separated from the underlying hardware and it will run over Ethernet, tokens ring and even over dial-up
Image Source: https://lh3.googleusercontent.com/proxy/MmQAe8LlPH97fO51WtYBRv6hMEL4GNj-QprSgwN8WXL_zGga4j
Transmission Control Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 559
Introduction
Internet Protocol is connectionless and unreliable protocol. It ensures no guarantee of successfully transmission of data.
In order to make it reliable, it must be paired with reliable protocol such as TCP at the transport layer.
Image Source: https://networkencyclopedia.com/wp-content/uploads/2019/09/internet-protocol-in-tcp-ip.jpg
Internet Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 560
Image Source: https://upload.wikimedia.org/wikipedia/commons/thumb/c/c4/IP_stack_connections.svg/350px-IP_stack_co
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 561
Image Source: htthttps://upload.wikimedia.org/wikipedia/commons/thumb/3/3b/UDP_encapsulation.svg/1024px-UDP_enca
Internet Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 562
Image Source: htthttps://upload.wikimedia.org/wikipedia/commons/thumb/3/3b/UDP_encapsulation.svg/1024px-UDP_enca
Internet Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 563
Image Source: https://www.w3.org/People/Frystyk/thesis/tcp.gif
Internet Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 564
Points to remember
The length of datagram is variable.
The Datagram is divided into two parts: header and data.
The length of header is 20 to 60 bytes.
The header contains information for routing and delivery of the packet.
Image Source: https://www.w3.org/People/Frystyk/thesis/tcp.gif
Internet Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 565
Introduction
User Datagram Protocol (UDP) is a Transport Layer protocol. UDP is a part of the Internet Protocol suite, referred to as UDP/IP suite.
Though Transmission Control Protocol (TCP) is the dominant transport layer protocol used with most of the Internet services; provides assured delivery, reliability, and much more but all these services cost us additional overhead and latency.
Image Source: https://media.geeksforgeeks.org/wp-content/uploads/UDP-header.png
User Datagram Protocol (UDP)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 566
Header
Source Port: Source Port is a 2 Byte long field used to identify the port number of the source.
Destination Port: It is a 2 Byte long field, used to identify the port of the destined packet.
Image Source: https://media.geeksforgeeks.org/wp-content/uploads/UDP-header.png
User Datagram Protocol (UDP)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 567
Header
Length: Length is the length of UDP including the header and the data. It is a 16-bits field.
Checksum: Checksum is 2 Bytes long field. It is the 16-bit one’s complement of the one’s complement sum of the UDP header, the pseudo-header of information from the IP header, and the data, padded with zero octets at the end (if necessary) to make a multiple of two octets.
Image Source: https://media.geeksforgeeks.org/wp-content/uploads/UDP-header.png
User Datagram Protocol (UDP)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 568
Introduction
The POP protocol stands for Post Office Protocol. As we know that SMTP is used as a message transfer agent.
When the message is sent, then SMPT is used to deliver the message from the client to the server and then to the recipient server.
Image Source: https://static.javatpoint.com/tutorial/computer-network/images/pop-protocol.png
POP Protoco
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 569
Working of the POP3 protocol
To establish the connection between the POP3 server and the POP3 client, the POP3 server asks for the user name to the POP3 client.
If the username is found in the POP3 server, then it sends the ok message.
It then asks for the password from the POP3 client; then the POP3 client sends the password to the POP3 server.
Image Source: https://static.javatpoint.com/tutorial/computer-network/images/pop-protocol2.png
POP Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 570
Working of the POP3 protocol
If the password is matched, then the POP3 server sends the OK message, and the connection gets established.
After the establishment of a connection, the client can see the list of mails on the POP3 mail server.
In the list of mails, the user will get the email numbers and sizes from the server. Out of this list, the user can start the retrieval of mail.
Image Source: https://static.javatpoint.com/tutorial/computer-network/images/pop-protocol2.png
POP Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 571
Introduction
HTTP is a communication protocol. It defines mechanism for communication between browser and the web server.
HTTP request comprises of lines which contains:
  Request line
  Header Fields
Image Source: https://www.ntu.edu.sg/home/ehchua/programming/webprogramming/images/HTTP.png
Hypertext Transfer Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 572
Key Points
The first line i.e. the Request line specifies the request method i.e. Get or Post.
The second line specifies the header which indicates the domain name of the server from where index.htm is retrieved.
Image Source: https://www.ntu.edu.sg/home/ehchua/programming/webprogramming/images/HTTP.png
Hypertext Transfer Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 573
Key Points
HTTP Response
  Like HTTP request, HTTP response also has certain structure. HTTP response contains:
  Status line
  Headers
Message body
Image Source: https://www.ntu.edu.sg/home/ehchua/programming/webprogramming/images/HTTP.png
Hypertext Transfer Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 574
Introduction
Hypertext Transfer Protocol Secure (HTTPS) is an extension of the Hypertext Transfer Protocol (HTTP). It is used for secure communication over a computer network, and is widely used on the Internet.
In HTTPS, the communication protocol is encrypted using Transport Layer Security (TLS) or, formerly, Secure Sockets Layer (SSL).
Image Source: https://www.edhotels.com/wp-content/uploads/2020/04/Difference-Between-HTTP-and-HTTPS.png
Hypertext Transfer Protocol
Secure
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 575
Advantages
User Data is Encrypted
You’ll Enjoy Better SEO
Protects your website from Phishing
Image Source: https://www.researchgate.net/profile/S_Dormido/publication/232652131/figure/fig5/AS:300619400269833@
Hypertext Transfer Protocol
Secure
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 576
Advantages
Authentication of the accessed website, and protection of the privacy and integrity of the exchanged data while in transit.
It protects against man-in-the-middle attacks, and the bidirectional encryption of communications between a client and server protects the communications against eavesdropping and tampering.
Image Source: https://www.researchgate.net/profile/S_Dormido/publication/232652131/figure/fig5/AS:300619400269833@
Hypertext Transfer Protocol
Secure
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 577
Limitations
SSL/TLS does not prevent the indexing of the site by a web crawler
SSL (Secure Sockets Layer) and TLS (Transport Layer Security) encryption can be configured in two modes: simple and mutual.
Image Source: https://www.researchgate.net/profile/S_Dormido/publication/232652131/figure/fig5/AS:300619400269833@
Hypertext Transfer Protocol
Secure (SSL)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 578
Limitations
SSL 1.0 – never publicly released due to security issues.
SSL 2.0 – released in 1995. Deprecated in 2011. Has known security issues.
SSL 3.0 – released in 1996. Deprecated in 2015. Has known security issues.
Image Source: https://techdifferences.net/wp-content/uploads/2019/01/Difference-Between-SSL-and-TLS-1024x800.png
History of SSL and TLS
releases
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 579
Introduction
FTP is used to copy files from one host to another browser and the web server.
FTP creates two processes such as Control Process and Data Transfer Process at both ends i.e. at client as well as at server.
FTP establishes two different connections: one is for data transfer and other is for control information.
Image Source: https://blog.ipswitch.com/hs-fs/hubfs/ftp-diagram.png?width=750&height=378&name=ftp-diagram.png
File Transfer Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 580
Introduction
Control connection is made between control processes while Data Connection is made between
FTP uses port 21 for the control connection and Port 20 for the data connection.
Image Source: https://blog.ipswitch.com/hs-fs/hubfs/ftp-diagram.png?width=750&height=378&name=ftp-diagram.png
File Transfer Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 581
Image Source: https://www.tutorialspoint.com/internet_technologies/images/internet-ftp_model.jpg
File Transfer Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 582
Introduction
SMTP is a set of communication guidelines that allow software to transmit an electronic mail over the internet is called Simple Mail Transfer Protocol.
It is a program used for sending messages to other computer users based on e-mail addresses.
Image Source: https://serversmtp.com/wp-content/uploads/2018/02/what-is-an-smtp-server.png
Simple Mail Transfer Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 583
Introduction
It provides a mail exchange between users on the same or different computers, and it also supports:
It can send a single message to one or more recipients.
Sending message can include text, voice, video or graphics.
It can also send the messages on networks outside the internet
Image Source: https://serversmtp.com/wp-content/uploads/2018/02/what-is-an-smtp-server.png
Simple Mail Transfer Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 584
Simple Mail Transfer Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 585
Simple Mail Transfer Protocol
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 586
Introduction
OSI stands for Open Systems Interconnection. It has been developed by ISO – ‘International Organization of Standardization‘, in the year 1984.
Designed to show the flow of moving data from one software application of one computer to another software application of another computer.
Image Source: https://cdn.educba.com/academy/wp-content/uploads/2019/07/OSI-Model.png
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 587
Introduction
Open Systems Interconnection (OSI) model is the virtual model which describes the Concept of a computer system with the concern of internal structure and technology.
Image Source: https://cdn.educba.com/academy/wp-content/uploads/2019/07/OSI-Model.png
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 588
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 589
Physical Layer Functions
The lowest layer of the OSI reference model is the physical layer. It is responsible for the actual physical connection between the devices.
Bit synchronization
Bit rate control
Physical topologies and Transmission mode
Image Source: https://qph.fs.quoracdn.net/main-qimg-2187fc128c7d7fe4aaaba74d2c4c7300
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 590
Physical Layer Functions
Hub, Repeater, Modem, Cables are Physical Layer devices.
Network Layer, Data Link Layer and Physical Layer are also known as Lower Layers or Hardware Layers.
Image Source: https://qph.fs.quoracdn.net/main-qimg-2187fc128c7d7fe4aaaba74d2c4c7300
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 591
Data Link Layer (DLL) Functions
The data link layer is responsible for the node to node delivery of the message. The main function of this layer is to make sure data transfer is error-free from one node to another, over the physical layer.
Packet in Data Link layer is referred as Frame.
Image Source: https://electricalfundablog.com/wp-content/uploads/2018/09/3-Data-Link-Layer-in-OSI-Model.png
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 592
Data Link Layer (DLL) Functions
Data Link layer is handled by the NIC (Network Interface Card) and device drivers of host machines.
Switch & Bridge are Data Link Layer devices.
  Logical Link Control (LLC)
  Media Access Control (MAC)
Image Source: https://electricalfundablog.com/wp-content/uploads/2018/09/3-Data-Link-Layer-in-OSI-Model.png
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 593
Data Link Layer (DLL) Functions
Framing
Physical addressing
Error control
Flow Control
Access control
Image Source: https://ars.els-cdn.com/content/image/3-s2.0-B9780123821966000029-f02-31-9780123821966.jpg
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 594
Data Link Layer (DLL) Functions
Packet in Data Link layer is referred as Frame.
Data Link layer is handled by the NIC (Network Interface Card) and device drivers of host machines.
Switch & Bridge are Data Link Layer devices.
Image Source: https://ars.els-cdn.com/content/image/3-s2.0-B9780123821966000029-f02-31-9780123821966.jpg
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 595
Network Layer Functions
Network layer works for the transmission of data from one host to the other located in different networks. It also takes care of packet routing.
Routing: The network layer protocols determine which route is suitable from source to destination.
Logical Addressing
Image Source: https://fossbytes.com/wp-content/uploads/2016/04/network-layer-osi-model.jpg
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 596
Network Layer Functions
Segment in Network layer is referred as Packet.
Network layer is implemented by networking devices such as routers.
Image Source: https://fossbytes.com/wp-content/uploads/2016/04/network-layer-osi-model.jpg
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 597
Transport Layer Functions
Service provided by transport layer
Connection Oriented Service: It is a three-phase process which include
– Connection Establishment – Data Transfer
– Termination / disconnection Connection less service: It is a one-phase process and includes Data Transfer
Image Source: https://www.technologyuk.net/computing/computernetworks/internet/images/tcp_end_to_end_communicati
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 598
Transport Layer Functions
Data in the Transport Layer is called as Segments.
Transport layer is operated by the Operating System. It is a part of the OS and communicates with the Application Layer by making system calls.
Transport Layer is called as Heart of OSI model.
Image Source: https://www.technologyuk.net/computing/computernetworks/internet/images/tcp_end_to_end_communicati
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 599
Session Layer Functions
This layer is responsible for establishment of connection, maintenance of sessions, authentication and also ensures security.
Session establishment, maintenance and termination
Synchronization
Dialog Controller
Image Source:
https://images.slideplayer.com/26/8849149/slides/slide_2.jpg
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 600
Session Layer Functions
All the below 3 layers(including Session Layer) are integrated as a single layer in the TCP/IP model as “Application Layer”.
Implementation of these 3 layers is done by the network application itself. These are also known as Upper Layers or Software Layers.
Image Source:
https://images.slideplayer.com/26/8849149/slides/slide_2.jpg
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 601
Presentation Layer Functions
Presentation layer is also called the Translation layer.
The data from the application layer is extracted here and manipulated as per the required format to transmit over the network.
Translation.
Image Source:
https://static.docsity.com/documents_pages/2012/11/03/73287fb7f97f04abcee7ddaf02e6d49e.png
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 602
Presentation Layer Functions
Encryption/ Decryption
Compression: Reduces the number of bits that need to be transmitted on the network.
Image Source:
https://static.docsity.com/documents_pages/2012/11/03/73287fb7f97f04abcee7ddaf02e6d49e.png
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 603
Application Layer Functions
The functions of the Application layer are :
Network Virtual Terminal
FTAM-File transfer access and management
Mail Services
Directory Services
Image Source:
https://1.bp.blogspot.com/-COEWCeLXPH8/XV0SQahkDKI/AAAAAAAAAoQ/ZR0HtmlMt0sDtyEMO FXzyboPUxMCg48pQCLcBGAs/s1600/application%2Blayer.jpg
Open System
Interconnection Model(OSI)
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 604
Introduction
A media access method refers to the manner in which a computer terminal on a network gains and controls access to the network's physical medium such as a cable.
The prime objective of media access is to prevent data packets from colliding when two or more computer terminals on a network try to transmit data simultaneously over a network.
Image Source:
https://lh6.googleusercontent.com/v1XCMM7aMys/TXQjf_saj7I/AAAAAAAACF0/xiFNvKeGorU/s1600/Taxo nomy
Media Access Methods
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 605
Introduction
Given below are some of the common media access methods:
  CSMA/CD
  CSMA/CA
  Demand Priority
  Token Passing
Image Source:
https://lh6.googleusercontent.com/v1XCMM7aMys/TXQjf_saj7I/AAAAAAAACF0/xiFNvKeGorU/s1600/Taxo nomy
Media Access Methods
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 606
Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
This is a media access method which defines how the network places data on the cable and how it takes it off.
CSMA/CD specifies how bus topologies such as Ethernet handle transmission collisions.
It usually operates in two modes of Carrier Sense, Multiple Access and Collision Detection.
Image Source:
https://image.slidesharecdn.com/csmamohammedabuibaid-160701034304/95/carrier-sense-multiple-access-csma-11-638.jpg?cb=1467345036
Media Access Methods
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 607
Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
Carrier Sense means that each station on the LAN continually listens to (tests) the cable for the presence of a signal prior to transmitting.
Multiple Access means that there are many computers attempting to transmit and compete for the opportunity to send data (i.e., they are in contention).
Image Source:
https://image.slidesharecdn.com/csmamohammedabuibaid-160701034304/95/carrier-sense-multiple-access-csma-11-638.jpg?cb=1467345036
Media Access Methods
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 608
Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
Collision Detection means that when a collision is detected, the stations will stop transmitting and wait a random length of time before retransmitting the data.
Image Source:
https://image.slidesharecdn.com/csmamohammedabuibaid-160701034304/95/carrier-sense-multiple-access-csma-11-638.jpg?cb=1467345036
Media Access Methods
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 609
Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
CSMA/CA stands for Carrier-Sense Multiple Access with Collision Avoidance and is a media access method very similar to CSMA/CD.
The difference is that the CD (collision detection) is changed to CA (collision avoidance).
Image Source:
https://image.slidesharecdn.com/csmamohammedabuibaid-160701034304/95/carrier-sense-multiple-access-csma-14-638.jpg?cb=1467345036
Media Access Methods
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 610
Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
Instead of detecting and reacting to collisions, CSMA/CA tries to avoid them by having each computer signal its intention to transmit before actually transmitting.
In effect, the transmitting computer gives a “Request” prior to transmitting.
Image Source:
https://image.slidesharecdn.com/csmamohammedabuibaid-160701034304/95/carrier-sense-multiple-access-csma-14-638.jpg?cb=1467345036
Media Access Methods
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 611
Token Passing
Token passing is a media access method by which collisions are prevented.
Collisions are eliminated under token passing because only a computer that possesses a free token (a small data frame) is allowed to transmit.
The token passing method also allows different priorities to be assigned to different stations on the ring.
Image Source:
https://images.slideplayer.com/16/5013077/slides/slide_10.jpg
Media Access Methods
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 612
Token Passing
Transmissions from stations with higher priority take precedence over stations with lower priority.
Token passing works best in an environment where a relatively large number of shorter data frames are being transmitted.
Image Source:
https://images.slideplayer.com/16/5013077/slides/slide_10.jpg
Media Access Methods
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 613
Token Passing
There are two common error conditions that can occur on a token passing LAN:
Constant Frame Error
A token cannot be acknowledged and continues to be passed around the ring.
b) Lost Token Error
A token is accidentally “hung up” or removed from the ring.
Image Source:
https://images.slideplayer.com/16/5013077/slides/slide_10.jpg
Media Access Methods
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 614
Demand Priority
Demand priority is the new Ethernet media access method that will probably replace the popular but older CSMA/CD method.
In demand priority, an active hub is an essential requirement that can control the access to the network.
Image Source:
https://onlinelibrary.wiley.com/cms/asset/70bc301f-349e-41bd-a976-bfcaf792ffcc/ett2869-toc-0001-m.jpg
Media Access Methods
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 615
Demand Priority
The terminals on a network are required to obtain permission from the hub before they start transmitting the bytes over a network.
Image Source:
https://onlinelibrary.wiley.com/cms/asset/70bc301f-349e-41bd-a976-bfcaf792ffcc/ett2869-toc-0001-m.jpg
Media Access Methods
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 616
Demand Priority
In this the terminals involved in communication can send and receive at the same time.
The transmission can be prioritized based on the requirements; for example, time sensitive data such as video can be given priority.
Image Source:
https://onlinelibrary.wiley.com/cms/asset/70bc301f-349e-41bd-a976-bfcaf792ffcc/ett2869-toc-0001-m.jpg
Media Access Methods
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 617
Difference
Media Access Methods
CSMA/CD | Token Passing
Used primarily by Ethernet LANs. | Used primarily by Token Ring LANs.
Works best in larger networks with relatively fewer, longer data frames. | Works best in small to medium size networks with many short data frames
Does not allow different priorities to be assigned to stations. | Allows different priorities to be assigned to stations.
Normally less expensive than token passing. | Normally more expensive than CSMA/CD.
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 618
Introduction
Domain Name System (DNS) is an Internet service that translates the domain names into IP addresses, which computer can understand.
Every device connected to the internet has a unique IP address which other machines use to find the device.
Image Source:
https://www.eternalsoftsolutions.com/blog/wp-content/uploads/2019/02/how_dns_works.png
DNS Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 619
DNS Records
Records | Description | Function
A | Address Record | It returns a 32bit IP addresses. This is where the actual Website is redirected towards most commonly.
CNAME | Canonical Name Record | This is an Alias. The DNS Server will continue to lookup with this new name.
DNAME | Delegation Name | This again is an alias for a name and also its subname, unlike CNAME, which is only an alias for itself. But similar to CNAME, the DNS Server tries to lookup with this new name as well.
DNSKEY | DNS KEY Record | There is another record known as KEY record which I haven’t mentioned here. The format of DNSKEY is same as the KEY, and is used in DNSSEC (more in description).
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 620
DNS Records
Records | Description | Function
LOC | Location Record | This provides the geographical location depending upon the domain name.
MX | Mail Exchange Record | This is related to the email routing which I mentioned previously. This maps the domain name with the email ID.
NS | Name Server Record | Provides a DNS ZONE to authorized name servers.
TKEY | Secret Key Record | This is the Key used with TSIG which is encrypted under Public Key.
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 621
DNS Records
Records | Description | Function
TSIG | Transaction Signature | This is used to authenticate updates coming from an approved source or name server. It is used along with TKEY.
TXT | Text Record | This file provides machine data related to frameworks and encryption.
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 622
There are 4 DNS servers involved in loading a webpage:
DNS recursor - The DNS recursor is a server designed to receive queries from client machines through applications such as web browsers.
Root nameserver - The root server is the first step in translating (resolving) human readable host names into IP addresses
Image Source:
https://d1.awsstatic.com/Route53/how-route-53-routes-traffic.8d313c7da075c3c7303aaef32e89b5d0b7885
DNS Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 623
There are 4 DNS servers involved in loading a webpage:
TLD nameserver - The top level domain server (TLD) ,This nameserver is the next step in the search for a specific IP address, and it hosts the last portion of a hostname (In example.com, the TLD server is “com”).
Image Source:
https://d1.awsstatic.com/Route53/how-route-53-routes-traffic.8d313c7da075c3c7303aaef32e89b5d0b7885
DNS Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 624
There are 4 DNS servers involved in loading a webpage:
Authoritative nameserver - If the authoritative name server has access to the requested record, it will return the IP address for the requested hostname back to the DNS Recursor (the librarian) that made the initial request.
Image Source:
https://www.internetsociety.org/wp-content/uploads/2019/02/dnsprivacy1.gif
DNS Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 625
Image Source:
https://www.internetsociety.org/wp-content/uploads/2019/02/dnsprivacy1.gif
DNS Lookup Process
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 626
Introduction
Dynamic Host Configuration Protocol (DHCP) is a network management protocol used to dynamically assign an Internet Protocol (IP) address to any device, or node, on a network so they can communicate using IP.
The DHCP client will demand an IP address by broadcasting a DHCP Discover message to the local subnet.
Image Source:
https://ars.els-cdn.com/content/image/1-s2.0-S0045790612001140-fx1.jpg
DHCP Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 627
Image Source:
https://networkencyclopedia.com/wp-content/uploads/2019/08/configuring-dhcp-scope.jpg
DHCP Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 628
DHCP Process
1. DHCPDISCOVER: The client broadcasts a request for a DHCP server.
2. DHCPOFFER: DHCP servers on the network offer an address to the client.
3. DHCPREQUEST: The client broadcasts a request to lease an address from one of the offering DHCP servers.
Image Source:
https://networkencyclopedia.com/wp-content/uploads/2019/08/dhcp.jpg
DHCP Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 629
DHCP Process
4. DHCPACK: The DHCP server that the client responds to acknowledges the client, assigns it any configured DHCP options, and updates its DHCP database. The client then initializes and binds its TCP/IP protocol stack and can begin network communication.
Image Source:
https://networkencyclopedia.com/wp-content/uploads/2019/08/dhcp.jpg
DHCP Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 630
Introduction
Windows Internet Name Service, or WINS, is a Microsoft Windows service that dynamically registers NetBIOS names of computers on the network.
The Windows Internet Naming Service (WINS) converts the NetBIOS host names into IP addresses.
Image Source:
https://networkencyclopedia.com/wp-content/uploads/2019/09/wins-windows-internet-name-service.jpg
Windows Internet Name
Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 631
Introduction
It allows the Windows machines on a given LAN segment to recognize Windows machines on other LAN segments.
It was designed specifically to support NetBIOS over TCP/IP (NetBT)
Image Source:
https://networkencyclopedia.com/wp-content/uploads/2019/09/wins-windows-internet-name-service.jpg
Windows Internet Name
Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 632
Advantages
In order for NetBIOS hosts (servers and clients running pre-Windows 2000 versions of Microsoft Windows) to communicate on a network, their NetBIOS names must first be resolved into IP addresses. WINS servers perform this task.
Image Source:
https://networkencyclopedia.com/wp-content/uploads/2019/09/wins-windows-internet-name-service.jpg
Windows Internet Name
Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 633
Advantages
Directed traffic to WINS servers generates less network traffic than broadcasts.
WINS provides a mechanism for browsing network resources across multiple domains and subnets.
The WINS database of NetBIOS name to IP address mappings is dynamically maintained, eliminating the need for lmhosts files on clients.
Image Source:
https://networkencyclopedia.com/wp-content/uploads/2019/09/wins-windows-internet-name-service.jpg
Windows Internet Name
Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 634
Example
In this example, the following occurs:
A WINS client, HOST-A, registers any of its local NetBIOS names with WINS-A, its configured WINS server.
Another WINS client, HOST-B, queries WINS-A to locate the IP address for HOST-A on the network.
WINS-A replies with the IP address for HOST-A, 192.168.1.20.
Image Source:
https://networkencyclopedia.com/wp-content/uploads/2019/09/windows-internet-name-service-wins.gif
Windows Internet Name
Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 635
Introduction
A remote access service (RAS) is any combination of hardware and software to enable the remote access tools or information that typically reside on a network of IT devices.
A remote access service connects a client to a host computer, known as a remote access server.
Image Source:
https://slideplayer.com/slide/14892336/91/images/2/Remote+Access+Just+another+computer+on+t he+network.+Functions+as+if+it+was+on+the+LAN..jpg
Remote Access Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 636
Introduction
RAS is arranged within an organization and directly connected with the organization's internal network and systems.
Image Source:
https://slideplayer.com/slide/14892336/91/images/2/Remote+Access+Just+another+computer+on+t he+network.+Functions+as+if+it+was+on+the+LAN..jpg
Remote Access Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 637
Introduction
A remote access server (RAS) is a type of server that provides a suite of services to remotely connected users over a network or the Internet.
It operates as a remote gateway or central server that connects remote users with an organization's internal local area network (LAN).
Image Source:
https://slideplayer.com/slide/14892336/91/images/2/Remote+Access+Just+another+computer+on+t he+network.+Functions+as+if+it+was+on+the+LAN..jpg
Remote Access Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 638
Introduction
RAS is a service that allows remote clients to connect to the server over a modem using a RAS-based protocol such as the Serial Line Internet Protocol (SLIP) or the newer Point-to-Point Protocol (PPP).
Image Source:
https://slideplayer.com/slide/14892336/91/images/2/Remote+Access+Just+another+computer+on+t he+network.+Functions+as+if+it+was+on+the+LAN..jpg
Remote Access Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 639
Introduction
PPP can run with network protocols such as TCP/IP, IPX/SPX, and NetBEUI; SLIP only supports TCP/IP.
Examples : Team Viewer, Ammyy software
Image Source:
https://slideplayer.com/slide/14892336/91/images/2/Remote+Access+Just+another+computer+on+t he+network.+Functions+as+if+it+was+on+the+LAN..jpg
Remote Access Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 640
Image Source:
https://slideplayer.com/slide/14892336/91/images/2/Remote+Access+Just+another+computer+on+t he+network.+Functions+as+if+it+was+on+the+LAN..jpg
Remote Access Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 641
Introduction
Web service is a standardized medium to circulate communication between the client and server applications on the World Wide Web.
A web service is a software module that is designed to perform a certain set of tasks.
Image Source:
Source:https://documentation.alphasoftware.com/pages/Guides/Services/Web%20Service%20Clients/imag es/WebServicesSimple.jpg
Web Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 642
Web Services Architecture
Provider
Requestor
Broker - The broker is nothing but the application which provides access to the UDDI. The UDDI, as discussed in the earlier topic enables the client application to locate the web service.(UDDI stands for Universal Description, Discovery, and Integration.)
Image Source:
https://www.guru99.com/images/3-2016/032316_0646_Webservicea3.png
Web Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 643
Types of Web Services
There are mainly two types of web services.
SOAP stands for Simple Object Access Protocol
SOAP a XML-based protocol for accessing web services
SOAP is platform and language independent
SOAP is a W3C recommendation for communication between two applications
Image Source:
https://documentation.alphasoftware.com/pages/Guides/Services/Web%20Service%20Clients/images/WebServicesOverview.jpg
Web Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 644
Types of Web Services
Image Source:
https://documentation.alphasoftware.com/pages/Guides/Services/Web%20Service%20Clients/images/WebServicesOverview.jpg
Web Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 645
Types of Web Services
REST stands for Representational State Transfer. REST is an architectural style not a protocol.
Restful Web Service is a lightweight, maintainable, and scalable service that is built on the REST architecture.
Restful Web Service, expose API from your application in a secure, uniform, stateless manner to the calling client.
Image Source:
https://res.cloudinary.com/practicaldev/image/fetch/s--FkyXorEz--/c_limit%2Cf_auto%2Cfl_progressive%2Cq_auto%2Cw_880/https://thepracticaldev.s3.amazonaws.com/i/ueg7okh8thprev2cay9s.jpg
Web Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 646
Types of Web Services
Image Source:
https://documentation.alphasoftware.com/pages/Guides/Services/Web%20Service%20Clients/images/WebServicesOverview.jpg
Web Service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 647
Web Service
Advantages
Type | Advantages | Description
SOAP | Security | SOAP defines its own security known as WS Security
 | Language and Platform independent | SOAP web services can be written in any programming language and executed in any platform
RESTful | Fast | RESTful Web Services are fast
 | Language and Platform independent | It is also language and platform independent
 | Can use SOAP | RESTful web services can use SOAP web services as the implementation
 | Permits different data format | RESTful web service permits different data format such as Plain Text, HTML, XML and JSON
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 648
Web Service
Disadvantages
Disadvantages | Description
Slow | SOAP uses XML format that must be parsed to be read. It defines many standards that must be followed while developing the SOAP applications. So it is slow and consumes more bandwidth and resource.
WSDL Dependent | SOAP uses WSDL and doesn't have any other mechanism to discover the service
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 649
Introduction
Monitoring and Filtering
Proxy servers allow us to do several kind of filtering such as:
Content Filtering
Filtering encrypted data
Bypass filters
Logging and eavesdropping
Image Source:
https://www.temok.com/blog/wp-content/uploads/2019/08/Featured.jpg
Disadvantages
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 650
Image Source:
https://www.google.com/url?sa=i&url=https%3A%2F%2Fen.wikipedia.org%2Fwiki%2FProxy_server&psig=
How Proxy Server Works
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 651
Forward Proxy
In this the client requests its internal network server to forward to the internet.
Image Source:
https://www.tutorialspoint.com/internet_technologies/images/internet-forward_proxy.jpg
Types of proxy servers
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 652
Open Proxy
Open Proxies helps the clients to conceal their IP address while browsing the web.
Image Source:
https://www.tutorialspoint.com/internet_technologies/images/internet-open_proxy.jpg
Types of proxy servers
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 653
Reverse Proxy
In this the requests are forwarded to one or more proxy servers and the response from the proxy server is retrieved as if it came directly from the original Server.
Image Source:
https://www.tutorialspoint.com/internet_technologies/images/internet-reverse_proxy.jpg
Types of proxy servers
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 654: Install & configure the different types of network devices in a network
15 Hours
Notes: Title - Able to Install and configure Linux server environment
Subtitle – 15 hours

## Slide 655: In this section, we will discuss:
Functions of Network Interface Card (NIC)
Repeaters
Hub
Switches
Routers
Bridges.
Internet Service Provider
Notes: Mention the parent topics one by one. This particular learning outcome has 4 parent topics.

## Slide 656: Network Devices
Functions of Network Interface Card (NIC)
It is an electronic device that joins a computer to a computer network, usually a LAN.
The NIC contains the electronic circuitry required to connect using a wired connection (e.g., Ethernet) or a wireless connection (e.g., WiFi).
Image Source: https://techterms.com/definition/nic
Notes: Reference:
https://www.kencorner.com/network-devices/

## Slide 657: Network Devices
Repeaters
Repeaters receive network signals on one port, amplify them, and repeat them out the other port.
Since they operate only at the Physical layer of the OSI model, repeaters can intersect different media types but cannot convert protocols.
The purpose of a repeater is to extend the maximum distance of a single network segment.
Image Source: https://www.tp-link.com/ae/support/faq/151/
Notes: Reference:
https://www.kencorner.com/network-devices/

## Slide 658: Network Devices
Hub
A hub (also called a concentrator) serves as a central joining point for several network devices.
At a basic level, a hub is nothing more than a multiport repeater.
A hub repeats what it obtains on one port to all other ports.
Image Source: https://www.lynda.com/Windows-Server-tutorials/Exploring-hubs/408231/435884-4.html
Notes: Reference:
https://www.kencorner.com/network-devices/

## Slide 659: Network Devices
Types of hub
Active Hub – It is usually powered and amplifies and cleans up the signal it receives, thus doubling the effective segment distance limitation for the specific topology.
Passive Hub – Typically it is unpowered and makes only physical, electrical connections. Usually, the maximum segment distance of a topology is shortened because the hub takes some power away from the signal strength in order to do its job.
Image Source: https://www.slideshare.net/patelgopal1044/network-d
Notes: Reference:
https://www.kencorner.com/network-devices/

## Slide 660: Switches
What is a Switch
Switches are key building blocks for any network.
They can connect multiple devices such as computers , printers , access points & servers etc. on same network within a building or campus .
Image Source: https://www.indiamart.com/proddetail/networking-switches-dlink-and-digisol-11032831233.html
Notes: Reference:
https://www.cisco.com/c/en_in/solutions/small-business/resource-center/networking/network-switch-how.html

## Slide 661: Switches
Role of switches in networking
Switching in a computer network is achieved by using switches.
Network switches operates at layer 2 (Data Link Layer) in the OSI Model
It is operated in a full duplex mode.
Image Source: https://www.indiamart.com/proddetail/networking-switches-dlink-and-digisol-11032831233.html
Notes: Reference:
https://www.javatpoint.com/computer-network-switching

## Slide 662: Switches
Types of switches (Unmanaged Switches)
These are the switches that are used in home networks and small businesses.
They do not need to be configured as they work on home /small networks .
They require small cabling and they are least expensive too.
Image Source: https://www.netgear.com/business/products/switches/unmanaged/
Notes: Reference:
https://www.geeksforgeeks.org/types-of-switches-in-computer-network/

## Slide 663: Switches
Types of switches (Managed Switches)
These are the switches used in large organizations containing a large network.
These are costly but their scalability makes them an ideal option for a network that is going.
They are achieved by setting a simple network management protocol(SNMP)
Image Source: https://www.netgear.com/business/products/switches/unmanaged/
Notes: Reference:
https://www.geeksforgeeks.org/types-of-switches-in-computer-network/

## Slide 664: Switches
Types of switches (LAN Switches)
These are also known as Ethernet switches or Data switches.
They are used to reduce network congestion or bottleneck by distributing a package of data only to its intended recipient
Image Source: https://www.netgear.com/business/products/switches/unmanaged/
Notes: Reference:
https://www.geeksforgeeks.org/types-of-switches-in-computer-network/

## Slide 665: Switches
Types of switches (PoE Switches)
PoE switches are used in PoE technology which stands for Power over Ethernet.
Technology that integrate data and power on the same cable allowing power devices to receive data in parallel to power
Image Source: https://www.wifi-stock.com/details/zq-poes-8-7.html/products/switches/unmanaged/
Notes: Reference:
https://www.geeksforgeeks.org/types-of-switches-in-computer-network/

## Slide 666: Switches
Advantages of switching
Increases the bandwidth of the network.
Reduces the workload of individual PC as it sends the information to only that device which has been addressed.
Increases the overall performance of the network by reducing the traffic on the network.
Image Source: https://www.indiamart.com/proddetail/networking-switches-dlink-and-digisol-11032831233.html
Notes: Reference:
https://www.javatpoint.com/computer-network-switching

## Slide 667: Switches
Disadvantages of switching
It is expensive as compared to network bridges.
It cannot determine the network connectivity issues easily.
Proper designing and configuration of the switches are required to handle multicast packets
Image Source: https://www.indiamart.com/proddetail/networking-switches-dlink-and-digisol-11032831233.html
Notes: Reference:
https://www.javatpoint.com/computer-network-switching

## Slide 668: Routers
What is a Router
The Router is a physical or virtual internetworking device that is designed to receive, analyze, and forward data packets between computer networks.
Some popular companies that develop routers are cisco , ibm , hp , asus , juniper d-link etc.
Image Source: https://www.lifewire.com/what-is-a-router-2618162
Notes: Reference:
https://www.javatpoint.com/router

## Slide 669: Routers
What is a Router
Is used in LAN and WAN Environments.
It shares information with other routers. in networking
It uses the RIP(Routing Information Protocol) to transfer the data across the network.
It is more expensive than other network devices like switches and hubs.
Image Source: https://www.lifewire.com/what-is-a-router-2618162
Notes: Reference:
https://www.javatpoint.com/router

## Slide 670: Routers
Features of Routers
A router works on the third layer (network layer) of OSI model
It allows the users to connect to several LAN and WAN .
Routers are capable of routing the traffic in a large networking system by subnetting .
Routers provide the redundancy as it always works in master and slave mode.
Image Source: https://www.lifewire.com/what-is-a-router-2618162
Notes: Reference:
https://www.javatpoint.com/router

## Slide 671: Routers
Types of Routers (Wireless Router)
They used to offer a wifi connectivity to laptop , smartphones and other devices.
Wireless routers are capable of generating a wireless signal in your home or office.
If the connection is indoors , the range of wireless router is 150 feet and when the connection is outdoors ,the range is upto 300 feet.
Image Source: https://www.lifewire.com/what-is-a-router-2618162
Notes: Reference:
https://www.javatpoint.com/router

## Slide 672: Routers
Types of Routers (BRouter)
It is the combination of bridge and the router.
It allows the transferring the data between network like a bridge and like a router , it can also route the data within the network to the individual systems.
Image Source: https://www.lifewire.com/what-is-a-router-2618162
Notes: Reference:
https://www.javatpoint.com/router

## Slide 673: Routers
Types of Routers (Core Router)
It is a router that can route the data within a network, but it is not able to route the data between the networks.
It is a computer communication system device and the backbone of networks, as it helps to link all network devices.
It is used by Internet Service Providers (ISPs).
Image Source: https://www.lifewire.com/what-is-a-router-2618162
Notes: Reference:
https://www.javatpoint.com/router

## Slide 674: Routers
Types of Routers (Edge Router)
An edge router is a lower-capacity device that is placed at the boundary of a network.
It is also known as an access router.
It allows a internal network to connect to the external network.
It uses bgp(border gateway protocol) for communication.
Image Source: https://www.technodabbler.com/edge-router-x/
Notes: Reference:
https://www.javatpoint.com/router

## Slide 675: Routers
Types of Routers (Broadband Router)
Broadband routers are used to provide high speed internet access to computers.
It is needed when you connect to the internet through phone and use voice over IP technology (VOIP).
It is configured and provided by the Internet Service Provider (ISP).
Image Source: https://www.technodabbler.com/edge-router-x/
Notes: Reference:
https://www.javatpoint.com/router

## Slide 676: Routers
Advantages of Routers
Security
Performance enhancement
Reliability
Networking Range
Image Source: https://www.lifewire.com/what-is-a-router-2618162
Notes: Reference:
https://www.javatpoint.com/router

## Slide 677: Routers
Disadvantages of Routers
They operates on routable network protocols.
They are expensive.
They are slower as they need to analyse from layer 1 throw layer 3 of OSI model.
Image Source: https://www.lifewire.com/what-is-a-router-2618162
Notes: Reference:
https://www.javatpoint.com/router

## Slide 678: Bridges
What is bridges
A networking Bridge is a device that divides a network into the segments.
Each segment represent a separate collision domain , & each collision domain has its own separate bandwidth
A Bridge works at layer 2 (Data link layer) of the OSI Model.
Image Source: https://jackleachipt.wordpress.com/bridge/
Notes: Reference:
https://geek-university.com/ccna/what-is-a-network-bridge/

## Slide 679: Bridges
Types of bridges (Transparent Bridge)
It is an Invisible bridge in the computer network.
The main function of this bridge is to block or forward the data depending on the MAC address.
The other devices within the network are unaware of the existence of bridges.
Image Source: https://jackleachipt.wordpress.com/bridge/
Notes: Reference:
https://www.elprocus.com/what-is-a-bridge-in-computer-network-working-types-its-functions/

## Slide 680: Bridges
Types of bridges (Translational Bridge)
It plays a key role in changing a networking system from one type to another.
These bridges are used to connect two different networks like token ring and Ethernet.
This bridge can add or remove the data based on traveling direction, and fields from the frames as needed.
Image Source: https://jackleachipt.wordpress.com/bridge/
Notes: Reference:
https://www.elprocus.com/what-is-a-bridge-in-computer-network-working-types-its-functions/

## Slide 681: Bridges
Types of bridges (Source-Route Bridge)
It is a one type of technique used for token ring network and it is designed by IBM.
The total frame route is embedded in one frame so it allow the bridge to make precise decision of how the frame is forwarding using a network.
In this method two similar network segments are connected to data link layer.
Image Source: https://jackleachipt.wordpress.com/bridge/
Notes: Reference:
https://www.elprocus.com/what-is-a-bridge-in-computer-network-working-types-its-functions/

## Slide 682: Bridges
Functions of Bridges
It is used to divide the local area network into several segments.
In the osi model it works under the data link layer
It is used to store the address of MAC in PC used in a network.
Image Source: https://jackleachipt.wordpress.com/bridge/
Notes: Reference:
https://www.elprocus.com/what-is-a-bridge-in-computer-network-working-types-its-functions/

## Slide 683: Bridges
Advantages of Bridges
It acts as a repeater to extend a network.
Collisions can be reduced.
Bridges increases the available bandwidth to individual nodes.
It avoids waste bandwidth
The length of the network can be increased
Image Source: https://jackleachipt.wordpress.com/bridge/
Notes: Reference:
https://www.elprocus.com/what-is-a-bridge-in-computer-network-working-types-its-functions/

## Slide 684: Bridges
Disadvantages of Bridges
It is unable to read specific IP address because they are more troubled with the mac address.
They cannot help while building the network between the different architectures of network.
It does not handle more variable and complex data load which occurs from WAN.
Image Source: https://jackleachipt.wordpress.com/bridge/
Notes: Reference:
https://www.elprocus.com/what-is-a-bridge-in-computer-network-working-types-its-functions/

## Slide 685: Internet Service Provider
What is ISP
An Internet Service Provider (ISP) ia a company that provides customers with internet access.
An Internet Service Provider (ISP) is also known as Internet Access Provider (IAP).
ISPs also provide their customers with the ability to communicate with one another.
Image Source: https://www.javatpoint.com/isp-full-form/
Notes: Reference:
https://www.techopedia.com/definition/2510/internet-service-provider-isp
https://www.javatpoint.com/isp-full-form

## Slide 686: Internet Service Provider
Types of ISPs (Dial-up Internet Access)
It is the oldest technology to provide internet access by modem to modem connection using telephone lines.
This method has become outdated today due to slow connection speed.
Image Source: https://www.javatpoint.com/isp-full-form/
Notes: Reference:
https://www.javatpoint.com/isp-full-form

## Slide 687: Internet Service Provider
Types of ISPs (DSL)
DSL stands for ‘Digital Subscriber Line’ is an advanced version of Dial-up internet access method.
This method offers Asymmetric Digital Subscriber(ASDL), where upload speed is less than download speed, and Symmetric Digital Subscriber (SDSL), where upload and download speed are equal.
Image Source: https://www.javatpoint.com/isp-full-form/
Notes: Reference:
https://www.javatpoint.com/isp-full-form

## Slide 688: Internet Service Provider
Types of ISPs (Wireless Broadband)
WiBB is a modern broadband technology for internet access.
It allows high-speed wireless internet within a large area.
Image Source: https://www.javatpoint.com/isp-full-form/
Notes: Reference:
https://www.javatpoint.com/isp-full-form

## Slide 689: Internet Service Provider
Types of ISPs (Wifi Internet)
Wifi stands for ‘Wireless fidelity’.
It is a wireless networking technology that provides wireless high-speed internet connections using Radio waves.
It is commonly used in public places such as hotels, airports, restaurants, etc.
Image Source: https://www.javatpoint.com/isp-full-form/
Notes: Reference:
https://www.javatpoint.com/isp-full-form

## Slide 690: Internet Service Provider
Types of ISPs (ISDN)
ISDN stands for Integrated Services Digital Network.
It is a telephone system network which integrates a high quality digital transmission of voice and data over the same standard phone line.
Image Source: https://www.javatpoint.com/isp-full-form/
Notes: Reference:
https://www.javatpoint.com/isp-full-form

## Slide 691: Internet Service Provider
Types of ISPs (Ethernet)
It is a wired LAN (Local Area Network) where computers are connected within a primary physical space.
It enables devices to communicate with each other via a protocol (a set of rules or common network language).
It may provide different speed such as 10 Mbps, 100 Mbps and 10 Gbps.
Image Source: https://www.javatpoint.com/isp-full-form/
Notes: Reference:
https://www.javatpoint.com/isp-full-form

## Slide 692
© Edunet Foundation. All rights reserved.
Modern Network Security

## Slide 693: Modern Network Security
Why Internet Security
Cybersecurity refers to the practice of reducing cyber risk through the protection of the entire information technology (IT) infrastructure, including systems, applications, hardware, software, and data.
It is very important in today's world.
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 694: Modern Network Security
Importance of Cyber Security
Cyber-attacks (Unauthorized access to your Systems )
Data breaches (Exposure of sensitive business, customer, & supplier data)
Identity thefts (the theft of logins, passwords, and other sensitive, personally identifiable data)
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 695: Modern Network Security
Cyber Security Practise Areas
Data Security
Application Security
Network Security
Operational Security
Cloud Security
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 696: Modern Network Security
Cyber Security Practise Areas
Identity and Access Management(IAM)
Privileged Access Management(PAM)
Vulnerability Management (VM)
Enterprise Mobility Management (EMM)
Business Continuity (BC) and Disaster Recovery (DR).
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 697: Threats and the Basics of securing a network
Common Network Security Threats
Computer Viruses
DOS (Denial of service) attack
Trojan Horse
Adware and Spyware
Computer Worm
Phishing
Rootkit
SQL Injection attack
Malware
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 698: Threats and the Basics of securing a network
Cyber Security Best Practices
Audit your existing IT ecosystem
Complete a gap Analysis
Used a risk based approach to cyber security
Take the advantages of modern cyber security software
Implement robust identity and access management
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 699: Threats and the Basics of securing a network
Cyber Security Best Practices
Use privileged access management
Employ vulnerability scanning
Use of Cyber Security Frameworks
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 700: Threats and the Basics of securing a network
Network security Models
Firewalls
Antivirus Software
Passwords
Cryptography
Algorithms
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 701: Threats and the Basics of securing a network
Firewalls
A firewall is a software program or hardware that stops the hackers, viruses and worms that try to reach computer.
It scans every message and blocks that information that does not meet the security norms.
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 702: Threats and the Basics of securing a network
Benefits of Firewalls
Shield from Vulnerable services.
Logging and statistics on network usage, and misuse of it.
Policy enforcement.
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 703: Threats and the Basics of securing a network
Authentication
User Identification and Password.
A signed digital certificate or even a fingerprint.
User’s voice, hand configuration, fingerprint, etc.
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 704: Threats and the Basics of securing a network
Intrusion Detection System
Intrusion Detection System (IDS) are mainly concentrated on recognizing possible occurrences, logging information and reporting attempts.
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 705: Threats and the Basics of securing a network
Antivirus software
Antivirus software is a program or set of programs that are designed to prevent, search for, detect and remove software viruses and other malicious software like worms, trojans, adware, etc.
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 706: Threats and the Basics of securing a network
Benefits of Antivirus software
Scan specific files or directories.
Allows to schedule scans to automatically run for you.
Allows you to initiate scan of a particular file or entire computer or of a CD or flash drive at any time.
Removes any malicious code detected.
Show you the ‘health’ of your computer.
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 707: Threats and the Basics of securing a network
Some popular Antivirus software
Norton
Kaspersky
McAfee
BullGuard
Avast Antivirus
Panda Cloud Antivirus
Quick Heal Antivirus
AVG
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 708: Threats and the Basics of securing a network
Cryptography
The term cryptography means the concept of encryption and decryption together.
Cryptography is the method in which plain text message is encoded that is called ciphertext at the transmitters end, which is then conveyed to the receiver. The receiver then decrypts to get the original message back.
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 709: Threats and the Basics of securing a network
Techniques of Cryptography
Symmetric Key Cryptography : In this the significant component used is equal for both encoding and decoding.
Asymmetric Key Cryptography : In this the key element used is unlike for both encryption as well as decryption.
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 710: Threats and the Basics of securing a network
Some Populars Encryption Algorithms
Triple DES
RSA
Blowfish
Twofish
AES
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 711: Secure Administrative Access
Techniques for secure administrative access
Setting User modes passwords
Setting Privilege mode passwords
Encryption Passwords in config files
Setting access privilege levels
Restrict telnet to the Device
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 712: Secure Administrative Access
Techniques for secure administrative access
Restrict web browser access to the Device.
Restrict SNMP access to the Device.
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 713: Secure Administrative Access
User Mode Passwords
Console (con) port Access for the console cable. Figure shows a typical console port on a router.
Auxiliary (AUX) port A console-like access that can be attached to an external modem for a dial-up connection.
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 714: Secure Administrative Access
User Mode Passwords
Virtual terminal (vty) ports The access points for Telnet sessions.
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 715: Secure Administrative Access
Privilege Mode Passwords
1 User exec mode only (prompt is router>), the default level for login
15 Privileged exec mode (prompt is router#), the Enable mode
0 Seldom used, but includes five commands: disable, enable, exit, help, and logout
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 716: Secure Administrative Access
Privilege Mode Passwords
The Syntax is
privilege mode {level level command
| reset command}
Image Source: https://antivirus.comodo.com/blog/computer-safety/importance-of-internet-security/
© Edunet Foundation. All rights reserved.

## Slide 717: LAN Security Considerations.
Understand Types of Network Devices
To build a strong network and defend it, you need to understand the devices that comprise it. Here are the main types of network devices; viz. Hub, Switch, Router, Gateway
https://cdn.educba.com/academy/wp-content/uploads/2019/10/Types-of-Network-Devices.png
© Edunet Foundation. All rights reserved.

## Slide 718: LAN Security Considerations.
Know Network Defenses
Using the proper devices and solutions can help you defend your network. Here are the most common ones you should know about; Firewall, IDS, IPS, NAC, Web Filters, Load Balancers, Proxy Server, Anti DDoS, Spam Filter
https://securityintelligence.com/wp-content/uploads/2015/04/application.jpg
© Edunet Foundation. All rights reserved.

## Slide 719: LAN Security Considerations.
Segregate Your Network
Network segmentation
involves
segregating the network into logical or functional units called zones.
You can separate them using routers or switches or using virtual local area networks (VLANs), which you create by configuring a set of ports on a switch to behave like a separate network.
https://www.cdn.geeksforgeeks.org/wp-content/uploads/52555.png
© Edunet Foundation. All rights reserved.

## Slide 720: LAN Security Considerations.
© Edunet Foundation. All rights reserved.
Segregate Your Network (Continue)
Segmentation is also useful in data classification and data protection.
Virtualization is another way to segment a network.
Segmentation limits the potential damage of a compromise to whatever is in that one zone.

## Slide 721: LAN Security Considerations.
Segregate Your Network (Continue)
Types of Network Segments:
  Public Networks
  Semi-private Networks
  Private Networks
  Demilitarized Zone (DMZ)
Software-Defined Networking (SDN)
https://upload.wikimedia.org/wikipedia/commons/thumb/e/e8/VPN_overview-en.svg/330px-VPN_overview-e
© Edunet Foundation. An.lsl vrgig.phntsg reserved.

## Slide 722: LAN Security Considerations.
https://www.websense.com/content/support/library/deployctr/v78/images/na_multiple_segments.png
© Edunet Foundation. All rights reserved.
Place Your Security Devices Correctly
As you design your network segregation strategy, you need to determine where to place all your devices
To determine where to place other devices, you need to consider the rest of your network configuration

## Slide 723: LAN Security Considerations.
https://upload.wikimedia.org/wikipedia/commons/thumb/c/c7/NAT_Concept-en.svg/1200px-NAT_Concept-e
© Edunet Foundation. An.lsl vrgig.phntsg reserved.
Use Network Address Translation
Network address translation (NAT) enables organizations to compensate for
the address networking.
NAT translates
deficiency of IPv4
private addresses
(internal to a particular organization) into routable addresses on public networks such as the internet.

## Slide 724: LAN Security Considerations.
https://www.onlinecomputertips.com/images/networking/n146.jpg
© Edunet Foundation. All rights reserved.
Use Network Address Translation (Continue)
In particular, NAT is a method of connecting multiple computers to the internet (or any other IP network) using one IP address.
NAT complements firewalls to provide an extra measure of security for an organization’s internal network

## Slide 725: LAN Security Considerations.
https://anydifferencebetween.com/wp-content/uploads/2016/09/Difference-Between-Personal-Firewall-and-
© Edunet Foundation. ANelltrwigohrkt-sFirreeswearllv.pendg.
Don’t Disable Personal Firewalls
Personal firewalls are software-based firewalls installed on each computer in the network. They work in much the same way as larger border firewalls
Instead of disabling personal firewalls, simply configure a standard personal firewall according to your organization’s needs

## Slide 726: LAN Security Considerations.
https://techdocs.f5.com/kb/global/manual_images/MAN-0622-00_v5/GUID-5C04B3DD-5407-48DA-B07C-F
© Edunet Foundation. AE7ll8r5igAh6t5s5rDe2s1e-orvnelinde..png
Use Centralized Logging and Immediate Log Analysis
Record suspicious logins and other computer events and look for anomalies
This helps you reconstruct what happened during an attack
You can take steps to improve your threat detection process and quickly block attacks in the future

## Slide 727: LAN Security Considerations.
Use Web Domain Whitelisting
Limiting users to browsing only the websites you’ve explicitly approved helps in two ways
  First, it limits your attack surface
  Second, whitelisting limits hackers’ options for communication after they compromise a system
https://www.chorus.co/media/1346/whitelisting-blacklisting.png
© Edunet Foundation. All rights reserved.

## Slide 728: LAN Security Considerations.
Route Through a Proxy Server
All outbound web access should be routed through an authenticating server where access can be controlled and monitored
Using a web proxy helps ensure that an actual person, not an unknown program, is driving the outbound connection
https://www.seobility.net/en/wiki/images/8/8a/Proxy-Server.png
© Edunet Foundation. All rights reserved.

## Slide 729: LAN Security Considerations.
Use Honeypots and Honeynets
A Honeypot is a separate system that appears to be an attractive target but is in reality a trap for attackers
A Honeynet is the next logical extension of a honeypot — it is a fake network segment that appears to be a very enticing target
https://www.umangsoftware.com/wp-content/uploads/2019/08/honeypot_2.png
© Edunet Foundation. All rights reserved.

## Slide 730: LAN Security Considerations.
Protect Your Network from Insider Threats
To deal with insider threats, you need both prevention and detection strategies
The most important preventive measure is to establish and enforce the least-privilege principle for access management and access control
https://media.threatpost.com/wp-content/uploads/sites/103/2019/09/10155113/insider-threat.jpg
© Edunet Foundation. All rights reserved.

## Slide 731: LAN Security Considerations.
https://lh3.googleusercontent.com/proxy/CQHj5c84rlAv_hk62zwW3XZXbpCAvNWIZRifeTQ1e8xosDTwhEn
© Edunet Foundation. A8ilTl EridgmhYtseCrebsweKr5vceVdP. -Q9JA8Yah4n9lSEQeosf3EVR2-jM61kDEfAqnWcYKyhH63AdKN2kdN6u_Apu5yWZg
Monitor and Baseline Network Protocols
You should monitor the use of different protocol types on your network to establish baselines both the organization level and a user level

## Slide 732: LAN Security Considerations.
https://embed-fastly.wistia.com/deliveries/d108d6daa05c480eacfc817179f39db37f4c118c.webp?image_cro
© Edunet Foundation. Ap_llrerisgizhetsd=r1e2s8e0rxv7e2d0.
Use VPNs
A virtual private network (VPN) is a secure private network connection across a public network
With a VPN, the remote end appears to be connected to the network as if it were connected locally
To improve security, VPNs usually encrypt data

## Slide 733: LAN Security Considerations.
https://www.networkcomputing.com/sites/default/files/styles/flexslider_full/public/1-intro_9_0.jpg?itok=K1U7
© Edunet Foundation. AuKllmrizghts reserved.
Use Multiple Vendors
In addition to diversity of controls, you should strive for diversity of vendors
Each vendor uses the same malware detection algorithms in all its products, if your workstation, network and firewall antimalware solutions all come from vendor A, then anything missed by one product will be missed by all others

## Slide 734: LAN Security Considerations.
https://slideplayer.com/slide/12716983/76/images/1/IDS%2FIPS+Intrusion+Detection+System%2F+Intrusio
© Edunet Foundation. An+llPrriegvhetnstiroens+eSryvsetedm. .jpg
Use Your Intrusion Detection System Properly
To get the most value from your IDS, take advantage of both ways it can detect potentially malicious activities
  Anomaly Detection
  Misuse Detection

## Slide 735: LAN Security Considerations.
https://i.ytimg.com/vi/Lq7qd0sGw7E/maxresdefault.jpg
© Edunet Foundation. All rights reserved.
Automate Response to Attacks
Many network devices and software solutions can be configured to automatically take action when an alarm is triggered, which dramatically reduces response time.

## Slide 736: LAN Security Considerations.
© Edunet Foundation. All rights reserved.
Automate Response to Attacks (Continue)
Suggested Actions:
  Block IP
  Terminate Connection
  Collect additional information
  Look for the point of initial access
  Determine how malicious software
was deployed
https://www3.rocketsoftware.com/rocketd3/support/documentation/fc/38/Admin/fcsocketterminatebutton.png

## Slide 737: LAN Security Considerations.
https://www.tailorednetworks.com/images/easyblog_shared/January_2019/1-7-19/b2ap3_large_physical_s
© Edunet Foundation. Aecllurriitgyh_tosfferer_s4e0r0v.ejpdg.
Physically Secure Your Network Equipment
Physical controls should be established and security personnel should ensure that equipment and data do not leave the building.
Moreover, direct access to network equipment should be prohibited for unauthorized personnel.

## Slide 738: Network Security Devices
https://m.media-amazon.com/images/I/31ZROS8moRL._SR500,500_.jpg
© Edunet Foundation. All rights reserved.
Firewall
One of the first lines of defense in a network
A firewall isolates one network from another.
Firewalls either can be standalone systems or included in other devices
You can find both hardware and software firewall solutions

## Slide 739: Network Security Devices
https://www.thesecuritybuddy.com/data-breaches-prevention/what-is-ids-intrusion-detection-system-how-do
© Edunet Foundation. Aesll-irt-igwhotrsk/reserved.
Intrusion Detection System (IDS)
An IDS enhances cybersecurity by spotting a hacker or malicious software on a network so you can remove it promptly to prevent a breach or other problems
Use the data logged about the event to better defend against similar intrusion incidents in the future

## Slide 740: Network Security Devices
https://www.exabeam.com/wp-content/uploads/2019/01/ips_security.png
© Edunet Foundation. All rights reserved.
Intrusion prevention system (IPS)
An IPS is a network security solution that can not only detect intruders, but also prevent them from successfully launching any known attack.
Intrusion prevention systems combine the abilities of firewalls and intrusion detection systems

## Slide 741: Network Security Devices
https://www.cisco.com/c/en/us/products/security/what-is-network-access-control-nac/_jcr_content/Grid/subc
© Edunet Foundation. Aatlel griogrhy_tsatrl_e8saecrcv/elady.out-subcategory-atl/anchor_info_127c.img.png/1584526264097.png
Network Access Control (NAC)
Involves restricting the availability of network resources to endpoint devices that comply with your security policy
NAC is most useful when the user environment is fairly static and can be rigidly controlled

## Slide 742: Network Security Devices
Web Filters
Web filters are solutions that prevents user browser from loading certain pages from particular websites.
There are different web filters designed for individual, family, institutional and enterprise use
https://cdome.comodo.com/images-new/home/web-filtering.png
© Edunet Foundation. All rights reserved.

## Slide 743: Network Security Devices
Proxy Server
Proxy servers act as negotiators for requests from client software seeking resources from other servers.
A client connects to the proxy server, requesting some service (for example, a website); the proxy server evaluates the request and then allows or denies it.
servers are filtering and
In organizations, proxy usually used for traffic performance improvement
https://s3.amazonaws.com/lintel-blogs-static-files/wp-content/uploads/2019/12/24050525/word-image-3.png
© Edunet Foundation. All rights reserved.

## Slide 744: Network Security Devices
Anti-DDoS Devices
Anti-DDoS devices detect distributed denial of service (DDoS) attacks in their early stages, absorb the volume of traffic and identify the source of the attack.
https://www.accuwebhosting.com/blog/wp-content/uploads/2017/10/anti-ddos-attacks.jpg
© Edunet Foundation. All rights reserved.

## Slide 745: Network Security Devices
© Edunet Foundation. All rights reserved.
Load Balancers
Load balancers are physical units that direct computers to individual servers in a network based on factors such as server processor utilization, number of connections to a server or overall server performance
https://www.f5.com/content/dam/f5-com/page-assets-en/home-en/resources/glossary/what%20is%20load%
20balancing.png

## Slide 746: Network Security Devices
Spam Filter
Spam filters detect unwanted email and prevent it from getting to a user's mailbox. Spam filters judge emails based on policies or patterns designed by an organization or vendor
https://blog.comodo.com/wp-content/uploads/anti-spam-filtering-techniques.jpg
© Edunet Foundation. All rights reserved.

## Slide 747: Able to Configure and Perform Remote Accessing & Routing.
Notes: Title - The learning outcome
Subtitle - Duration

## Slide 748: In this section, we will discuss:
Overview of Remote Access
VPN Concept
Remote Access Authentication Protocol
TCP/IP Routing
Notes: Mention the parent topics one by one. This particular learning outcome has 4 parent topics.

## Slide 749: Overview of Remote Access
Introduction to Remote Access
Remote access is the act of connecting to IT services, applications, or data from a location other than headquarters.
This connection allows users to access a network or computer remotely via the internet.
Image Source: https://1e1851c3a3519282423c-9ba0ce2ac411d9ff878c3235c5043bea.ssl.cf1.rackcdn.com/post/remote-desktop-security-040119-h.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 750: Overview of Remote Access
Introduction to Remote Access
For example, storing and access files in the cloud grants remote access to a network that stores those files.
Examples of include services such as Dropbox, Microsoft One Drive, and Google Drive.
Image Source: https://my5xi5jq5p-flywheel.netdna-ssl.com/wp-content/uploads/2020/02/remote-access-vpn.svg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 751: Overview of Remote Access
How Remote Access Works
Remote access simply works by linking the remote user to the host computer over the internet. ...
Image Source: https://www.cloudcodes.com/img-new/article/what-is-remote-access-control-big.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 752: Overview of Remote Access
How Remote Access Works
Once the software is installed, the local computer can access the remote computer and perform several tasks like running applications, managing updates, and even handling administrative tasks.
Image Source: https://s3.studytonight.com/curious/uploads/pictures/1632209457-79542.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 753: Overview of Remote Access
Types of Remote Access
In the past, remote access was possible by hardwiring to a telephone network.
Analog modems and dial-up technology allowed two different devices to interact with one another by calling assigned phone numbers.
This has changed significantly with broadband technology.
Image Source:
Image Source: https://computertechpro.net/wp-content/uploads/2019/01/blog-dont-underestimate-smart-and-secure-remote-access-840x420.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 754: Overview of Remote Access
Types of Remote Access
Broadband
Cable Broadband
DSL (digital subscriber line)
Cellular internet service
Satellite
Fiber optics broadband
Image Source: https://computertechpro.net/wp-content/uploads/2019/01/blog-dont-underestimate-smart-and-secure-remote-access-840x420.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 755: Types of Remote Access
Broadband
Broadband provides remote users with high-speed connection options to business networks and to the internet.
Image Source:https://www.snetconnect.com/images/Wireless-Broadband/Wireless-Broadband-Graphic.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 756: Types of Remote Access
Cable Broadband
Cable broadband shares the bandwidth with many users.
Image Source:https://www.ciscopress.com/content/images/chap3_9781587134326/elementLinks/03fig01.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 757: Types of Remote Access
DSL (digital subscriber line)
DSL (digital subscriber line) uses a telephone network and is not always available if the infrastructure is poor.
Image Source:https://media.geeksforgeeks.org/wp-content/uploads/Capture-86.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 758: Types of Remote Access
Cellular internet service
Cellular internet service uses mobile devices via a wireless connection; only possible if a cellular network is available.
Image Source:https://hackaday.com/wp-content/uploads/2020/12/vpn-wikiimage.png?w=400
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 759: Types of Remote Access
Satellite
Satellite uses satellites to provide internet access.
Image Source: https://www.scadalink.com/support/img/dwg-slapp-sat-2.gif
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 760: Types of Remote Access
Fiber optics broadband
Fiber optics broadband one of the best ways to transfer massive amounts of data and do so quickly.
Image Source:https://telecomtalk.info/wp-content/uploads/2020/07/differences-fiber-optic-broadband-standard-connection.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 761: Overview of Remote Access
Remote Access Protocol
PPP (Point-to-Point Protocol)
IPsec (Internet Protocol Security)
PPTP (Point-to-Point Tunneling)
L2TP (Layer Two Tunneling Protocol)
Remote Authentication Dial-In User Service (RADIUS)
Terminal Access Controller Access Control System (TACACS)
Image Source: https://support.novell.com/techcenter/articles/img/nc200112dFig1.gif
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 762: Remote Access Protocol
PPP (Point-to-Point Protocol)
Point-to-Point Protocol (PPP) enables hosts to set up a direct connection between two endpoints.
Image Source: https://image3.slideserve.com/6628395/point-to-point-protocol-n.jpg
Notes: This slide talks about the case if we have to divide a subtopic further.
Title Box - Parent Topic
Subtitle box - Sub Topic
Body Text - Subtopic divisions (Subtopics of subtopics)

## Slide 763: Remote Access Protocol
IPsec (Internet Protocol Security)
IPsec (Internet Protocol Security) enables authentication and encryption for IP packet transfers using several security protocols.
Image Source: https://cdn.ttgtmedia.com/rms/onlineimages/security-ipsec_tunnel_mode_mobile.png
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 764: Remote Access Protocol
PPTP (Point-to-Point Tunneling)
Point-to-Point Tunneling (PPTP) is one of the oldest protocols for implementing virtual private networks.
However, over the years, it has proven to be vulnerable to many types of attack.
Although PPTP is not very secure, it persists in some cases.
Image Source: https://networkencyclopedia.com/wp-content/uploads/2019/09/point-to-point-tunneling-protocol-pptp.gif
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 765: Remote Access Protocol
Layer Two Tunneling Protocol (L2TP)
L2TP (Layer Two Tunneling Protocol) VPN protocol without authentication or encryption; usually paired with another protocol.
Image Source: https://sc1.checkpoint.com/documents/R76/CP_R76_VPN_AdminGuide/45218.gif
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 766: Remote Access Protocol
Remote Authentication Dial-In User Service (RADIUS)
Remote Authentication Dial-In User Service (RADIUS) is a networking protocol that provides centralized authentication, authorization, and accounting (AAA) management for users who connect and use a network service.
Image Source: https://www.tech-faq.com/wp-content/uploads/RADIUS.gif
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 767: Remote Access Protocol
Terminal Access Controller Access Control System (TACACS)
Terminal Access Controller Access-Control System (TACACS) refers to a family of related protocols handling remote authentication and related services for networked access control through a centralized server.
Image Sourcehttps://2.bp.blogspot.com/-jQ2GHIJGQsA/WgL3eKjhexI/AAAAAAAAFrA/MzZ5HRYf7UQoTwZkCSIAjntnYd6K5ioXACLcBGAs/s1600/Screen%2BShot%2B2017-11-08%2Bat%2B5.53.33%2BPM.png
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 768: VPN Concept
Introduction to VPN
VPN stands for the virtual private network.
A virtual private network (VPN) is a technology that creates a safe and encrypted connection over a less secure network, such as the internet.
A Virtual Private Network is a way to extend a private network using a public network such as the internet.
Image Source: https://www.okta.com/sites/default/files/styles/1640w_scaled/public/media/image/2020-12/What-is-a-VPN.png?itok=VLLDnRu_
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 769: VPN Concept
VPN Benefits
Secure your network
Hide Your Private Information
Network Scalability
Reduce Support Costs
Image Source:https://i.pinimg.com/originals/8a/3e/16/8a3e16757aa24e512564e10665b4702f.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 770: VPN Concept
Features of VPN
Security
Reliability
Scalability
Image Source:https://cdn.ttgtmedia.com/rms/onlineImages/sWAN_VPN_03.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 771: Features of VPN
Security
The VPN should protect data while it's traveling on the public network.
If intruders attempt to capture the data, they should be unable to read or use it.
Image Source: https://www.cloudwards.net/wp-content/uploads/2018/01/vpn-security.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 772: Features of VPN
Reliability
The VPN should protect data while it's traveling on the public network.
If intruders attempt to capture the data, they should be unable to read or use it.
Image Source:https://i1.wp.com/pingify.me/wp-content/uploads/vpn-security-internet-privacy.png?w=884&ssl=1
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 773: Features of VPN
Scalability
As a business grows, it should be able to extend its VPN services to handle that growth without replacing the VPN technology altogether..
Image Source: https://www.attilasec.com/hubfs/how%20scalable%20are%20hardware%20vpns.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 774: VPN Concept
Types of VPN
Public VPN
Remote Access VPN
Site-to-Site VPN
Image Source: https://www.elprocus.com/wp-content/uploads/types_of_virtual_private_network.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 775: Types of VPN
Public VPN
Public VPN is a type of VPN connection that can be accessed publicly or openly by end users.
It differs from standard or private VPN, which is generally reserved for specific users, organizations or subscribers.
It is normally accessed using a standard Internet connection.
Image Source: https://cooldroid.net/wp-content/uploads/what-is-a-vpn-1068x475.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 776: Types of VPN
Remote Access VPN
Remote access VPN allows a user to connect to a private network and access its services and resources remotely.
The connection between the user and the private network happens through the Internet and the connection is secure and private.
Remote Access VPN is useful for business users as well as home users.
Image Source: https://www.greyson.com/wp-content/uploads/2020/03/remote-access-vpn-1.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 777: Types of VPN
Site-to-Site VPN
A Site-to-Site VPN is also called as Router-to-Router VPN and is mostly used in the corporates.
Companies, with offices in different geographical locations, use Site-to-site VPN to connect the network of one office location to the network at another office location.
Image Source: https://openvpn.net/wp-content/uploads/vpn_server_resources/layer-3-routing-diagram.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 778: VPN Concept
VPN Tunneling
A VPN tunnel is an encrypted link between your computer or mobile device and an outside network.
A VPN tunnel connects your smartphone, laptop, computer, or tablet to another network in which your IP address is hidden and all the data you generate while surfing the web is encrypted.
Image Source https://www.researchgate.net/publication/320536838/figure/fig1/AS:732633726214157@1551684900881/VPN-Tunneling-structure.png:
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 779: VPN Concept
Equipment used for VPN
Network access server
Firewall
AAA Server
VPN Concentrator
VPN-enabled/VPN-optimized Router
VPN-enabled Firewall
VPN Client
Image Source: https://www.webhostingsecretrevealed.net/wp-content/uploads/2018/12/what-is-vpn-service.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 780: Equipment used for VPN
Network access server
As previously described, a NAS is responsible for setting up and maintaining each tunnel in a remote-access VPN.
As previously described, a NAS is responsible for setting up and maintaining each tunnel in a remote-access VPN.
Image Source: https://www.researchgate.net/profile/Zornitsa-Yakova/publication/256843676/figure/fig2/AS:297856234737671@1448025868760/Remote-access-VPN-1.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 781: Equipment used for VPN
Firewall
A firewall provides a strong barrier between your private network and the Internet.
IT staff can set firewalls to restrict what type of traffic can pass through from the Internet onto a LAN, and on what TCP and UDP ports. Even without a VPN, a LAN should include a firewall to help protect against malicious Internet traffic.
Image Source: https://docs.oracle.com/cd/A97630_01/em.920/a96670/img/firewalc.gif
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 782: Equipment used for VPN
AAA Server
The acronym stands for the server's three responsibilities: authentication, authorization and accounting.
For each VPN connection, the AAA server confirms who you are (authentication), identifies what you're allowed to access over the connection (authorization) and tracks what you do while you're logged in (accounting).
Image Source: https://media.geeksforgeeks.org/wp-content/uploads/20200418171147/AAa11.gif
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 783: Equipment used for VPN
VPN Concentrator
This device replaces an AAA server installed on a generic server.
The hardware and software work together to establish VPN tunnels and handle large numbers of simultaneous connections.
Image: https://vpnpick.com/wp-content/uploads/2015/02/VPN-Concentrator-Setup.jpg
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 784: Equipment used for VPN
VPN-enabled/VPN-optimized Router
This is a typical router that delegates traffic on a network, but with the added feature of routing traffic using protocols specific to VPNs.
Image: https://www.techrepublic.com/a/hub/i/2015/06/03/4d31da68-098c-11e5-940f-14feb5cc3d2a/r00220001108jim03_01.gif
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 785: Equipment used for VPN
VPN-enabled Firewall
This is a conventional firewall protecting traffic between networks, but with the added feature of managing traffic using protocols specific to VPNs.
Image: https://www.techrepublic.com/a/hub/i/2015/06/03/4d31da68-098c-11e5-940f-14feb5cc3d2a/r00220001108jim03_01.gif
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 786: Equipment used for VPN
VPN Client
This is software running on a dedicated device that acts as the tunnel interface for multiple connections.
This setup spares each computer from having to run its own VPN client software.
Image: https://www.concordia.ca/content/concordia/en/finearts/cda/support/faq/vpn-client/_jcr_content/content-main/image_1660899872.img.png/1586871321105.png
Notes: Continuing from the last slide:
Title - Subtopic
Subtitle - Subtopic of Subtopic
Body - Description

## Slide 787: VPN Concept
VPN Security
L2F (Layer 2 Forwarding)
PPTP (Point-to-Point Tunneling Protocol)
L2TP (Layer 2 Tunneling Protocol)
Image Source: https://sites.google.com/site/virtualprivatenetworks/_/rsrc/1472764625920/website-builder/what-is-vpn.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 788: VPN Security
L2F (Layer 2 Forwarding)
L2F (Layer 2 Forwarding) developed by Cisco; uses any authentication scheme supported by PPP.
Image Source: https://networkencyclopedia.com/wp-content/uploads/2019/08/l2f-layer2-forwarding-cisco.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 789: VPN Security
PPTP (Point-to-Point Tunneling Protocol)
PPTP (Point-to-point Tunneling Protocol) supports 40-bit and 128-bit encryption and any authentication scheme supported by PPP.
Image Source: https://networkencyclopedia.com/wp-content/uploads/2019/09/point-to-point-tunneling-protocol-pptp.gif
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 790: VPN Security
L2TP (Layer 2 Tunneling Protocol)
L2TP (Layer 2 Tunneling Protocol) combines features of PPTP and L2F and fully supports IPSec; also applicable in site-to-site VPNs
Image Source: https://sc1.checkpoint.com/documents/R76/CP_R76_VPN_AdminGuide/45218.gif
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 791: Remote Access Authentication Protocol
Password Authentication Protocol (PAP)
PAP is the least secure authentication protocol.
The username and password is sent in plaintext.
It does not protect against anyone listening to network traffic from stealing the username and password.
Image Source:
Image Source: https://i0.wp.com/networkustad.com/wp-content/uploads/2020/05/Picture1.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 792: Password Authentication Protocol (PAP)
Features of PAP
The password is sent in cleartext.
All network operating systems support PAP.
It uses a two-way Handshake Protocol.
It is non-interactive.
PAP supports both one-way authentication (unidirectional) and two-way authentication (bidirectional).
Image Source: https://i0.wp.com/networkustad.com/wp-content/uploads/2020/05/Picture1.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 793: Password Authentication Protocol (PAP)
When to use PAP
PAP is usually used in the following scenarios:
When the application doesn’t support CHAP.
Circumstances where it is necessary to send a plain text password to simulate a login at the called device (remote host).
When there is the occurrence of incompatibilities between different vendors of CHAP.
Image Source: http://orbit-computer-solutions.com/wp-content/uploads/2015/10/PAP-Authentication-Protocol.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 794: Password Authentication Protocol (PAP)
Advantage of CHAP over PAP
Some of the advantages are:
CHAP is more secure than PAP.
CHAP can provide authentication periodically to recognize that the user accessing the PPP link is the same or not.
In CHAP, the real passwords are never shared on the link instead a hash value of it is calculated and transferred.
Image Source:
Image Source: https://webeduclick.com/wp-content/uploads/2020/02/Challenge-Handshake-Authentication-Protocol-CHAP.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 795: Password Authentication Protocol (PAP)
Advantage of PAP over CHAP
The only advantage PAP holds over CHAP is that it is supported by the all the network operating system vendors therefore it can be said that PAP is used where CHAP is not supported.
But if CHAP is supported then it is recommended to use CHAP as it is more secure.
Image Source: https://webeduclick.com/wp-content/uploads/2020/02/Challenge-Handshake-Authentication-Protocol-CHAP.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 796: Remote Access Authentication Protocol
CHAP
Challenge Handshake Authentication Protocol (CHAP) is a Point-to-point protocol (PPP) authentication protocol developed by IETF (Internet Engineering Task Force).
It is used at the initial startup of the link. Also, it performs periodic checkups to check if the router is still communicating with the same host.
Image Source:
Image Source: https://networkencyclopedia.com/wp-content/uploads/2019/08/CHAP-Challenge-Handshaking-Authentication-Protocol.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 797: Remote Access Authentication Protocol
Features of CHAP
It uses 3-way handshaking protocol (not like TCP). First, the authenticator sends a challenge packet to the peer then, the peer responds with a value using its one way hash function.
The authenticator then matches the received value with its own calculated hash value. If the values match then the authentication is acknowledged otherwise, the connection will be terminated.
Image Source:
Image Source: https://networkencyclopedia.com/wp-content/uploads/2019/08/CHAP-Challenge-Handshaking-Authentication-Protocol.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 798: Remote Access Authentication Protocol
Features of CHAP
It uses one-way hash function called MD5.
It also authenticates periodically to check if the communication is taking place with the same device or not.
Image Source:
Image Source: https://networkencyclopedia.com/wp-content/uploads/2019/08/CHAP-Challenge-Handshaking-Authentication-Protocol.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 799: Challenge Handshake Authentication Protocol (CHAP)
Features of CHAP
Also, it provides more security than PAP (Password Authentication Procedure) as the value used (find out by hash function) is changed variably.
CHAP requires to know the plaintext of the secret as it is never sent over the network.
Image Source: https://networkencyclopedia.com/wp-content/uploads/2019/08/CHAP-Challenge-Handshaking-Authentication-Protocol.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 800: Challenge Handshake Authentication Protocol (CHAP)
CHAP Packets
Challenge packet
Response Packet
Success packet
Failure packet
Image Source:https://cdn.ttgtmedia.com/rms/onlineimages/challenge_handshake_authentication_protocol-f_mobile.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 801: Challenge Handshake Authentication Protocol (CHAP)
The Extensible Authentication Protocol (EAP)
Extensible Authentication Protocol (EAP) is an authentication framework, not a specific authentication mechanism, frequently used in wireless networks and point-to-point connections.
It provides some common functions and negotiation of authentication methods called EAP methods.
Image Source: https://i0.wp.com/wentzwu.com/wp-content/uploads/2020/03/extensible-authentication-protocol-eap-1.jpg?ssl=1
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 802: Remote Access Authentication Protocol
MS-CHAP
Microsoft Challenge Handshake Authentication Protocol version 2 (MS-CHAP v2) is a password-based authentication protocol which is widely used as an authentication method in PPTP-based (Point to Point Tunneling Protocol) VPNs.
Image Source: https://docs.microsoft.com/en-us/openspecs/windows_protocols/ms-chap/ms-chap_files/image001.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 803: Remote Access Authentication Protocol
MS-CHAP v2
Microsoft Challenge Handshake Authentication Protocol version 2 (MS-CHAP v2) is a password-based authentication protocol which is widely used as an authentication method in PPTP-based (Point to Point Tunneling Protocol) VPNs.
Image Source: https://i.stack.imgur.com/Iu8Bi.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 804: Remote Authentication Dial-In User Service (RADIUS)
What is RADIUS
Remote Authentication Dial-In User Service (RADIUS) is a networking protocol that provides centralized authentication, authorization, and accounting (AAA) management for users who connect and use a network service.
Image Source: https://blog.miniorange.com/wp-content/uploads/sites/19/2021/02/radius-mfa-flow.webp
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 805: Remote Authentication Dial-In User Service (RADIUS)
How it works
The working of the RADIUS Server depends on the exact nature of the RADIUS ecosystem.
However, all servers have AAA capabilities (Authentication, Authorization, and Accounting).
In some RADIUS ecosystems, a RADIUS Server can also act as a proxy client to other RADIUS Servers.
Image Source:https://www.freelancinggig.com/blog/wp-content/uploads/2019/05/What-is-RADIUS-Server.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 806: Remote Authentication Dial-In User Service (RADIUS)
Background Information
Communication between a network access server (NAS) and a RADIUS server is based on the User Datagram Protocol (UDP).
Generally, the RADIUS protocol is considered a connectionless service.
Issues related to server availability, retransmission, and timeouts are handled by the RADIUS-enabled devices rather than the transmission protocol.
Image Source:
Image Source:https://www.freelancinggig.com/blog/wp-content/uploads/2019/05/What-is-RADIUS-Server.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 807: Remote Authentication Dial-In User Service (RADIUS)
RADIUS is a Client/Sver Protocol
RADIUS is a client/server protocol.
The RADIUS client is typically a NAS and the RADIUS server is usually a daemon process running on a UNIX or Windows NT machine.
The client passes user information to designated RADIUS servers and acts on the response that is returned.
Image Source:
Image Source:https://www.freelancinggig.com/blog/wp-content/uploads/2019/05/What-is-RADIUS-Server.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 808: Remote Authentication Dial-In User Service (RADIUS)
Connection Steps
This figure shows the interaction between a dial-in user and the RADIUS client and server.
User initiates PPP authentication to the NAS.
NAS prompts for username and password (if Password Authentication Protocol [PAP]) or challenge (if Challenge Handshake Authentication Protocol [CHAP]).
User replies.
Image Source: https://www.cisco.com/c/dam/en/us/support/docs/security-vpn/remote-authentication-dial-user-service-radius/12433-32a.gif
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 809: Remote Authentication Dial-In User Service (RADIUS)
Connection Steps
RADIUS client sends username and encrypted password to the RADIUS server.
RADIUS server responds with Accept, Reject, or Challenge.
The RADIUS client acts upon services and services parameters bundled with Accept or Reject.
Image Source:
Image Source: https://www.cisco.com/c/dam/en/us/support/docs/security-vpn/remote-authentication-dial-user-service-radius/12433-32a.gif
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 810: Remote Authentication Dial-In User Service (RADIUS)
Authentication and Authorization
A RADIUS Server supports a variety of methods to authenticate a user.
RADIUS Server authentication and authorization go hand in hand and usually start when a user tries to connect to the RADIUS Client using a username and password.
Image Source:https://docs.microsoft.com/en-us/windows/win32/nps/images/ias01.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 811: Remote Authentication Dial-In User Service (RADIUS)
Accounting
The accounting features of the RADIUS protocol can be used independently of RADIUS authentication or authorization.
The RADIUS accounting functions allow data to be sent at the start and end of sessions, indicating the amount of resources (such as time, packets, bytes, and so on) used during the session.
Image Source: https://www.researchgate.net/profile/Dr-Govardhan/publication/228973856/figure/fig2/AS:300905783152653@1448752937571/RADIUS-accounting-In-Accounting-Request-packet-the-generation-of-Request-Authenticator.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 812: TCP/IP Routing
Introduction to TCP/IP Routing
TCP/IP (Transmission Control Protocol/Internet Protocol) is a set of protocols independent of the physical medium used to transmit data, but most data transmission for Internet communication begins and ends with Ethernet frames.
The Ethernet can use either a bus or star topology.
Image Source https://www.cisco.com/c/dam/en/us/support/docs/ip/routing-information-protocol-rip/13769-fig-5-new.gif:
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 813: TCP/IP Routing
Protocol Types
Host Route
Network Route
Default Route
Image Source: https://cdn.educba.com/academy/wp-content/uploads/2019/05/Routing-Protocol.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 814: Protocol Types
Host Route
Defines a gateway that can forward packets to a specific host or gateway on another network.
Image Source: https://docs.oracle.com/cd/E95619_01/html/esbc_ecz810_configuration/img/GUID-F7451319-0AEC-4793-8027-7CBE81E7FB05-default.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 815: Protocol Types
Network Route
Defines a gateway that can forward packets to any of the hosts on a specific network.
Image Source: https://networkencyclopedia.com/wp-content/uploads/2019/08/routing.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 816: Protocol Types
Default Route
Defines a gateway to use when a host or network route to a destination is not otherwise defined.
Image Source: https://www.networxsecurity.org/fileadmin/user_upload/images/2015-08/Default_Route.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 817: TCP/IP Routing
Static & Dynamic Routing
In TCP/IP, routing can be one of two types: static or dynamic.
With static routing, you maintain the routing table manually using the route command.
Static routing is practical for a single network communicating with one or two other networks.
Image Source:
Image Source: https://snabaynetworking.com/wp-content/uploads/2019/10/Static-Routing-vs-Dynamic-Routing-565x420.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 818: TCP/IP Routing
Static & Dynamic Routing
With dynamic routing, daemons update the routing table automatically.
Routing daemons continuously receive information broadcast by other routing daemons, and so continuously update the routing table.
Image Source: https://snabaynetworking.com/wp-content/uploads/2019/10/Static-Routing-vs-Dynamic-Routing-565x420.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 819: TCP/IP Routing
Gateways
Gateways are a type of router. Routers connect two or more networks and provide the routing function.
Some routers, for example, route at the network interface level or at the physical level.
Image Source: https://i.ytimg.com/vi/ai5bFPVToMU/maxresdefault.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 820: TCP/IP Routing
Interior and Exterior Gateways
Interior Gateway Protocol (IGP) is a Routing Protocol which is used to find network path information within an Autonomous System.
Exterior Gateway Protocol (EGP) is a Routing Protocol which is used to find network path information between different Autonomous Systems.
Image Source: https://snabaynetworking.com/wp-content/uploads/2019/12/routing-protocols-2.gif
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 821: TCP/IP Routing
Gateway Protocols
Routing Information Protocol Next Generation
Open Shortest Path First (OSPF)
Exterior Gateway Protocol (EGP)
Border Gateway Protocol (BGP)
Border Gateway Protocol 4+
Intermediate System to Intermediate System (IS-IS)
Image Source: https://documents.trendmicro.com/images/TEx/articles/protocol-gateways-fig-1.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 822: Gateway Protocols
Routing Information Protocol Next Generation
Routing Information Protocol or RIP is one of the first routing protocols to be created.
RIP is used in both Local Area Networks (LANs) and Wide Area Networks (WANs), and also runs on the Application layer of the OSI model.
There are multiple versions of RIP including RIPv1 and RIPv2.
Image Source: https://static.javatpoint.com/tutorial/computer-network/images/rip-protocol.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 823: Gateway Protocols
Open Shortest Path First (OSPF)
Open Shortest Path First or OSPF protocol is a link-state IGP that was tailor-made for IP networks using the Shortest Path First (SPF) algorithm.
The SPF routing algorithm is used to calculate the shortest path spanning-tree to ensure efficient data transmission of packets.
Image Source https://media.geeksforgeeks.org/wp-content/uploads/rrf.png:
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 824: Gateway Protocols
Exterior Gateway Protocol (EGP)
Exterior Gateway Protocol or EGP is a protocol that is used to exchange data between gateway hosts that neighbor each other within autonomous systems.
In other words, EGP provides a forum for routers to share information across different domains.
Image Source:https://networkencyclopedia.com/wp-content/uploads/2019/08/exterior-gateway-protocol.jpg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 825: Gateway Protocols
Border Gateway Protocol (BGP)
Border Gateway Protocol or BGP is the routing protocol of the internet that is classified as a distance path vector protocol.
BGP was designed to replace EGP with a decentralized approach to routing.
Image Sourcehttps://www.cisco.com/c/dam/en/us/support/docs/ip/border-gateway-protocol-bgp/212881-border-gateway-protocol-bgp-optimal-ro-01.jpeg:
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 826: Gateway Protocols
Border Gateway Protocol 4+
Border Gateway Protocol version 4 (BGP4) is an exterior gateway protocol that performs inter-autonomous system (AS) or inter-domain routing.
It peers to other BGP-speaking systems over TCP to exchange network reachability and routing information.
Image Source:https://www.cisco.com/c/dam/en/us/support/docs/ip/border-gateway-protocol-bgp/212881-border-gateway-protocol-bgp-optimal-ro-02.jpeg
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 827: Gateway Protocols
Intermediate System to Intermediate System (IS-IS)
Intermediate System-to-Intermediate System (IS-IS) is a link-state, IP routing protocol and IGPP protocol used on the internet to send IP routing information.
IS-IS uses a modified version of the Dijkstra algorithm.
An IS-IS network consists of a range of components including end systems, (user devices), intermediate systems (routers), areas, and domains.
Image Source: https://networkdirection.net/wp-content/uploads/RoutingAndSwitching/IS-IS.png
Notes: Left (White Color space):
Title - Parent Topic
Subtitle - Subtopic 1
Body Text - Description in bullets
Right (Grey Color Space):
Body Text - Relevant image (with source)/code snippet
Put reference links in Speaker Notes
Reference:
https://www.tutorialspoint.com/internet_technologies/internet_overview.htm/

## Slide 828
Notes: THANK YOU!